## Slide 1: Preliminary results of the multipacting measurements
Bat. 181, Meyrin site / magnet reference MBB013,uncoated
Week 15

## Slide 2: Principle

## Slide 3: assembly of the vacuum system (week 11 )
General assembly outside the supervised area during week 11

## Slide 4: Set up of the vacuum system in front of the MBB magnet (week 12-13)
Connected the vacuum system to the MBB magnet (magnet reference MBB 013, uncoated)
Connected the residual gas analyzer (RGA) and the pressure gauges to acquire pressure data
Leak detection for several days, RGA showed increased oxygen, nitrogen and argon => air leak (fixed)
RGA’s filaments have been very dirty => started degassing procedure

## Slide 5
Simultaneously made a labview program to acquire pressure data automatically and save it to a spreadsheet format (e.g. Excel)
Attached tungsten wire (had to open flanges which resulted in a vacuum loss)

## Slide 6: Attachment of the tungsten wire

## Slide 9: Labview data acquisition program
Block diagram

## Slide 10
Graphical user’s interface

## Slide 11: Network analysis of the tungsten wire
Applied vector network analyzer (Agilent E5071C)
Short circuit at the end of the wire
Measurement of the characteristic impedance showed short circuit at 2 – 3 meters => conclusion: tungsten wire touched bottom of the beam pipe
After tightening the wire, characteristic impedance looked (almost) as it should be

## Slide 12
Characteristic impedance over time

## Slide 13
Measurement of S11 (reflection) showed good resonances at 187.73 MHz (marker 2) and 205.54 MHz (marker 1)

## Slide 14
After applying a matching network with a trombone, smith-chart showed critical coupling for f=187.73 MHz

## Slide 15
Matched network with trombone

## Slide 16: First test runs with injected RF power
Available power amplifier amplifies with 50 dB in a frequency range of 30 MHz – 200 MHz up to 50 W
Therefore the excitement frequency 187.73 MHz has been selected for the first test run

## Slide 18
Main gas in the system is water (normal)
Multipacting starts at the end of the power sweep close to its maximum power
Scrubbing effect and conditioning over several power cycles (surface becomes more and more clean)
These results fit to former results

## Slide 19
Measurements at other resonances (e.g. 130.38 MHz; 225.25 MHz with open circuit) did not cause any different behavior after matching the network
No dependency on frequency so far

## Slide 20: First tests with magnetic field
Applying a magnetic field has a huge impact on multipacting
Selected frequency is 130.48 MHz
Measurements with various magnetic field strengths

## Slide 22
Hydrogen is the main content in the system now
Conclusion:
Electrons are concentrating on smaller areas due to the magnetic field. The higher intensity is releasing hydrogen from deeper layers of the beam pipe material

## Slide 23: Outlook
Measurements with magnetic field and a closed main valve to simulate SPS pumping speed
Simulations with microwave studio / particle studio to acquire simulation data for comparison and to track the particles

## Slide 24: Electric field distribution, Phase=0°

## Slide 25: Particle tracking
Primaries' energy = 400 eV, 10% spread, 960 initial particles
40 Watt constant power, one initial pulse
Simulation time is 20 ns

## Slide 26: Emitted secondaries

## Slide 27: Particles versus time

## Slide 28: Summary concerning the simulation
Primary energy of 400 eV chosen, most secondaries are expected at this primary energy (see SEY measurements of stainless steel)
Simulation data is preliminary
Have to check all the parameters and choose the correct excitation signal and particle distribution