## Slide 1: Preparation of Microwave transmission E-Cloud measurements in the CPS
F. Caspers, S. Federmann, E. Mahner
SPSU meeting, 27th October 2009

## Slide 2: Contents
Motivation
Setup
Outlook

## Slide 3: Motivation
We have the possibility in PS84 to turn the e-cloud on and off due to the presence of a clearing electrode
Comparison of the microwave (µw) transmission method with signals on shielded button pick up for direct e-cloud detection
Does it make sense to change the direction of the µw signal between parallel and antiparallel w.r.t. beam direction?

## Slide 4: Motivation
Having always assumed so far that there is no direct interaction with the beam (Lawson Woodward theorem: The net energy gain of a relativistic electron interacting with an electromagnetic field in vacuum (or in a very large wave guide) is zero. “J.D. Lawson, IEEE Trans. Nucl. Sci. NS-26, 4217, 1979”)
This theorem is only valid for homogeneous beam pipes of infinite length
  We might be able to check whether this holds (not certain since we do not really know the mode type and mode pattern we excite in this setup since we have simply selected the strongest trapped mode (interaction with beam small) close to 3 GHz – details explained later)

## Slide 5
Slide courtesy of E. Mahner

## Slide 6: Setup
Slide courtesy of E. Mahner

## Slide 7: Setup
HP
HP
VSA
RF source
HP ….. High pass, sharp cutoff at 2.2 GHz
VSA … Vector Spectrum Analyzer
Receiver path
Transmitter path
Measurement room
Tunnel
RF signal
Clearing electrode
Shielded button pick up for direct ecloud measurements
For the preparation of the measurements the signal output of a Vector Network Analyzer was used as RF source since we did not have anything else above 3 GHz avaliable
RF antennas(feedthrough without button)
Wave guide
Wave guide
Gain ~ 30 dB

## Slide 8: Preparation for MD in w45
Transmission measurements in order to determine which frequency we should use for the carrier wave
HP
HP
Clearing electrode
Shielded button pick up for direct ecloud measurements
Tunnel
RF antennas (feedthrough without button)
VNA
Measurement room
Port 1
Port 2
VNA … Vector Network Analyzer
CROSS TALK !!
2GHz Wave
guide
2GHz Wave
guide

## Slide 9: Preparation
Hardware transfer function (HTF) of the PS84 region:
Frequency [Hz]
dB
f = 3.205 GHz
Coupling via RF antennas

## Slide 10: Discussion of frequency choice
We need a fairly high frequency in order to escape the coherent beam spectrum, but
The higher the frequency, the more the attenuation of the cables becomes an issue
We don’t want to have electronics in the tunnel (avoid radiation damage of electronics – PS is electromagnetically dirty, would have to get DC Voltage into the tunnel, access problems)
we have to find a compromise between frequency and cable damping

## Slide 11: HTF in the time domain (wideband)
Crosstalk (RF leakage of connectors, high passes and amplifier in the measurement room) is not excluded a priori
Check via measurements in time domain (in frequency domain difficult to diagnose):
Time [µs]
dB
Residual cross talk
Signal via PS84

## Slide 12: HTF in the time domain (narrowband)
dB
Time [µs]
55 dB
Since signal from PS84 is so much bigger, cross talk can be neglected for this type of measurements

## Slide 13: VSA
PS revolution frequency 476 kHz
We would expect a modulation signal here

## Slide 14: VSA with beam harmonics
PS revolution frequency 476 kHz
We would expect a modulation signal here
Note: we see no AM or PM modulation in this setup!

## Slide 15: Comparison PS - SPS
In the PS: We have not seen AM or PM modulation with “small” beam (21. 10. 09) in this setup – we see no intermodulation (IM)
IM was main problem in SPS setup
Why is it different?
  No electronics in the tunnel
  No intermodulation with electronics in measurement room due to very good HP, good cable shielding (low transfer impedance, which is a measure of cable leakage) and 476 kHz much higher than 43 kHz (SPS)

## Slide 16: Outlook
Installation of :
  Circulator in the transmitter part to avoid IM at the output of the signal generator with beam signals above 2 GHz
  Filter to suppress strong signal from beam harmonics
  Practical question: How to get such kind of filter quickly?
Circulator
Filter + circulator

## Slide 17: Do-it-yourself Filter
How to produce quickly and cheap a filter yourself:
Concept: λ/2 coaxial resonator
We take a suco box
Put an inner conductor (solid brass rod of 10 mm diameter) in it, supported by 2 Teflon rings:
Fine tuning can be done with grinding tool (difficult to predict the exact resonance frequency due to fringe fields and detuning of coupling pins as well as dielectric supports)
et voilá
Capacitive coupling

## Slide 18: Outlook
Planned Measurements for next MD:
  Unfortunately in this setup it does not make sense to check for any difference between forward and backward transmission since we have a resonator and we cannot attribute any difference of interaction since we cannot disentangle the forward and backward travelling wave in this resonator
  Check validity after PM demodulation of received signal by switching e-cloud on and off via clearing electrode

## Slide 19
Slide courtesy of E. Mahner