## Slide 1: Beam observations during MD w42
participants:
T. Argyropoulos, T. Bohl, C. Bhat, G. Rumolo, M. Taborelli, E. Shaposhnikova, +
help from OP shift (+ K. Cornelis)

## Slide 2: MD w42 – 19.10
50 ns and 25 ns spaced nominal LHC beam with correspondingly 1.3x1011 and 1.15x1011/bunch
Dedicated MD cycle → even for 50 ns spaced beam problems with
  MKE heating: 54 deg with 1 batch (36 -> 24 bunches, 4 -> 2 -> 1 batches)
  pressure (spike, 10 min recovery)
50 ns beam:
  beam losses (4.5 – 9) %
  transverse emittances: inj. H/V 2.5/2.9 ±0.4, extracted: 2.2/2.8 ± 0.4
At the beginning too long bunches from PS (80 MHz problem), losses during controlled emittance blow-up during the ramp

## Slide 3: Transverse emittance for 25 ns spaced beam for different number of batches
Chart: SPS MD 2010/10/19 extraction 25 ns, 36 bunches, 1.2E11p/bunch
| 1 | 2 | 3 | 4 | 4
e_H(um) | 3.4525 | 2.4 | 3.6149 | 3 | 3.296
e_V(um) | 3.54 | 0 | 3.7434 | 3.9 | 3.7236
Chart: SPS MD 2010/10/19, Injection 25 ns, 36 bunches/batch ~1.2E11/bunch
| 1 | 2 | 3 | 4 | 4
e_H(um) | 3.045 | 2.8267 | 2.9538 | 2.8225 | 3.1657
e_V(um) | 3.4 | 3.5917 | 3.7193 | 3.7797 | 3.5913
Vertical emittance increases with number of batches
measurement time: t=0.55 s (26 GeV) and t=15.4 s (450 GeV)
C. Bhat
C. Bhat

## Slide 4: MD on 19.10.2010 - no longitudinal blow-up: stable 50 ns beam
Nominal intensity: 1.3x10^11/bunch injected
1-4 batches
800 MHz on, usual phase shift relative to 200 MHz
nominal voltage program
T. Argyropoulous et al.

## Slide 5: MD on 9.11.2010 - no longitudinal blow-up - unstable 50 ns beam
Injected bunch length (emittance) is significantly smaller!

## Slide 6: MD on 19.10.2010 - no longitudinal blow-up: 50 ns beam
…also unstable for shorter injected bunches?

## Slide 7: SPS transmission versus injected longitudinal emittance (25 ns beam)
H. Damerau et al
MD on 19.10.2010

## Slide 8: Summary
There is a narrow window for the injected longitudinal emittance – losses increase for higher values and beam is unstable for lower.
In the latter case emittance blow-up is required even for stability of the 50 ns spaced beam
Need more accurate measurements of transverse emittance