## Slide 1: Electron cloud effects in the SPS in nominal and low γt optics
H. Bartosik, E. Benedetto, K. Li, Y. Papaphilippou, G. Rumolo

## Slide 2: Motivation
Study impact of the new low γt optics in SPS on the onset of electron cloud instability
Difference between low γt (Q20) and nominal optics (Q26)
  Q20 has higher slippage factor (η is increased by a factor of 2.85 at injection and 1.6 at extraction)
   higher synchrotron tune for same bucket parameters (in this case Qs~η)
  Q20 has increased average β-functions and increased dispersion function
  Q20 has lower tunes  may affect incoherent effects
Expected scaling of instability threshold?
  Interaction with electron cloud is non-linear
  Nb,th~Qs/β (similar to TMCI)?
Goal
  Understand scaling of threshold with Qs and with β
  Study the electron cloud density threshold in the two optics for different bunch intensities

## Slide 3: E-cloud simulations with HeadTail
HeadTail is used to study the impact of a given elctron cloud on the stability of a single bunch  build-up of cloud itself not simulated
  Consecutive bunch slices interact with the cloud sequentially and deform it dynamically (“pinch”)  electron cloud serves as “wake field”
  After all bunch slices have interacted, cloud is reset to uniform distribution
  Electron cloud interaction regions (“kicks”) can be distributed symmetrically around the circumference  reduce numerical effects due to strong local kick
  Bunch particles interact with electrons, but no proton-proton or electron-electron interaction
  Uniform focusing used for now (smooth approximation, constant β-functions)
Electron cloud in field free regions and in dipole fields
  Electron motion in field free region defined by interaction with proton bunch in both transverse dimension
  Electron motion in dipole regions “frozen” in horizontal direction to model magnetic field (Larmor precession); electrons move only in vertical direction  no pinching and no instability in horizontal direction
Coherent head-tail motion can be observed as exponential emittance growth  used to find instability threshold

## Slide 4: Simulation parameters
  E-cloud distributed over 192 kicks (for numerical convergence)
  Simulations for injection energy (26 GeV), εx,y=2.5μm, 512 turns
  Synchrotron motion in nonlinear bucket
  No additional non-linearity (Chromaticity set to 0, no octupoles, …)
  RF-voltage adjusted to provide same bucket parameters in both cases
Parameter | Low γt optics | Nominal SPS optics
Bunch length (rms) | 0.23 m | 0.23 m
Momentum spread | 0.002 | 0.002
RF-voltage (injection) | 5.75 MV | 2 MV
Synchrotron tune | 0.017 (=1/59) | 0.0059 (=1/170)
Momentum compaction factor | 0.00308 | 0.00192
Transition energy (γt) | 18 | 22.8
Tunes (Qx, Qy) | 20.13, 20.18 | 26.13, 26.18
Average β-functions in LSS (βx, βy) | 54.6m | 42m
Average β-functions in MBB (βx, βy) | 45.5m, 78.4m | 34.4m, 72.3m
Average dispersion in MBB (Dx) | 3m | 1.8m

## Slide 5: Instability threshold
Threshold can be identified when scanning electron cloud density ρ
  Start with low density  almost constant emittance
  Clear exponential growth for ρ above the threshold
   Possible definition of threshold: smallest value of electron cloud density for which the emittance after investigated number of turns is bigger than threshold value (arbitrary!!)
  Threshold considered here: emittance growth by ~5% after 512 turns
  Absolute rise-times are compared (not with respect to synchrotron periods)
  Threshold density marked in plots as dashed line
  For ρ above threshold (but not too high), instability observed as exponential growth of emittance

## Slide 6: Incoherent effects for high ρ
“Incoherent” effects far above threshold density
  Depend on kicks per turn, number of particles, tune, number of grid points, …
  Saturation of growth rate after initial fast growing emittance for intermediate ρ
  For ρ far above threshold, incoherent growth of emittance can be observed
  Simulation artifact?
  Makes high electron cloud density appear less harmful …
  We are interested in onset of instability  very important to start scan from low values of ρ
  ρ is the quantity to scan to find instability threshold!
  Scanning for other parameters (like bunch intensity) may not reveal threshold (if by chance ρ is too high)

## Slide 7: Changing synchrotron tune Qs
Electron cloud density scans for different values of Qs
  Changing momentum compaction factor and RF-voltage for constant longitudinal bunch parameters
  Corresponds to change of optics
  Simulation for dipole regions
  Higher threshold for higher Qs  higher synchrotron tune helps stabilizing beam
  ρth(Qs=0.006)~3.2e11/m3
  ρth(Qs=0.018)~8.4e11/m3
Qs=0.006
Qs=0.018
Factor 3??

## Slide 8: Threshold as function of Qs
Within the studied range, threshold increases linearly with synchrotron tune
  Extrapolation of data-points (linear fit) is not crossing origin  maybe explained by roughness of scan
  Definition of threshold not optimal?
Within “precision“ of simulation: ρth~Qs
  Dipole regions
  Nominal optics
  Nb=1.3e11ppb
  512 turns
  Constant longitudinal bunch parameters
  Dispersion included in simulation

## Slide 9: Changing βy in dipole regions
For constant βx, βy is changed in dipole regions
  Pinch depends on charge density of proton bunch  beam dimensions (and bunch intensity)
  Similar to wakefield due to impedance, kick strength due to interaction with electron cloud increases for higher values of β function  threshold should decrease for higher β
Simulation for nominal optics and Nb=2e11ppb
βy=30m
βy=78m

## Slide 10: Threshold as function of βy
Simulation for dipole regions
  Within studied range, threshold decreases with βy
  Scaling not like classical TMCI (~ρc~1/β) but rather like ρc~1/βn, with 0.5<n<1
  Depending on βx ? (Through the dependence of the electron oscillation frequency on the proton charge density and thus beam size)
What happens when changing simultaneously βx and βy?
  Dipole regions
  Nominal optics
  Nb=2e11ppb
  512 turns
  Constant longitudinal bunch parameters
  Dispersion included in simulation

## Slide 11: Threshold as function of intensity
Comparing the two optics
  Thresholds for different values of bunch intensity for parameter sets of nominal and low γt optics
Simulations for field free and dipole regions
  In both cases, increased threshold for low γt optics for all intensities
  Field free region: threshold increased for Q20 by roughly factor 2.3 on average
  Dipole region: threshold increased for Q20 by factor 2 on average

## Slide 12: Summary
Analyzed onset of electron cloud instability
  Threshold not unambiguously defined
Studied dependence of instability threshold on β-functions and synchrotron tune
  Threshold increases with higher synchrotron tune
  Threshold decreases with larger β-function (dispersion included)
According to simulation, low γt optics has higher threshold
  How about electron cloud build up?
  How about incoherent effects  careful setup and choice of parameters needed
  Very interesting for comparison with measurements! (To be done …)