## Slide 1: Outcome from 2011 Chamonix workshop New structure of the SPSU Study Group
E. Shaposhnikova
17.02.2011

## Slide 2: New structure of the SPSU SG
SPS Upgrade is a part of the LIU project
(leader - R. Garoby, deputy - M. Meddahi)
SPS Upgrade coordination - B. Goddard
(deputy - E.S., scientific secretary - G. Rumolo ) – more information at the next SG meeting
Mitigation of e-cloud (coatings and electrodes) will be studied by separate WG chaired by M. Jimenez (TE/VAC)
SPSU SG will be responsible for all Beam Dynamics studies (calculations, simulations, measurements, data analysis) related to the SPS upgrade:
  SPSU SG → SPSU-BD SG
  scientific secretary – B. Salvant
  convener – E. S.
  new web site?

## Slide 3: Is it a good name?
Google tells…
SPSU: Worst Schools Reviewed - Home
- [ Diese Seite übersetzen ] Find out why one should avoid SPSU and choose an alternative for higher education… www.spsusucks.com/ -

## Slide 4: And what about BD? (Beam Dynamics or Bande Dessinee?)

## Slide 5: Proposed membership for SPSU-BD SG
G. Arduini (optics, LHC)
T. Argyropoulos (double RF)
H. Bartosik (low γt )
T. Bohl (RF, MDs)
F. Caspers (impedance)
K. Cornelis (OP, MDs)
W. Hofle (FB, MDs)
E. Metral (impedance)
J. Muller (MDs, long. HOM)
Y. Papaphilippou (optics, low γt)
G. Rumolo (e-cloud)
M. Taborelli (e-cloud)
B. Salvant (MDs, impedance)
E. Shaposhnikova (convenor)
plus
C. Bhat (LARP)
N. Monet (multi-bunch)
H. Maury Cuna (e-cloud)
N. Biancacci (impedance)

## Slide 6: LHC beams in SPS
Beam parameters |  | SPS @ 450 GeV/c (intensity maximum injected minus losses) |  |  |  |  | 
 |  | nom. | nom. | nom. | 2010 | 2010 | 2010
bunch spacing | ns | 25 | 50 | 75 | 25 | 50 | indiv
max bunch intensity | 1011 | 1.2 | 1.2 | 1.2 | 1.5 | 1.52 | 3.2
number of bunches |  | 4x72 | 4x36 | 4x24 | 3x72 | 4x36 | 1
total intensity on FT | 1013 | 3.5 | 1.7 | 1.2 | 3.2 | 2.2 | 0.03
long. emittance | eVs | 0.7 | 0.5 | 0.4 | 0.8 | 0.6 | 0.4
norm. h/v emittance | μm | 3.6 | 2.0* | 2.0* | ~10 | ? | 6.0
* double batch injection in PS: 1.1/1.4

## Slide 7: LHC Performance Estimates
7
Chamonix, January 2011 Oliver Brüning BE-ABP
Parameter | nominal | 25ns | 50ns | 50ns
N | 1.15E+11 | 1.2E+11 | 1.7E+11 | 1.7E+11
nb | 2808 | 2808 | 1404 | 1404
beam current [A] | 0.58 | 0.61 | 0.43 | 0.43
x-ing angle [mrad] | 300 | 320 | 320 | 270
beam separation [s] | 10 | 10 | 10 | 10
b* [m] | 0.55 | 0.5 | 0.5 | 0.5
en [mm] | 3.75 | 3.75 | 3.75 | 2.5
eL [eVs] | 2.51 | 2.5 | 2.5 | 2.5
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 101 | 71 | 29
IBS longitudinal [h] | 61 -> 60 | 58 | 41 | 25
Piwinski parameter | 0.68 | 0.76 | 0.76 | 0.78
geom. reduction | 0.83 | 0.80 | 0.80 | 0.79
beam-beam / IP | 3.10E-03 | 3.1E-03 | 4.4E-03 | 6.6E-03
Peak Luminosity | 1 1034 | 1.0 1034 | 1.2 1034 | 1.7 1034
nominal emittance
small emittance
Performance reach for existing machines @ 7 TeV:
Radiation
damping:
hor: 26h
ver: 13h
Notes: Smaller than nominal beam current for small emittance beam; aperture margin due to smaller required crossing angle; potential for smaller beta*, less e-cloud effect due to larger bunch spacing; Transverse damping time = 26 h and longitudinal damping time = 13 h; RF noise seems to be small

## Slide 8: LHC Performance Estimates
8
Chamonix, January 2011 Oliver Brüning BE-ABP
Parameter | nominal | 25ns | 50ns | 25ns | 50ns
N | 1.15E+11 | 2.0E+11 | 3.3E+11 | 2.0E+11 | 3.3 E+11
nb | 2808 | 2808 | 1404 | 2808 | 1404
beam current [A] | 0.58 | 1.02 | 0.84 | 1.02 | 0.84
x-ing angle [mrad] | 300 | 420 | 520 | 270 | 320
beam separation [s] | 10 | 10 | 10 | 10 | 10
b* [m] | 0.55 | 0.2 | 0.2 | 0.5 | 0.5
en [mm] | 3.75 | 2.5 | 3.75 | 2.5 | 3.75
eL [eVs] | 2.51 | 2.5 | 2.5 | 2.5 | 2.5
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 25 | 37 | 25 | 37
IBS longitudinal [h] | 61 -> 60 | 21 | 21 | 21 | 21
Piwinski parameter | 0.68 | 1.92 | 1.95 | 0.78 | 0.76
geom. reduction | 0.83 | 0.46 | 0.46 | 0.79 | 0.80
beam-beam / IP | 3.10E-03 | 4.5E-03 | 4.9E-03 | 7.7E-3 | 8.6E-3
Peak Luminosity | 1 1034 | 7.0 1034 | 6.3 1034 | 4.8 1034 | 4.4 1034
small b*
‘large’ b*
Performance reach for LINAC4 + LIU + HL triplet:

## Slide 9: intensity & emittance from injectors
 | spacing [ns] | bunch intensity [1011] | transv. rms norm. emittance [mm]
nominal | 25 | 1.15 | 3.75
available “now” | 25 | 1.20 | 3.75
available “now” | 50 | 1.70 | 3.75
available “now” | 50 | 1.70 | 2.50
w LINAC4 | 25 | 1.40 | 3.75
w LINAC4 | 50 | 2.50 | 3.75
w LINAC4+LIU | 25 | 2.00 | 2.50
w LINAC4+LIU | 50 | 3.30 | 3.75
talk by O. Bruning
could we get 20% more?
HL-LHC class
F. Zimmerman:

## Slide 10: High priority studies in 2011
ultimate intensities at 50 ns and 25 ns bunch spacings
    losses: statistics → J. Muller, optimisation - everybody
    e-cloud with intensity and injected trans. emittance → G. Rumolo
    beam parameters at extraction:
      long. → J. Muller,
      trans. → K. Cornelis (tbc)
transverse emittance blow-up (nominal optics)
    origin for single bunch (simulations and meas.) → B. Salvant
    multi-bunch at different spacings → C. Bhat (leaving…)
low gamma transition optics
    optics optimisation during nominal LHC cycle (21.6 s) → Y. Papaphilippou
    long. stability, voltage program and required long. controlled emittance blow-up for coupled-bunch instabilities → E. S.
    space charge limit (single bunch measurements) → H. Bartosik
    effect on e-cloud instabilities → G. Rumolo

## Slide 11: High priority studies in 2011 – cont.
Long. beam stability in a double RF system
  single bunch stability → T. Argyropoulos
  optimum phase offset during cycle → T.A.
Impedance identification:
  transverse → E. Metral/B. Salvant/N. Biancacci
  longitudinal HOM → J. Muller + N. Monet
Beam loading in the 200 MHz RF system:
  limitations, optimum voltage partition → T. Bohl
Low harmonic RF system in the SPS for PS-SPS transfer optimisation → E.S.
  …

## Slide 12: Nominal intensity now
Voltage
Power

## Slide 13: Ultimate intensity (based on 2010 experience with 25 ns beam)
Voltage
Power

## Slide 14: Power/cavity in 4- & 5- section cavities with P4=P5 (but V4 ≠ V5)
nominal intensity & 0.5 eVs
ultimate intensity & 0.6 eVs