## Slide 1: Update on SPS BPM impedance
B. Salvant for the 2008 impedance team

## Slide 2
Reference:
http://cdsweb.cern.ch/record/1208424/files/CERN-ATS-2009-046.pdf
106 BPH and 96 BPV in the SPS
Low frequency imaginary impedance for a BPH : Zlong/n ~ 1 mΩ, Zx=- 0.1 kΩ/m and Zy=2 kΩ/m.
Separate simulations for a BPV:
Zlong/n~0.5mΩ, Zy= 0.1 kΩ/m and Zx= 0.2 kΩ/m.

## Slide 3: Modelled structure for the BPH
All materials are perfect conductors (except the ceramic spacers)
In fact:
- Electrodes + pipe should be in Stainless Steel
- Casing should be in Anticorodal
Ultrarelativistic beams
Rs=|V|^2/Plosses

## Slide 4: BPH longitudinal (with material losses)
fres (GHz) | Q | Rs (“center”) in Ohm | Rs/Q In Ohm
0.265 | 263 | 1766 | 6.7
0.885 | 482 | 275 | 0.6
0.892 | 493 | 374 | 0.8
1.052 | 773 | 3013 | 3.9
1.062 | 773 | 3591 | 4.6
1.598 | 672 | 804 | 1.2
1.613 | 686 | 11274 | 16.4
1.859 | 896 | 5567 | 6.2

## Slide 5: BPH vertical (with material losses)
fres (GHz) | Q | Rs (“center”) in Ohm | Rs (y=2mm) in Ohm | Abs(DeltaRs(y=2)) /Deltay in Ohm/m | Abs(DeltaRs(y=2)) /Deltay/Q in Ohm/m
0.528 | 465 | 0 | 52 | 26118 | 56.1
0.532 | 483 | 0 | 9 | 4641 | 9.6
1.206 | 1276 | 0 | 21 | 10286 | 8.1
1.258 | 764 | 0 | 10 | 4910 | 6.4
1.271 | 688 | 0 | 5 | 2471 | 3.6
1.414 | 1514 | 0 | 68 | 34172 | 22.6
1.613 | 686 | 11274 | 11339 | 32727 | 47.7
1.665 | 1223 | 0 | 67 | 33402 | 27.3
1.859 | 896 | 5567 | 5590 | 11554 | 12.9

## Slide 6: BPH horizontal (with material losses)
fres | Q | Rs (“center”) | Rs (x=2mm) | Abs(DeltaRs) /Deltay | Abs(DeltaRs) /Deltay/Q
0.885 | 482 | 275 | 282 | 3511 | 7.3
0.892 | 493 | 374 | 378 | 2006 | 4.1
1.598 | 672 | 804 | 815 | 5379 | 8.0
1.613 | 686 | 11274 | 11210 | 32005 | 46.7
1.833 | 905 | 71 | 92 | 10945 | 12.1
1.859 | 896 | 5567 | 5544 | 11285 | 12.6
Quite insignificant change of transverse displacement on shunt impedance

## Slide 7: BPV

## Slide 8
From PhD thesis…

## Slide 9: BPV (with material losses)
fres | Q | Rs (“center”) In Ohm | Rs(center)/Q In Ohm | Rs (y=2mm) In Ohm | Abs(DeltaRs(y=2)) /Deltay In Ohm/m | Abs(DeltaRs(y=2)) /Deltay/Q In Ohm/m | Rs (x=2mm) In Ohm | Abs(DeltaRs) /Deltay In Ohm/m | Abs(DeltaRs) /Deltay/Q In Ohm/m
0.293 | 239 | 90 | 0.4 | 93 | 1571 | 6.6 | 90 | 17 | 0.1
0.298 | 241 | 1595 | 6.6 | 1595 | 142 | 0.6 | 1596 | 240 | 1.0
0.704 | 525 | 0 | 0.0 | 0 | 0 | 0.0 | 17 | 8282 | 15.8
0.715 | 548 | 0 | 0.0 | 0 | 0 | 0.0 | 7 | 3611 | 6.6
1.069 | 654 | 945 | 1.4 | 943 | 1146 | 1.8 | 948 | 1643 | 2.5
1.092 | 667 | 1188 | 1.8 | 1185 | 1692 | 2.5 | 1191 | 1668 | 2.5
1.185 | 610 | 241 | 0.4 | 254 | 6533 | 10.7 | 235 | 3033 | 5.0
1.215 | 624 | 26 | 0.0 | 43 | 8499 | 13.6 | 25 | 680 | 1.1
1.570 | 745 | 0 | 0.0 | 0 | 0 | 0.0 | 0 | 10 | 0.0
1.576 | 724 | 0 | 0.0 | 0 | 0 | 0.0 | 2 | 1087 | 1.5
1.610 | 773 | 0 | 0.0 | 0 | 0 | 0.0 | 0 | 34 | 0.0
1.661 | 686 | 0 | 0.0 | 0 | 0 | 0.0 | 1 | 531 | 0.8
1.871 | 2873 | 0 | 0.0 | 0 | 48 | 0.0 | 0 | 54 | 0.0
1.910 | 2430 | 0 | 0.0 | 0 | 0 | 0.0 | 0 | 148 | 0.1
1.960 | 1993 | 1503 | 0.8 | 1509 | 2584 | 1.3 | 1501 | 1439 | 0.7
Longitudinal
vertical
horizontal

## Slide 10: Effect on the beam  Headtail simulations
Simulations done at the time with small longitudinal emittance (0.15 eVs)
All BPMs are lumped in one location accounting for the respective beta functions.
Linear longitudinal restoring force
No direct space charge

## Slide 11: BPMs alone (vertical plane)

## Slide 12: BPMs alone (horizontal plane)

## Slide 13: Summary
Effect of impedance of BPH and BPV is small on transverse single bunch dynamics
Longitudinal modes :
  Rs~1 to 10 k Ω
  R/Q~ 5 to 20 Ω
  Larger for BPHs than BPVs
  Frequencies above 1 GHz
Transverse modes:
  Modes at 0.5 GHz (vertical for BPH) and 0.7 GHz (horizontal for BPV)
  Rs~1 to 20 kΩ/m
  R/Q~ 5 to 50 Ω/m

## Slide 14: However…
fres (GHz) | Q | Rs (“center”) in Ohm | Rs/Q In Ohm
0.265 | 263 | 1766 | 6.7
0.885 | 482 | 275 | 0.6
0.892 | 493 | 374 | 0.8
1.052 | 773 | 3013 | 3.9
1.062 | 773 | 3591 | 4.6
1.598 | 672 | 804 | 1.2
1.613 | 686 | 11274 | 16.4
1.859 | 896 | 5567 | 6.2
?

## Slide 15: Effect of matching the impedance at electrodes coaxial ports in Particle Studio simulations (BPH)
Electrode coaxial port
Modes are damped by the “perfect matching layer” at the coaxial port
Short bunch (1 cm rms)
SPS bunch (20 cm rms)
Importance to match the BPM electrodes!

## Slide 17: BPH
fres | Q | Rs (“center”) | Rs(center)/Q | Rs (y=2mm) | Abs(DeltaRs(y=2)) /Deltay | Abs(DeltaRs(y=2)) /Deltay/Q | Rs (x=2mm) | Abs(DeltaRs) /Deltay | Abs(DeltaRs) /Deltay/Q
0.260 | 260 | 77 | 0.3 | 77 | 10 | 0.0 | 78 | 354 | 1.4
0.265 | 263 | 1766 | 6.7 | 1767 | 256 | 1.0 | 1766 | 234 | 0.9
0.528 | 465 | 0 | 0.0 | 52 | 26118 | 56.1 | 0 | 0 | 0.0
0.532 | 483 | 0 | 0.0 | 9 | 4641 | 9.6 | 0 | 0 | 0.0
0.885 | 482 | 275 | 0.6 | 277 | 1189 | 2.5 | 282 | 3511 | 7.3
0.892 | 493 | 374 | 0.8 | 377 | 1594 | 3.2 | 378 | 2006 | 4.1
1.034 | 1798 | 0 | 0.0 | 14 | 7065 | 3.9 | 0 | 0 | 0.0
1.052 | 773 | 3013 | 3.9 | 3015 | 1294 | 1.7 | 3014 | 517 | 0.7
1.062 | 773 | 3591 | 4.6 | 3594 | 1559 | 2.0 | 3591 | 67 | 0.1
1.206 | 1276 | 0 | 0.0 | 21 | 10286 | 8.1 | 0 | 0 | 0.0
1.258 | 764 | 0 | 0.0 | 10 | 4910 | 6.4 | 0 | 0 | 0.0
1.271 | 688 | 0 | 0.0 | 5 | 2471 | 3.6 | 0 | 0 | 0.0
1.414 | 1514 | 0 | 0.0 | 68 | 34172 | 22.6 | 0 | 0 | 0.0
1.598 | 672 | 804 | 1.2 | 809 | 2404 | 3.6 | 815 | 5379 | 8.0
1.613 | 686 | 11274 | 16.4 | 11339 | 32727 | 47.7 | 11210 | 32005 | 46.7
1.638 | 982 | 0 | 0.0 | 4 | 1844 | 1.9 | 0 | 0 | 0.0
1.665 | 1223 | 0 | 0.0 | 67 | 33402 | 27.3 | 0 | 0 | 0.0
1.801 | 3024 | 0 | 0.0 | 11 | 5458 | 1.8 | 0 | 0 | 0.0
1.833 | 905 | 71 | 0.1 | 71 | 159 | 0.2 | 92 | 10945 | 12.1
1.859 | 896 | 5567 | 6.2 | 5590 | 11554 | 12.9 | 5544 | 11285 | 12.6
Longitudinal
vertical
horizontal

## Slide 18: Longitudinal
Frequency (GHz) | Rs (Ohm) (PEC) | Q (PEC) | R/Q (Ohm)
1.04 | 1.6 104 | 3150 | 5
1.61 | 4.6 104 | 2690 | 17
1.81 | 2.5 104 | 3357 | 7
Time domain (CST PS)
Frequency domain eigenmode solver at the peaks (CST MWS)

## Slide 19: Dipolar vertical impedance (PEC)
Frequency | Rs (Ohm) (PEC) at y=1mm | Rs (Ohm) (PEC) at y=4 mm | Q (PEC) | Rs/Q (Ohm/m)
0.53 |  |  |  | 
1.03 |  |  |  | 
1.2 |  |  |  | 
1.92 |  |  |  | 

## Slide 20: Longitudinal (with losses)
Frequency | Rs (Ohm) (PEC) | Rs (Ohm) (with losses) | Q (PEC) | Q (with losses) | R/Q (Ohm)
1.04 | 8.2 104 | 1.96 104 | 3080 | 740 | 27
1.61 | 378 | 88 | 2620 | 610 | 0.14
1.81 | 4.9 105 | 1.2 105 | 3380 | 820 | 145
Electrodes + pipe  Stainless Steel
Casing  Anticorodal