## Slide 1: Review of 2011 studies and priorities for 2012
LIU-SPS-BD

## Slide 2: Main results from 2011 (B. Goddard, LIU-SPS, 7.12.2011)
LHC can digest half-nominal transverse emittance
SPS can deliver nominal 25 ns intensity in ~3 um, and almost ultimate 50 ns intensity in 2 um
Smaller emittances in SPS for 50 and 25 ns beams
(Where) has the e-cloud gone?
E-cloud mitigation industrialisation works
Q20 optics deployment progress
Q20 instability limits progress
PS-SPS longitudinal transfer studied
Limits still there from MKE heating and ZS sparking
BI upgrades are not for overnight
Transverse emittance measurement crucial, but still shaky
High bandwidth feedback needs kick-start for implementation

## Slide 3: Discussion points
Brightness:
  Can we draw all the limitation curves in the intensity-emittance diagram for 25 and 50 ns? Do we know by how much the upgrades will move them??
Smaller emittances in 2011:
  Are we confident this is a real change, or the BI ‘improvements’?
  (LHC emittances confirm 2 – 2.5 um from SPS, but what was in 2010?)
E-cloud in 2011
  Where has it gone?
Q20 optics:
  Are results for single- and multi-bunch beams as expected (emittances, instabilities, losses, RF)?
PS-SPS longitudinal transfer
  What are the implications of the results on capture losses?

## Slide 4: E-cloud in 2011 (B. G.)
Where has it gone?
  What SEY values are consistent with observed thresholds?
  Are these SEY values explainable from ‘operational’ 50 ns scrubbing?
    Saw this for LHC where initial 25 ns injection was much easier than 50 ns
What are the essential things to demonstrate in 2012?
  Scrubbing test period
    Effective scrubbing with lower average beam power?
    Quantification of SEY values and ecloud density
    Measurement techniques (stable phase??)
    Performance reach for 25 ns beams
  Mitigation measure tests
    Validation of coated dipoles with in-situ monitors
    Understand vacuum pressure at coated dipoles – theoretical progress? Desorption?
    Removal of coatings, magnet measurement of coated dipoles, ...
Big decision to make at end of 2012..coat or scrub.
  High bandwidth feed-back: need urgently to define project plan in detail

## Slide 5: Limits from MKE and ZS (B. G.)
MKE heating should cease to be a limit for 2014
  Any detailed impedance measurements planned to check differences 2011-2012?
ZS sparking problematic for ‘operatically driven’ intensity increases
  Modulation of voltage on PPM basis for ion traps only
  Negative bump at ZS not tested – plan for 2012?
  Longer term – not much prospect of major improvement
Should we plan new filling schemes for these ‘total intensity’ limits (e.g. 3 batches only?!)
What about longer bunches or more bunch shape control?

## Slide 6: Q20 optics
Excellent results for
  single bunch stability and emittances
  multi-bunch LHC beams (1.8 x1011 at 450 GeV for 50 ns beam!)
  need to set-up: controlled longitudinal emittance blow-up
  working point optimisation (“space charge” limit)
  dedicated optimisation and studies in 2012 for Q20
  how many efforts should still go to Q26?
When we will be ready to inject to LHC?
  transfer lines
  capture losses in LHC - MDs
  batch-by-batch longitudinal emittance blow-up in the LHC
  (could be feasible, but not very clean – P. Baudrenghien)?
Other SPS cycles: ions, FT&CNGS, LHC pilot?

## Slide 7: Priorities for 2012
Test scrubbing as e-cloud mitigation
Q20 multi-bunch injected to LHC, tested for other cycles – different MD scheme (H.B.)?
Push up intensity for 25 ns beam (Q20?) to see possible limitations – the way to go after LS1 (clear message from LHC experiments about role of pile-up)
Double RF system
  stability
  controlled emittance blow-up
Impedance identification (reference measurements < LS1)
=>

## Slide 8: Priorities for 2012
Test scrubbing as e-cloud mitigation
Q20 multi-bunch injected to LHC, tested for other cycles – different MD scheme (H.B.)?
Push up intensity for 25 ns beam (Q20?) to see possible limitations – the way to go after LS1 (clear message from LHC experiments about role of pile-up)
Double RF system
  stability
  controlled emittance blow-up
Impedance identification (reference measurements < LS1)
=> Happy New Year!