## Slide 1: Emittance and intensity dependence of PS-to-SPS transfer
Helga Timkó
BE-RF-BR
in collaboration with
Theodoros Argyropoulos, Thomas Bohl, Heiko Damerau, Steven Hancock, Juan Esteban Müller, Elena Shaposhnikova

## Slide 2: Measurement conditions
Dedicated cycle: LHCMDION
  Single batch, 50 ns spaced LHC-type beam, 36 bunches
  Intensity: ~1.6 1011 ppb, unless stated otherwise
  Varying the PS rotation timings t40 MHz and t80 MHz
  SPS voltage as usual
  SPS FB is shortened to 1260 ms
  SPS acceleration ramp only until at 30 GeV
Bunch length:
  at PS ejection
Transmission:
  (intensity at 30 GeV) / (injected intensity)

## Slide 3: Reminder
Gain:
TOP ≈ 94.8 % (1+2 cav’s)
TMAX = 97.7 % (2+2 cav’s)
Highest loss reduction was achieved when switching on the spare 40 MHz cavity

## Slide 4: Why did we not see an improvement earlier?
Reproducing last year’s MD results: optimising t80MHz based on τ doesn’t help; need to optimise t40MHz as well

## Slide 5: Best settings: 2+2 cavities
Even with an emittance increased by 50 %, we can achieve similar transmission to currently operational settings!

## Slide 6: Intensity dependence
About ~ 15 % intensity margin for the same transmission

## Slide 7: Conclusions
We have performed 7 MDs with a dedicated cycle, 1 batch
  Results are reproducible and consistent with simulations
  Preferred settings:
    V40MHz = 600 kV, V80MHz = 600 kV, t40MHz = 130 μs, t80MHz = 90 μs
    Gain: transmission 94.8  97.7 %, losses 5.2  2.3 %
  We understand now the results of previous years and know what we have to do differently
  With the new settings, we gain also a significant emittance and intensity margin
Our studies with the test cycle are now complete (for Q26)
Need to test the new scheme with 4 batches, filling-type scenario