## Slide 1: MDs in 2013
E. Shaposhnikova
LIU- SPS-BD WG meeting
13.12.2012

## Slide 2: The 2012 requests should be based on results of MDs in 2011
MDs in 2011 not yet completed, but only one dedicated period is left (W45, ions), probably one floating MD and some parallel MDs
Pending issues:
  limitations for ultimate 50 ns and 25 ns beams in Q26
    involves a lot of time for optimization (tunes and chroma settings, voltage program, LLRF, controlled emittance blow-up)
  multi-bunch beams in Q20 optics:
    longitudinal stability limits with 800 MHz off and on
    transverse damper set-up
    transverse emittance blow-up, e-cloud
  PS-SPS transfer:
    SPS transmission as a function of PS parameter space
    requires optimisation in the SPS (simulations started)
  space charge limit (for HL-LHC scaling)

## Slide 3: Some important questions
Do we continue in 2012 MDs with two optics in parallel?
  need significantly more time and manpower
  but probably not ready yet to go for Q20
Validation of e-cloud mitigation (coating)
  is e-cloud still a limitation?
    transverse emittance blow-up (50 ns vs 25 ns)
    losses (need careful setting-up)
  would it be a limitation in future (HL-LHC beam)?
  what can be achieved by scrubbing
  role of high bandwidth transverse feedback

## Slide 4: Proposed MD studies for 2012 (1/3)
re-establish low-loss nominal 25 ns beam (careful OP and LLRF set-up)
scrubbing (reference measurements for e-cloud) – 3 days?
limitations with “above nominal” intensity beams, increase of intensity in steps with time for optimisation (50 ns beam with 1.4E11 is operational)
  50 ns and then 25 ns beam
  each MD block, 24 hours minimum
e-cloud mitigation
  transverse emittance blow-up (systematic measurements during each MD with BI expert)

## Slide 5: Proposed MD studies for 2012 (2/3)
impedance identification (transverse + HOM longitudinal)
  transverse – parallel MDs
  longitudinal - with 50 ns and 25 ns beam of variable (low) intensity
TMCI – single bunch - parallel MDs
  threshold in a double RF system
  multi-bunch stability
double RF system
  stability (for high intensity beams)
  controlled emittance blow-up
working point optimisation (“space charge” limit)

## Slide 6: Proposed MD studies for 2012 (3/3): low gamma transition
optics studies (tunes, chromaticity, orbit)
transverse damper
ultimate LHC beams (long dedicated MDs)
minimum longitudinal emittance/bunch length at 450 GeV/c sufficient for beam stability
different optics for fast cycles?
e-cloud stability
SPS-LHC beam transfer : any problems with lower emittance (IBS, stability) or longer bunches (losses) in LHC itself?

## Slide 7: Priorities for 2012
Test scrubbing as e-cloud mitigation
Q20 multi-bunch injected to LHC, tested for other cycles – different MD scheme (H.B.)?
Push up intensity for 25 ns beam (Q20?) to see possible limitations – the way to go after LS1 (clear message from LHC experiments about role of pile-up)
Double RF system
  stability
  controlled emittance blow-up
Impedance identification (reference measurements < LS1)

## Slide 8: Priorities for MDs in 2013 (one month period)
Reference impedance measurements (quadrupole synchrotron frequency shift) in Q26 with single bunches of:
  variable, in range (1-15)x1010 , intensity (relatively easy)
  constant small (0.25 eVs) longitudinal emittance (difficult)
Impedance identification: long bunches with RF off in Q20 (very high intensity ~ 8x3x1011)
Single bunch stability in Q26 and Q20 (effect of bunch distribution due to the PS bunch rotation)
Single bunch stability in double RF system (Q26&Q20)
Happy New Year!