## Slide 1: (Quick?) update on the PS-to-SPS transfer MDs
Helga Timkó
BE-RF-BR
in collaboration with
Theodoros Argyropoulos, Thomas Bohl, Heiko Damerau, Steven Hancock, Juan Esteban Müller, Elena Shaposhnikova

## Slide 2: Measurement conditions
We have a dedicated cycle now, LHCMDION, for systematic measurements under stable conditions
  Single batch, 50 ns spaced LHC-type beam, 36 bunches
  Intensity: 1.6-1.7 1011 ppb
  Varying the PS rotation timings t40 MHz and t80 MHz
  SPS voltage as usual
  SPS FB is shortened to 1260 ms
  SPS acceleration ramp only until at 30 GeV
Bunch length:
  at PS ejection
Transmission:
  (intensity at 30 GeV) / (injected intensity)

## Slide 3: 140 MHz, 280 MHz cavities
Gain:
TOP = 96.2 %
TMAX = 97.1 %

## Slide 4: … in agreement with the previous MD & simulations…
Previous MD w/ 25 ns, different intensity, cycle, etc.
Simulated T & τ
FAIRLY REPRODUCIBLE!

## Slide 5: 140 MHz, 380 MHz cavities
Gain:
TOP = 95.4 % (1+2 cav’s)
TMAX = 96.3 % (1+3 cav’s)
N.B. we used larger εlong than operational, also for measuring TOP
 not a perfect reference

## Slide 6: 240 MHz, 280 MHz cavities
Gain:
TOP ≈ 94.8 % (1+2 cav’s)
TMAX = 97.7 % (1+3 cav’s)
As predicted by sim’s…
N.B. we used larger εlong than operational, but not for TOP

## Slide 7: Loss balance
Simulated:
  LOP = 4.4 %
  LMIN,1+2cav = 3.5 %
  LMIN,1+3cav= 2.1 %
  LMIN,2+2cav = 1.9 %
  LMIN,2+3cav = 1.3 %
Measured:
  1+2 cav.: 3.8  2.9 %
  1+3 cav.: 4.6(?)  3.7 %
  2+2 cav.: 5.2  2.3 %
Optima in the predicted places
Optimum ‘corridor’ slope as expected, too

## Slide 8: Conclusions
We have now a set of systematic, reproducible measurements for different voltage options
  The ‘2+2 cavity’ case shows significant improvement
  The ‘1+3 cavity’ case should be repeated for completeness
  An additional measurement of the optimal timings with different voltages and one single reference point is also necessary to correctly estimate the gain in the different cases
We used larger εlong than usual for the measurements with spare cavities
  For 1+2 cavities, once we also tried the optimal timing when additional blow-up was applied in the PS; the transmission got slightly worse
  Need further studies on the emittance margin
Only 3 weeks left to complete our studies, to verify the above!