## Slide 1: Plans for the MDs on impedance
Benoit, Elias, Giovanni, Hannes, Nicolo, Yannis

## Slide 2: Transverse impedance MDs in 2011
MDs in 2011 focused on the optimization of the Q20 and the TMCI threshold
2 transverse impedance parallel MDs in 2011 (Nicolo and Hannes, ~12h)
  Transverse tune shifts as a function of intensity for Q20 and Q26
  Attempt at impedance localization, but turned out to be very difficult (need for BI support)

## Slide 3: Plans for transverse impedance MDs in 2012
Significant improvements of the Headtail simulation tool are being implemented (Nicolo, Nicolas) see HDWG talk tomorrow
Requests for MDs (in order of priority):
  Transverse tune shift with intensity following the shielding of 2 MKE kickers and ZS in LSS6 in order to:
    Confirm the difference observed between the effective impedance computed from Q20 and Q26 measurements, and check the effect of other optics (split tunes in particular)
    Measure the horizontal plane and check the predicted change of sign of the effective impedance with shielded MKEs
    Check the effect of bunch length, longitudinal distribution, energy
    Reference measurements before LS1
  Impedance localization
    ask for help from BI/QP to try to optimize the signals from the MOPOS system to conclude on the feasibility of the technique for SPS
    Assess the possibility to use scraping and multiple kicks to get rid of the cycle to cycle reproducibility issues
  Growth rates with chromaticity
    Enable to measure the frequency dependence of the real and imaginary part of the transverse impedance
    Check the effect of bunch length and longitudinal distribution
   Request for at least 8 parallel MDs with the MD1 cycle (short flat bottom without acceleration)