## Slide 1: 2012 SPS scrubbing run Collecting ideas …
H. Bartosik, G. Iadarola
SPSU meeting, 26.1.2012

## Slide 2: Beam scenarios
25ns beam
  With 4 batches with nominal settings as reference
  With shorter bunch length
  25ns + 5-10% uncaptured beam
  Increasing the number of batches (up to 6 if feasible)
  With high intensity (up to maximal achievable in PS)
5ns fast extracted beam injected at 26 GeV
  Feasibility in the PS is currently investigated by PS experts
  Potential problem of retuning the 200 MHz cavities (4 out of 6 cavities need access to be retuned)
  Can we keep gap for extraction kicker rise-time in PS in order not to destroy the extraction septum
  Possible complications in the SPS? (LLRF, feedback, beam loading, …)
  Limited total intensity? Need at least 5e10 p/b …
  To be checked more carefully in simulations if efficiency at low SEY (rise time is quite long already for SEY=1.5, where 2 batches are needed) is really improving
10+15ns bunch spacing
  Probably not feasible within given timeframe …
  Also to be checked in simulation if half nominal intensity is sufficient for efficient scrubbing
50ns beam will be kept for a few cycles after LHC filling to study electron cloud build-up in strip monitors with magnetic field

## Slide 3: Beam scenarios
Nominal 25ns beam

## Slide 4: Beam scenarios
5ns beam
5e10 ppb
SEYmax = 1.5

## Slide 5: Beam scenarios
Effect of 10% uncaptured
SEYmax = 1.5

## Slide 6: Beam scenarios
Effect of 10% uncaptured
SEYmax = 1.5
More evident at low SEY!

## Slide 7: Beam scenarios
Effect of bunch shortening
SEYmax = 1.5

## Slide 8: Machine cycles
Long flat bottom cycle (maximal possible length allowed by supercycle timings)
  Will be used most of the time for direct comparison of scrubbing schemes, as electron cloud build-up is not expected to depend on beam energy
  Up to 6 batches if allowed by machine interlocks
  Varying batch spacing to study rise-time of electron cloud build-up
Coasting beam
  In case we do not see emittance blow-up or instability on long flat bottom cycle, a coasting beam with and without uncaptured beam could be tried
Nominal LHC acceleration cycle with 4 batches

## Slide 9: Draft schedule
Time | Day 1 | Day 2 | Day 3 | Day 4 | Day 5
Daytime | Preparation of beam and setup, it will be the first time of 25ns beam in the SPS in 2012?!?! | Machine conditioning … Ramp up total intensity (+ studies if allowed by machine condition) | Study of 10% uncaptured beam with as many batches as allowed by the machine (vacuum, heating, …) + higher intensity | Exotic beam (either 5ns bunch spacing or 10+15ns) | Exotic beam (either 5ns bunch spacing or 10+15ns)
Nights | Machine conditioning with nominal intensity and as many batches as possible (kickers, ZS, …) | Reference measurements (comparison with nominal beam) | Reference measurements (comparison with nominal beam) | Reference measurements (comparison with nominal beam) | Reference measurements (comparison with nominal beam)

## Slide 10: Electron cloud observables I
Electron cloud observation
  Electron current in 4 strip monitors – at injection B field
  (if feasible, partly used in time resolving mode)
    Fresh StSt liner
    Fresh clearing electrode (with W liner)
    Long term a-C liner
    Miguels configuration
  a-C coated with solenoids installed before scrubbing run
    Round vacuum chamber (r=159mm)
    Equipped with e-cloud pick-up
    Vacuum gauges
    Which tests should be done?
  Time resolved e-cloud build-up along bunch train
    Setup similar to what is used in the PS could be (re)-installed in the SPS
    Need to borrow electronics from PS setup
  Pressure measurements with Penning gauges, switch off vacuum pumps close to strip monitors to study dependence of e-cloud on residual gas pressure
  Revive microwave measurement on dipole magnet
Scrubbing run 2008
C. Vallgren et al.

## Slide 11: Electron cloud observables II
Observation of electron cloud through the beam
  Incoherent effects  emittance blow-up
    transverse emittance to be monitored continuously
    if possible measure bunch by bunch to identify e-cloud build-up along the batch
  Coherent instability
    damper pick-ups
    head-tail monitor
    threshold chromaticity for stabilizing the beam
  Beam loss at injection
    Uncaptured beam
  Tune shift along bunch train
    Using transverse damper pick-up for analyzing turn-by-turn, bunch-by-bunch beam position data
Could be tried
  “Impedance localization” using all BPMs in the ring (feasibility to be checked, limited number of turns?)

## Slide 12: General points for discussion
Closed orbit steering or radial steering for scanning the surface of the liners for studying local scrubbing effects
  In some scrubbing scenarios the width of the bombarded area is narrow compared to nominal beam  a “sweep” of the beam across the vacuum chamber may become necessary
  Also to understand how localized is the scrubbed region
Transverse emittance blow-up towards the end of the run to see dependence of electron cloud build on beam size close to threshold
Best method to produce 5-10% uncaptured beam
  Longer bunches from PS or low voltage (phase) at SPS capture …
Other observables … ?