## Slide 1: Final steps for making Q20 operational
T. Argyropoulos, W. Bartmann, H. Bartosik, T. Bohl, C. Bracco,
J. Esteban Muller, E. Gianfelice-Wendt, B. Goddard, V. Kain,
Y. Papaphilippou, E. Shaposhnikova, G. Vanbavinckhove
LIU-SPS-BD August 15, 2012

## Slide 2: Final steps for making Q20 operational
Final checks on extraction conditions
  Aperture in extraction channels (DONE)
  Steering in transfer lines with final extraction settings (WHEN INJECTING INTO LHC)
Preparation and setup of probe cycle with Q20 optics (IN PREPARATION)
Study bunch length and transverse emittance evolution on LHC flat bottom (TEST FILL)
  Measure transverse emittance growth on LHC flat bottom
  Find optimal settings for controlled longitudinal blow-up in SPS to minimize IBS
Fill 2944
from Q20 – short bunches
(≈1.58e11 p/b)
from Q20 – long bunches
Fill 2947
(≈1.58e11 p/b)

## Slide 3: Final steps for making Q20 operational
Final checks on extraction conditions
  Aperture in extraction channels (DONE)
  Steering in transfer lines with final extraction settings (WHEN INJECTING INTO LHC)
Preparation and setup of probe cycle with Q20 optics (IN PREPARATION)
Study bunch length and transverse emittance evolution on LHC flat bottom (TEST FILL)
  Measure transverse emittance growth on LHC flat bottom
  Find optimal settings for controlled longitudinal blow-up in SPS to minimize IBS
Test ramp and going into collisions to qualify the beam from Q20 (TEST FILL)
  Small issue with tune feedback on test ramp during LHC MD – coincidence?
Minimize impact on other physics users (DONE)
  No particular disturbance on physics users was observed during tests last week

## Slide 4: Additional items to consider
Optimize RF settings if blow-up in SPS is needed/wanted
  Total spread of bunch lengths smaller compared to Q26
  Systematic increase along train when using controlled longitudinal blow-up
  Reason for increasing bunch length not clear yet
No controlled blow-up: εl≈0.37eVs
N≈1.58x1011p/b
SPS flat top – Q20
Controlled blow-up: εl≈0.48eVs
N≈1.58x1011p/b
SPS flat top – Q20

## Slide 5: Additional items to consider
Optimize RF settings if blow-up in SPS is needed/wanted
  Total spread of bunch lengths smaller compared to Q26
  Systematic increase along train when using controlled longitudinal blow-up
  Reason for increasing bunch length not clear yet
SPS flat top – Q20
N≈1.58x1011p/b
SPS flat top – Q26
Controlled blow-up: εl≈0.48eVs
No controlled blow-up: εl≈0.37eVs
N≈1.58x1011p/b
SPS flat top – Q20

## Slide 6: Additional items to consider
Optimize RF settings if blow-up in SPS is needed/wanted
  Total spread of bunch lengths smaller compared to Q26
  Systematic increase along train when using controlled longitudinal blow-up
  Reason for increasing bunch length not clear yet
Prepare 25ns beam nominal intensity with Q20 optics
Choose the best moment to start with Q20
  Should be ready with 25ns beam for scrubbing run and LHC MDs with 25ns beam after TS3
  Avoid switching back and forth several times (consider also ion beams, …)
TODAY