## Slide 1
IBS and Touschek studies for the ion beam at the SPS
F. Antoniou, H. Bartosik, Y. Papaphilippou, T. Bohl
Notes: 1

## Slide 2
2
Intra-beam scattering
Two different approaches for the probability of scattering:
  Classical approach (Piwinski):
    Rutherford cross section
  Quantum approach (Bjorken-Mtingwa):
    The relativistic “Golder Rule” for the 2-body scattering process
  The tracking codes use the classical Rutherford c.s. as well
Small angle multiple Coulomb scattering effect
  Redistribution of beam momenta
  Beam diffusion
    Luminosity decrease in colliders
    Brightness reduction in light sources
Several theoretical models and approximations developed over the years
  At strong IBS regimes not always agreement between them
  Gaussian beams assumed
  Betatron coupling not included
Multi-particle tracking codes recently developed (SIRE, IBStrack-CMAD) to study interesting aspects of IBS such as:
  Impact on beam distribution and on damping process
  Include coupling
Notes: 2

## Slide 3
3
IBS calculations with and w/o SR
If = 0
Steady State emittances
If ≠0
All theoretical models consider the uncoupled frame and Gaussian beams!
The IBS growth rates in one turn (or one time step)
Complicated integrals averaged around the ring.
Horizontal, vertical and longitudinal equilibrium states and damping times due to SR damping
w/o synchrotron radiation this term is not needed
Notes: 3

## Slide 4: IBS calculations for Q20 & Q26 optics
Emittance evolution with time for the Q20 (left) and Q26 (right) optics for same initial parameters
  Based on Piwinski formalism
The effect is smaller for the Q20
  Due to larger beam sizes and dispersion
Damping is expected in the longitudinal plane
  The effect is small to be observed

## Slide 5: IBS for measured current
For the measured current using the measured bunch length at t=0 as input, the expected bunch length evolution with time due to IBS is calculated both for the Q26 (blue) and the Q20 (red).
The expected IBS growth factors for the three planes and the two optics are shown in the right plot

## Slide 6: Touschek lifetime calculations
The Touschek effect refers to single particle Coulomb scattering events with large exchange of momentum between the particles
  Particles go off the bucket and get lost  Lifetime reduction
The general lifetime expression:
Touschek term
α: Touschek factor
Other effects
b: Lifetime at low current

## Slide 7: Touschek lifetime calculations
Non-relativistic round beam approach
Ref: “The Touschek effect in strong focusing storage rings”, A. Piwinski, DESY 98-179, Nov. 1998
Acceptance
Particle/bunch

## Slide 8: Touschek lifetime calculations
Touschek parameter
The Touschek parameter is calculated from the comparison of the general lifetime and the touschek lifetime expressions

## Slide 9: Lifetime calculations
Touschek fit is applied to the current decay data with time
  Bunch length and acceptance are considered constant
The behavior is similar to Touschek especially for the Q20
The Q26 is also not far but the decay in the first seconds is faster than touschek
QQ20
QQ26

## Slide 10: Touschek parameter for data – Q26
Q26
The bunch length changes with time
The touschek parameter depends on bunch length, thus, is calculated for each data point
Transverse emittances and acceptance are considered constant with time
Calculations are done for three different acceptance values
Q26

## Slide 11: Touschek parameter for data – Q20
Q20
The theoretical touschek parameter for each measured bunch length for Q20 optics
Transverse emittances and acceptance are considered constant with time
Calculations for three different acceptance values
Q20

## Slide 12: Touschek lifetime Vs data – Q26
From the α parameter calculated before, the current decay with time is calculated for three different acceptance values.
Ignoring the first seconds (starred curves), we can find parameters for a Touschek fit to the data
  For larger acceptance the first seconds become less Touschek dominated

## Slide 13: Touschek lifetime Vs data – Q20
In the case of Q20, the data fit well to a Touschek behavior almost from the beginning
  Less injection losses?
The dependence on the b parameter is less pronounced
  Due to the fact that is Touschek dominated almost from the begining

## Slide 14: Outline
The expected IBS effect is smaller in Q20 than in Q26 (especially in the transverse plane) due to larger beam sizes and dispersion
However, IBS cannot explain the bunch shortening observed
  Even though it predicts bunch shortening the expected effect is much smaller than the observed one
The current decay with time can be fitted by a Touschek curve
  Q20 follows the Touschek lifetime behavior better than Q26 from the first seconds
  In Q26 the current decays faster than what Touschek predicts in the first seconds
  More injection losses for Q26 than Q20?
  Both seem to follow the 0.9% acceptance curve better

## Slide 15
Thank you!!!