## Slide 1: First PS-to-SPS Transfer MD
Helga Timkó
BE-RF-BR
in collaboration with
Theodoros Argyropoulos, Thomas Bohl, Heiko Damerau, Steven Hancock, Juan Esteban Müller, Elena Shaposhnikova

## Slide 2: Outline
Reminder of simulation results
Report on the MD of 29th March 2012
  Aim: Optimise the PS bunch rotation timings
  Measurement conditions
  Results and preliminary conclusions
Why further MDs are needed

## Slide 3: WHAT SIMULATIONS PREDICT
PS-TO-SPS TRANSFER:

## Slide 4: Optimising the PS bunch rotation timings
For 1+2 cavities, optimal timing reduces losses: 4.4 %  3.5 %
Using 2+3 cavities instead of 1+2:
3.5 %  1.3 %
Transmission can be improved even w/o more voltage

## Slide 5: Optimised bunch shapes
… now improved:
tails less populated

## Slide 6: WHAT WE MEASURE
PS-TO-SPS TRANSFER:

## Slide 7: Measurement conditions
Single batch, 25 ns spaced LHC-type beam, 72 bunches
  Nominal intensity, 1.1  1011 ppb
In the PS: voltage programme as ‘usual’
  Varying the rotation timings t40 MHz and t80 MHz
In the SPS: FB voltage was 2 MV at injection, then immediately increased to 3 MV (“usual” procedure)
  V800 MHz = 0.35 MV In bunch-shortening mode
Bunch length: measured at ejection from the PS with BSM
  Cross-checked with bunch length measured at SPS injection
Transmission: logged from “LARGER” at the end of the FB (26 GeV) and at 62 GeV
  Cross-checked with BCT data

## Slide 8: Transmission
The transmission at 62 GeV is the relevant quantity for us, since it includes losses from the acceleration ramp

## Slide 9: Transmission & bunch length
Better transmission can sometimes require longer bunches
Currently operational
Optimum predicted by simulations

## Slide 10: Comparison with simulations
Systematically shorter bunches in this MD than earlier
In (b), we could fit the simulated curve, but also a constant
In (b), higher transmission for t40 MHz = 150 μs than expected
  Measurement needs to be repeated
Unexpectedly high transmission

## Slide 11: Comparison with simulations
Simulations predict a maximum ~ t40 MHz = 170-190 μs, t80 MHz = 120 μs
Note: longer bunches, since we took the distributions of a previous MD
Effect is small with the current intensities (order of error bars); need very accurate measurements to verify this

## Slide 12: Conclusions
The first measurements are encouraging
  At least, they don’t contradict the simulations
  No conclusive results yet
However, measurements are ‘tricky’
  We’re looking at percent-level differences
  We have only percent-level accuracy
  Need extremely stable beam conditions and need to ensure that the losses in the transverse plane are constant
Further measurements are planned for the future
  Repeat the above & do the same scan with higher voltage