## Slide 1: Where are we on the impedance of the new design of the SPS wirescanner
Mauro Migliorati, Benoit Salvant and Carlo Zannini for the impedance team
Many thanks to Hannes Bartosik, Nicolas Critin, Heiko Damerau, Bernd Dehning, Federico Roncarolo and Ray Veness

## Slide 2: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 3: New Model (LHC)
CATIA model from Nicolas Critin
Model heavily simplified to be able to mesh the geometry
Only one longitudinal gap (2.3 mm)
Wire and gaps difficult to mesh

## Slide 4: Results
Significant low frequency mode due to the longitudinal gap:
  Shunt impedance (longitudinal): 250 kOhm
  Quality factor: 2500
  Frequency: 140 MHz
Quite worrying as is (for longitudinal coupled bunch instabilities)
Possibility to use ferrites (like in wall current monitor) or mode couplers to damp the mode

## Slide 5: Solutions with ferrite?
Frequency (GHz)
Frequency (GHz)
Re(Zlong) in Ohm
Re(Zlong) in Ohm
With ferrite in green
With less ferrite in red
To be checked if these solutions can be implemented
To be compared with the current wire scanner design

## Slide 6: New model for SPS
Same as LHC but bigger aperture
Resonance now at 80 kOhm at around f=160 MHz (Q=1300), without ferrites.

## Slide 7: Proposal of Heiko and Hannes
Frequency in GHz
Longitudinal impedance in Ohm
 Better than the initial solution, still worse than the current design
 However, solution not feasible for BI (“the fork should rotate completely around the axis”)

## Slide 8: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 9: Current design (also simplified)
Wakefield simulations
Very high Q resonances, solver
Resonant frequencies are much lower for the new design

## Slide 10: Subtleties of the current design
Taper in 416 H
vertical fork much wider than horizontal fork
 resonance frequency change
416H Wire out
416 Wire in

## Slide 11: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 12: Comparison for the resonant modes (no ferrites)
Frequency | Shunt impedance (kOhm) | Q | Fields close to the wire? | Power loss at 450 GeV (from LHC spectrum)
140 MHz | 250 | 2500 | No | 60 kW
470 MHz | 15 | 3500 | Yes (partly H) | 0.3 kW
Frequency | Shunt impedance (kOhm) | Q | Fields close to the wire? | Power loss at 450 GeV (from LHC spectrum)
290 MHz | 18.5 | 1660 | Yes | 1.3 kW
658 MHz | 55 | 7000 | Yes | 0.8 kW
682 MHz | 146 | 5500 | Yes | 2.4 kW
1020 MHz | 210 | 12000 | Yes | 0.5 kW
New design
Current design
 Hopefully there are ferrites to partially damp these modes!
 Need to do that also for the SPS spectrum at injection energy?

## Slide 13: Spectrum at injection
8
72
8
72
72
8
72
25ns buckets
From C. Zannini
First lobe of the beam spectrum after around 700 MHz

## Slide 14: Comparison for the resonant modes (no ferrites) modes also significant at injection?
Frequency | Shunt impedance (kOhm) | Q | Fields close to the wire? | Power loss at 450 GeV (from LHC spectrum)
140 MHz | 250 | 2500 | No | 60 kW
470 MHz | 15 | 3500 | Yes (partly H) | 0.3 kW
Frequency | Shunt impedance (kOhm) | Q | Fields close to the wire? | Power loss at 450 GeV (from LHC spectrum)
290 MHz | 18.5 | 1660 | Yes | 1.3 kW
658 MHz | 55 | 7000 | Yes | 0.8 kW
682 MHz | 146 | 5500 | Yes | 2.4 kW
1020 MHz | 210 | 12000 | Yes | 0.5 kW
New design
Current design
 Hopefully there are ferrites to partially damp these modes!

## Slide 15: Simulated power loss with 50 ns SPS beam with ferrite as a function of bunch length
Still between 50 and 100 W in the ferrite
Is that ok with the duty factor of LHC beams in the SPS?
Would cooling be needed and is it possible to cool there?
Carlo Zannini

## Slide 16: Power loss (with ferrites)
New design
modified design (Heiko)
Current design
Predicted for post LS1
HL-LHC

## Slide 17: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 18: New design
H field
E field
138 MHz
472MHz
H field
E field

## Slide 19: Old design
All fields for all modes are located around the wire forks
Ferrite location not ideal.
293 MHz
658 MHz
1018 MHz
681 MHz

## Slide 20: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 21: Previous measurements by Federico et al in 2003
Frequency Of main modes | Shunt impedance (kOhm) | Q
290 MHz | 18.5 | 1660
658 MHz | 55 | 7000
682 MHz | 146 | 5500
1020 MHz | 210 | 12000
 Modes around 700 MHz
To be checked with the actual location of shielding and ferrite
To be checked with simulations of transmission measurements
Cavity Mode Related Wire Breaking of the SPS Wire Scanners and Loss Measurements of Wire Materials" F. Caspers, B. Dehning, E. Jensen, J. Koopman, J.F. Malo, F. Roncarolo - Proc DIPAC 2003
Simulation results (from eigenmode, 2013)

## Slide 22: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 23: Example of Wall current monitor (J. Belleman - BI) impedance reduction of the pipe interruption with coaxial line
 This reduction of the impedance of the gap does not seem possible with the wire scanner

## Slide 24: Agenda
New design
Current design
Power loss
Mode geometry
Previous measurements
Comparison with wall current monitor
Summary

## Slide 25: Outlook
New design of wire scanner seems very unfavourable from the impedance point of view due to the abrupt unmatched beam pipe interruption
Interesting solution proposed by Heiko and Hannes after MSWG helps reducing impedance, but not feasible for BI.
Putting ferrites reduces efficiently the heat load, but:
  Is it possible to put ferrites there?
  If needed, is it possible to cool the ferrites?
Work still on-going to:
  Find acceptable solutions
  Compare with previous measurements of Federico
  See the impact of the position of the wire in the tank