## Slide 1: Threshold for microwave instability of the LHC beam
T. Argyropoulos, E. Shaposhnikova
LIU-SPS BD WG
11/07/2013

## Slide 2
Introduction
Beam measurements with RF off and long injected bunches (τ4σ ~ 25 ns) showed a strong resonance at 1.4 GHz: high Rsh and low Q
Macro-particle simulations performed to identify the parameter space of this effective impedance:
Next step is to identify the source of this impedance in the SPS ring:
Most probable candidate the isolated vacuum flanges
(talk of J. E. Varela Campelo‎)
What is the effect that this impedance has on the beam?  important to understand for future actions
  Results of simulations for the SPS flat top are presented
fr (GHz) | Q | Rsh (kΩ)
1.35 – 1.45 | 5 – 10 | 300 – 400

## Slide 3
Outline
Measurements used as reference for our simulation studies
  Q20: bunch rotation at the SPS extraction
  Q26: LHC single bunch MD
Simulation results
Summary

## Slide 4
Measurements (1)
  Bunch rotation: Q20 optics , V200 = 2 MV, V800 = 0.2 MV, p = 450 GeV/c , Np: (1.1 - 2.7)x1011 - (Action from the previous meeting to check the bunch length dependence after filamentation (~60 ms FB))

## Slide 5
Measurements (2)
  LHC single bunch MD: Q26 optics , V200 = 4.5 MV, V800 = 0.5 MV, p = 450 GeV/c , Np: (0.6 - 2.4)x1011
Bunch length vs Intensity at FT
Threshold estimation at the time:
Nth~2.2x1011
Selected to reduce
the dependence of the
bunch lengths at FT on
intensity
constant εl at injection
εl~0.35 eVs

## Slide 6
Simulation set-up
Distribution function: ,
corresponds to and
SPS known impedance model:
+ SPS kickers (C. Zannini)
Initial matched distribution created iteratively with conditions to match those in measurements
5x105 macro-particles tracked for 5x104 turns ( ~ 1.15 s)
 | fr (MHz) | Rsh (MΩ) | Q
TWC200 – F (long) | 200.2 | 2.86 | 150
TWC200 – F (short) | 200.2 | 1.84 | 120
TWC200 – H | 629 | 0.388 | 500
TWC800 - F | 800.8 | 1.94 | 300

## Slide 7
Simulation vs Measurements (1)
  Bunch rotation: Q20 optics , V200 = 2 MV, V800 = 0.2 MV, p = 450 GeV/c , Np: (1.1 - 2.7)x1011
εl = 0.4 eVs (> measurements?)
comparable bunch lengths
similar slopes (see talks from
previous meeting)
threshold from simulations
Nth~1.3x1011
does not correspond to reality
(no ramp and phase loop in
simulations)
errobars indicate the stability of the bunches - (quadrupole oscillations)

## Slide 8
Simulation vs Measurements (2)
Measurements
Simulations
  LHC single bunch MD: Q26 optics , V200 = 4.5 MV, V800 = 0.5 MV, p = 450 GeV/c , Np: (0.6 - 2.4)x1011
εl = 0.35 eVs
comparable bunch lengths
threshold from simulations Nth~1.4x1011

## Slide 9
Simulation Q26 vs Q20
Nth~1.3x1011
Nth~1.5x1011 (estimated)
Nth~1.9x1011
For Q26 is clearly better with 7 MV  threshold for microwave
Instability starts later during the tracking > 20.000 turns (for 4.5 MV <5000 turns)
For Q20 again fast instability (<5000 turns)
Comparing thresholds between Q26 (4.5 MV) and Q20 (5.5 MV) it seems that it scales according to the Keil-Schnell-Boussard criterion
εl = 0.35 eVs

## Slide 10
Summary
Results generally agree with the bunch rotation and LHC MD
measurements
Threshold seems to improve with higher RF voltage  indication of microwave instability (MI)  1.4 GHz
Comparison of Q20 and Q26 scales according to the Keil-Schnell-Boussard criterion
In reality we have a mixture of MI and LLD
More accurate simulations are needed for better agreement:
  Particle distribution to be close to the measured one
  Simulation of the ramp where the actual blow-up was observed
  Implementation of phase loop

## Slide 11
Simulation results - with 1.4 GHz
With the 1.4 GHz resonance:
  fr=1.42 GHz, Q=10, Rsh = 400 kΩ
Micro-structure pattern inside the bunch
Bunch is blowing-up after a few hundreds of turns (depends on the intensity)
Phase-space at different times for Np = 1.9x1011
Bucket corresponds to Turn=1
High azimuthal mode(s) (m=3,4 ?) of bunch oscillations for this resonance

## Slide 12
Simulation results - w/o 1.4 GHz
Bunch is more stable
Blows-up slowly and at higher intensities
Phase-space at different times for Np = 2.3x1011
Bucket corresponds to Turn=1
Initial distribution

## Slide 13
Simulation results
Bunch length evolution with 1.4 GHz
zoom
Bunch length evolution w/o 1.4 GHz
with 1.4 GHz resonance: bunch blows-up at the beginning even at low intensities (~1.4x1011 p)
w/o 1.4 GHz: higher intensity threshold

## Slide 14
Simulation results
Fit with the formula: (neglecting synch. phase shift) (Laclare) for parabolic amplitude density and constant inductive
, with (from simulation)
Injection: - at 50k Turns: