## Slide 1: Present status of the SPS longitudinal impedance model
C. Zannini and G. Rumolo
Thanks to: T. Argyropoulos, M. Barnes, E. Chapochnikova, E. Métral, N. Mounet, B. Salvant

## Slide 2: Overview
Status of the longitudinal SPS impedance model
  Wall Impedance model
  Kicker Impedance model
Summary

## Slide 3: Status of the SPS longitudinal impedance model
Elements included in the database:
  Realistic model that takes into account the different SPS vacuum chambers weighted by the respective length
  19 kickers (CST 3D simulation)
Kickers
Wall impedance
Notes: Specificare che la cavita’ e’ quella a 200 MHz

## Slide 4: Overview
Status of the longitudinal SPS impedance model
  Wall Impedance model
  Kicker Impedance model
Summary

## Slide 5: Wall impedance model
1. Different vacuum chambers weighted by the respective length and beta function
2. The iron in the magnets is also taken into account

## Slide 6: Wall Impedance model
The wall impedance is defined as the sum of the resistive wall impedance and the indirect space charge.
Calculation based on analytical calculations
  Tlwall (based on Transmission Line theory)
    Longitudinal: resistive wall impedance
    Transverse: resistive wall impedance + indirect space charge
  ImpedanceWake2D (based on the field matching theory)
    Longitudinal: wall impedance
    Transverse: wall impedance
F. Roncarolo, F. Caspers, T. Kroyer, E. Métral, N. Mounet, B. Salvant, and B. Zotter. Comparison between laboratory measurements, simulations and analytical predictions of the transverse wall impedance at low frequencies. Phys. Rev. ST Accel. Beams, 12(084401), 2009.

## Slide 7
TL model
Copper 0.05 mm
S.steel 1 mm
Boundary: PEC
Re-Wall
Copper 0.05 mm
S.steel 1 mm Boundary : Quasi PEC
The agreement with ReWall is very good
Comparison with ReWall: PEC boundary
g=10000
L= 1 m

## Slide 8
Re-Wall
S.steel 1 mm Boundary : Vacuum
TL model
S.steel 1 mm Boundary : Vacuum
Comparison with ReWall: Vacuum boundary
There is a perfect agreement with the ReWall code
g=10000
L= 1 m

## Slide 9
Re-Wall
S.steel 1.5 mm Boundary : silicon-steel
TL model
S.steel 1.5 mm Boundary : silicon-steel
Comparison with ReWall: Conductive boundary
There is a perfect agreement with the Re-Wall code
g=10000
L= 1 m

## Slide 10: Longitudinal wall impedance
Calculation performed with ImpedanceWake2D

## Slide 11: Longitudinal wall impedance
Does not account for the iron in the magnet
Does not include the indirect space charge term
Old calculation
New calculation
Accounts for the iron in the magnet
Includes the indirect space charge term

## Slide 12: Overview
Status of the longitudinal SPS impedance model
  Wall Impedance model
  Kicker Impedance model
Summary

## Slide 13: Kicker impedance model

## Slide 14: SPS extraction kicker (MKE)

## Slide 15: MKE kicker with serigraphy

## Slide 16: Comparing MKE with and without serigraphy
f=44 MHz

## Slide 17: Experimental confirmations
The impedance model of the SPS extraction kicker can explain the beam induced heating observed in the SPS machine
Bench impedance measurements are in reasonable agreement with the impedance model
C. Zannini, G. Rumolo. “MKE heating with and without seigraphy”, Presented at the SPSU meeting, 2 August 2012, http://paf-spsu.web.cern.ch/paf-spsu/

## Slide 18: Beam induced heating
Bunchlength during the experiment
Beam induced heating
Power loss from the impedance model

## Slide 19: Comparing longitudinal impedance measurements and model for the MKP-L module

## Slide 20: Longitudinal kicker impedance model
As for the MKEs for a better estimation of the low frequency behavior (below few tens of MHz) dedicated simulations are needed also for the other kickers.

## Slide 21
Longitudinal kicker impedance model: MKEs
Tsutsui model overestimates the MKEs impedance contribution because of the serigraphy

## Slide 22
Longitudinal kicker impedance model: MKEs
Tsutsui model overestimates the MKEs impedance contribution because of the serigraphy

## Slide 23
Longitudinal kicker impedance model: MKEs
MKEs contribution very low due to the effect of the serigraphy: considering only the kicker impedance we should have a situation similar to 2001

## Slide 24
Longitudinal kicker impedance model: MKEs
MKEs contribution very low due to the effect of the serigraphy: considering only the kicker impedance we should have a situation similar to 2001

## Slide 25: Overview
Status of the transverse SPS impedance model
Status of the longitudinal SPS impedance model
  Wall Impedance model
  Kicker Impedance model
Summary

## Slide 26: Summary
Longitudinal impedance model
  The Wall impedance of SPS has been estimated
    The tools used for the calculations have been successfully benchmarked
  The kicker impedance model has been discussed
    Benchmarks with beam observations and wire measurements have been presented
    Differences with respect to the Tsutsui model have been showed

## Slide 27: Thank you for your attention