## Slide 1: SPS Impedance Model: Latest Results from Simulations
Theodoros Argyropoulos, Elena Shaposhnikova, Helga Timko, Jose Varela
BE-RF-BR

## Slide 2: Status at the previous meeting
    No BPM&Zs impedance
    Damping resistors, w/ R/Q increased; ~15 % higher Rsh at 1.4 GHz
    Simulated w/ different measured distributions
    Fits on average
N.B. non-linear scaling between amplitude and impedance

## Slide 3: Uncertainties in our simulations
Sources of uncertainty in simulations
  Longitudinal phase-space distribution
    Can affect the outcome largely!
  Impedance model
    Flanges
    Kickers
    In-between Zs
    200 MHz and 800 MHz cavities
  Let’s try to reduce first some of these uncertainties.

## Slide 4: Impedance model: Flanges
For simplicity: model with single BB resonator
  fr = 1.41 GHz, Q = 210, Rsh = 1.871 MΩ

## Slide 5: Impedance model: Kickers
Wake obtained as an FFT of Carlo’s data  updated!
  Using an analytic continuation of ReZ ~ 1/f2 and ImZ ~ 1/f

## Slide 6: Impedance model: Kickers
Wake obtained as a resonator fit
  An 8-resonator model (red) gives a very similar wake

## Slide 7: Impedance model: Cavities
A more accurate model of the SPS TW cavities
  Following G. Dôme (CERN-SPS/ARF/77-11, 1977)
  , where .
Cavity | R (MΩ) | a (μs)
200 MHz Short | 20.876 | 3.56
200 MHz Long | 21.38 | 4.47
800 MHz | 20.969 | 2.07
Less impedance than before

## Slide 8: SPS impedance in total
fr (GHz) | Rsh (MOhm) | Q | R/Q (kOhm)
0.629 | 0.388 | 500 | 0.78
0.885 | 0.0146 | 482 | 0.030
0.892 | 0.0198 | 493 | 0.040
1.052 | 0.1597 | 773 | 0.207
1.062 | 0.1903 | 773 | 0.246
1.069 | 0.0454 | 654 | 0.069
1.092 | 0.0570 | 667 | 0.085
1.185 | 0.0116 | 610 | 0.019
1.215 | 0.0012 | 624 | 0.002
1.598 | 0.0426 | 672 | 0.063
1.613 | 0.5975 | 686 | 0.871
1.859 | 0.2951 | 896 | 0.329
1.960 | 0.0721 | 1993 | 0.036
0.550 | 0.2275 | 1000 | 0.228
1.050 | 0.2275 | 1250 | 0.182
1.41 | 1.871 | 210 | 8.91
BPMs
Zs (?)
200 MHz HOM
Flanges
+ cavity & kicker impedance

## Slide 9: Distributions: from tomoscope
At PS flat top C1160 – measured within ~5 ms
At injection to the SPS (after tracking in ESME)
D1
D2
D3
D4
D5
D6
D1
D2
D2
D4
D5
D6
D3

## Slide 10: Distributions from average profile
Reconstructed average
Reconstructed + Gaussian
25.9 ns
26.5 ns

## Slide 11: Reconstructed distribution
Amplitude evolution
Projection
Doesn’t fit the measurements: 1.4 GHz grows too fast, 200 MHz too slowly

## Slide 12: Reconstructed + Gaussian
Amplitude evolution
Projection
Better: 1.4 GHz is more reasonable, but 200 MHz is still too slow

## Slide 13: Measured distributions, 11011
Amplitude evolution
Projection
Better, but growth rates are still not perfect, hence the sidebands cannot be seen

## Slide 14: Measured distributions, 81010
Amplitude evolution
Projection
In measurements, 81010 was the threshold of 1.4 GHz instability.
This is correctly reproduced here, but the 1.4 GHz growth rate is sill not correct

## Slide 15: Sidebands at 1.2 GHz and 1.6 GHz
Sidebands observed experimentally
  Are due to the interaction between 200 MHz and 1.4 GHz
  When the 2 modulations
  overlap, the sidebands
  always follow the 1.4 GHz
  When there is no overlap,
  no sidebands are seen

## Slide 16: Why are sidebands important?
Source of 1.4 GHz peak: flanges
  Now we are confident: flange impedance is sufficient to explain the 1.4 GHz peak in the de-bunching spectrum
Is this impedance harmful?
  Does it lead to microwave instability?
    Need simulations with RF on to answer this question
     Need an accurate SPS impedance model
     Need to know whether missing sidebands are due to a wrong distribution or an incomplete impedance model (or both)

## Slide 17: Conclusions, Plans
1.4 GHz peak identified
  Flange impedance is enough to explain the peak
Importance of the 1.4 GHz impedance
  Not yet fully understood
    Too many uncertainties in our model
  Will have to find an impedance model that explains all our measurements; only then we can know whether or not the 1.4 GHz impedance is harmful