## Slide 1: Effect of the 1.4 GHz impedance on a single bunch at the SPS flat top
T. Argyropoulos
LIU-SPS BD WG
25/04/2013

## Slide 2
Introduction
Beam measurements with RF off and long injected bunches (τ4σ ~ 25 ns) showed a strong resonance at 1.4 GHz: high Rsh and low Q
Macro-particle simulations performed to identify the parameter space of this impedance:
Next step is to identify the source of this impedance in the SPS ring:
Most probable candidate the isolated vacuum flanges
(talk of J. E. Varela Campelo‎)
What is the effect that this impedance has on the beam?  important to understand for future actions
  Preliminary results of simulations for the SPS flat top are presented
fr (GHz) | Q | Rsh (kΩ)
1.35 – 1.45 | 5 – 10 | 300 – 400

## Slide 3
Simulation set-up
Distribution function: ,
corresponds to
SPS known impedance model:
+ SPS kickers (C. Zannini)
Initial matched distribution created iteratively with conditions to match those in measurements (for the bunch rotation):
  Only with Q20 optics , V200 = 2 MV, V800 = 0.2 MV, p = 450 GeV/c , Np: (1.1 - 2.7)x1011
5x105 macro-particles tracked for 5x104 turns ( ~ 1.15 s)
 | fr (MHz) | Rsh (MΩ) | Q
TWC200 – F (long) | 200.2 | 2.86 | 150
TWC200 – F (short) | 200.2 | 1.84 | 120
TWC200 – H | 629 | 0.388 | 500
TWC800 - F | 800.8 | 1.94 | 300

## Slide 4
Simulation results - with 1.4 GHz
With the 1.4 GHz resonance:
  fr=1.42 GHz, Q=10, Rsh = 400 kΩ
Micro-structure pattern inside the bunch
Bunch is blowing-up after a few hundreds of turns (depends on the intensity)
Phase-space at different times for Np = 1.9x1011
Bucket corresponds to Turn=1
High azimuthal mode(s) (m=3,4 ?) of bunch oscillations for this resonance

## Slide 5
Simulation results - w/o 1.4 GHz
Bunch is more stable
Blows-up slowly and at higher intensities
Phase-space at different times for Np = 2.3x1011
Bucket corresponds to Turn=1
Initial distribution

## Slide 6
Simulation results
Bunch length evolution with 1.4 GHz
zoom
Bunch length evolution w/o 1.4 GHz
with 1.4 GHz resonance: bunch blows-up at the beginning even at low intensities (~1.4x1011 p)
w/o 1.4 GHz: higher intensity threshold

## Slide 7
Simulation results
Fit with the formula: (neglecting synch. phase shift) (Laclare) for parabolic amplitude density and constant inductive
, with (from simulation)
Injection: - at 50k Turns:

## Slide 8
Summary
Preliminary simulations at the SPS flat top show that the 1.4 GHz resonance has a strong effect.
  Bunch blows-up for Np > 1.4x1011
  Higher threshold without the 1.4 GHz impedance
Results generally agree with the bunch rotation measurements
More accurate simulations are needed for better agreement:
  Particle distribution to be close to the measured one
  Simulation of the ramp where the actual blow-up was observed
  Implementation of phase loop