## Slide 1: Single- and multi- bunch instabilities on the SPS flat top
T. Argyropoulos,
Acknowledgements: A. Lasheen, E. Shaposhnikova
LIU-SPS BD WG 04/09/2014

## Slide 2: Outline
Simulation procedure
Impedance model
Single bunch simulations
Mutli-bunch simulations
Summary

## Slide 3: Simulation procedure
Simulations where performed at SPS flat top (450 GeV/c)
using either my Matlab code (multi-bunch) or the new PyHEADAIL
(longitudinal version) (single bunch)
The bunch(es) where initially matched to the bucket with intensity
effects taken into account
The distribution function:
Single bunch: 500k macro-particles were tracked for 50k (~ 1.15 s)
Multi-bunch (6 bunches only): 300k macro-particles per bunch were tracked for 30k (~ 0.69 s)
Stability criteria was based on the bunch length growth and on the bunch length or bunch position oscillations at the end

## Slide 4: Longitudinal impedance model
  The longitudinal impedance model used here includes (Jose E. Varela at LIU-SPS 31/07/14):
  Traveling Wave Cavities (200 MHz + HOM, 800 MHz)
  Flanges
  BPMs
  Kickers (C. Zannini)
  Resistive wall (C. Zannini)
  Unshielded Pumping Ports
  Y – Chamber
  Beam Scrapers

## Slide 5: Single bunch
Goals:
  Understand the nature of single bunch instability provoked by the current SPS impedance model: loss of Landau damping or microwave  find the instability thresholds in intensity Nth for:
    different longitudinal emittances
    different optics: Q20, Q26, Q22
    different main RF voltages V200: 7 MV, 4.5 MV, 2 MV
    single or double RF system (in BSM with V800/V200=1/10)
  Compare with measurements when possible
Instability threshold: or
ε = 0.3 eVs – Nth =3.5E11
ε = 0.5 eVs – Nth =3.4E11
Q20 - Double RF - V200 = 7 MV

## Slide 6: Single bunch
Instability thresholds (E. Shaposhnikova LIU-SPS 08/08/2013):
  Loss of Landau damping (simplified scaling):
  Microwave instability (simplified scaling)
    - broad-band impedance:
    - narrow-band impedance:
Most of the important resonances in the impedance model are in the narrow-band regime Q > 10

## Slide 7: Single bunch – voltage scan
For the same optics and same emittance, Nth increases with the RF voltage for microwave and decreases for the LLD 
Nth behaves like in microwave instability but most probably is a mixture of both!
Complicated impedance  non monotonic synchrotron frequency distribution  regions where might reduce the thresholds (next slides)
For single RF and large emittances LLD becomes critical – probably due to both spread and shape
more sim to find Nth
fs distr. (?)

## Slide 8: Single bunch – voltage scan
For the same optics and same bunch length, Nth increases with the RF voltage for all

## Slide 9: Single bunch – different optics
For the same voltage and same emittance, Nth increases with the slippage factor: more for LLD () and less for microwave ( or )
Nth behaves more like in microwave instability (narrow-band)
Again for single RF and large emittances LLD becomes critical  spread and shape
Similar for all optics

## Slide 10: Single bunch – different optics
For the same voltage and same bunch length, Nth same for all optics
Simple scaling used so far for Q20 and Q26 proves to be valid even in double RF and with this complicated impedance!!
For a double RF system threshold increases with larger emittance

## Slide 11: Single bunch – fs distribution
Fs distribution for a double RF with V200 = 7 MV at the instability threshold
  ε = 0.4 eVs: N = 2.4E11
  ε = 0.3 eVs: N = 3.4E11
Vertical lines show the corresponding emittances
Complicated shape: in both but much more spread in the case of ε=0.3 eVs

## Slide 12: Single bunch – comparison with meas.
Measurements at flat top with V200 = 2 MV before bunch rotation
Quite good agreement for the case of the ε = 0.5 eVs
Difference from distr. function
Simplifications in simulation (no phase loop, no ramp, etc)
Measurement error on bunch profile

## Slide 13: Multi-bunch
Preliminary results
Only 6 bunches simulated
Both with 25 ns and 50 ns bunch spacing
Q20 and Q26 optics were considered
Single and double RF systems with V200 = 7 MV
Only for small emittance for the moment (ε = 0.4 eVs)
Same impedance model but not the TWC200 MHz fundamental mode 
assumed perfect FF/FB

## Slide 14: Multi-bunch – Q20 - 25 vs 50 ns
Lower threshold for 25 ns compared to 50 ns bunch spacing
The 3rd bunch seams to suffer more!
50 ns bunch spacing
25 ns bunch spacing

## Slide 15: Multi-bunch – Q20 – single vs double RF
Threshold seams higher for double RF!
Single RF
Double RF

## Slide 16: Multi-bunch – Q20 vs Q26 – double RF
Higher threshold with the Q20
Q20
Q26

## Slide 17: Summary
Single bunch instability threshold
  Microwave instability observed in simulations
  Simple scaling used so far for Q20 and Q26 proves to be valid
  even in double RF and with this complicated impedance!!
  For a double RF system threshold increases with larger emittance
  Relatively good agreement with measurements
Multi-bunch instability threshold
  Behavior for different cases qualitatively agrees with measurements (no phase loop, beam loading in 200 MHz RF system):
    25 ns vs 50 ns
    Single vs double RF system
    Q20 vs Q26
  More simulations are needed
  The contribution from the vacuum flanges to the instability threshold needs to be determined (simulations are running)