## Slide 1: 2014 scrubbing run: hot news from the CCC
H. Bartosik, G. Iadarola, G. Rumolo,
Many thanks to T. Argyropoulos, T. Bohl, E. Carlier, H. Damerau, J. Esteban Muller, B. Goddard, S. Hancock, W. Höfle, V. Kain, G. Kotzian, K. Kornelis, K. Li, G. Papotti, M. Schenk, E. Shaposhnikova, M. Taborelli, D. Valuch,
and SPS OP crew

## Slide 2: Scrubbing run
Monday
  Prepared machine for scrubbing
  MKP4 vacuum interlocks optimized for scrubbing
    During LS1 the MKP4 module was exchanged with a new one (E. Carlier) + intervention due to problem on water manifold in August
    High static pressure level (~1e-7 mbar) since beginning of the run, not significantly improving
    Dynamic pressure rise with LHC beams  was expected to be limitation during scrubbing run
    Therefore, ABT suggested to raise SW interlock from 2e-7 mbar to 4e-7 mbar but decrease HW interlock from 1e-6 to 6e-7 mbar
  Scrubbing cycles setup
  COLDEX moved into IN position
    No impact on beam lifetime
  Started maximizing integrated beam intensity on scrubbing cycle
    limited by TIDVG vacuum interlock (which is mainly there to protect the MKP) — agreed with EN-STI and TE-ABT to raise interlock from 4e-7 to 6e-7 mbar
Monday
Tuesday
Wednesday
Thursday
Friday
Saturday
Sunday
Week 45

## Slide 3: Monday (Nov. 3)

## Slide 4: Scrubbing run
Tuesday
  transverse emittance around 3um for 1.2e11 p/b (3 batches)
  setup of 200 MHz LL RF on acceleration cycle (1 batch) for 6h
  reached 4 batches on FB with dump at 13s
  ZS spark rate interlock reached a couple of times
  now limited by MKP4 vacuum level
    related also to the beam induced heating (presently MKP4 at ~44 deg)
  reduced number of batches during the night due to vacuum interlocks on MKP4
  Measurements with lower chromaticity
    Acquisitions with high bandwidth pickups
    No clear evidence of e-cloud instability; due to Q20 …
  MKP4 SW interlock reached several times
Monday
Tuesday
Wednesday
Thursday
Friday
Saturday
Sunday
Week 45

## Slide 5: Tuesday (Nov. 4)

## Slide 6: Tuesday (Nov. 4)

## Slide 7: Tuesday (Nov. 4) – Ecloud monitor
MBA - StSt

## Slide 8: Tuesday (Nov. 4) – Ecloud monitor
MBB - StST
MBB - StSt

## Slide 9: Scrubbing run
Wednesday
  MD on 800 MHz (from 10:00 to 00:45)
  Meeting with TE-ABT about the MKP4 threshold
    Raise MKP4 SW interlock to 5e-7 mbar
    Raise TIDVG interlock to 1.2e-6 mbar (agreed with EN-STI)
  started setting up the doublet beam on MD1
    started transverse damper setup on doublet
  mains tripped during the night (4h no beam)
Monday
Tuesday
Wednesday
Thursday
Friday
Saturday
Sunday
Week 45

## Slide 10: Wednesday (Nov. 5)

## Slide 11: Scrubbing run
Thursday
  Scrubbing with up to 5 batches nominal LHC beam
    Problems with heating TT2 magnets due to high duty cycle
  In parallel: SPS-LHC synchronization tests
  Tonight:
    Acceleration of as many batches as possible
Monday
Tuesday
Wednesday
Thursday
Friday
Saturday
Sunday
Week 45

## Slide 12: Present status: pressure gauge in Arc 5

## Slide 13: Present status

## Slide 14: Present status: Emittances 4 batches

## Slide 15
Thank you for your attention!