## Slide 1: Longitudinal Microwave Instability in a Multi- RF System
T. Argyropoulos
LIU-SPS BD WG 06/11/2014
Acknowledgements: H, Bartosik, T. Bohl, F. Caspers, H. Damerau, A. Lasheen, J. E. Muller , D. Quartullo, B. Salvant, E. Shaposhnikova
H. Timkó, J. E. Varela, C. Zannini

## Slide 2: Outline
Introduction
Uncontrolled longitudinal emittance blow-up in the SPS
  Beam observations
  Impedance identification
Longitudinal instability of a high frequency resonator
  Single RF system
  Double RF system
Present situation in the CERN SPS
Summary

## Slide 3: Introduction
Microwave instability observed in the proton machines as a fast increase of the bunch length (longitudinal emittance)
Microwave (μw) instability observed in the CERN SPS in the past  main source the resonant (Q~50) impedance of the pumping ports (~1000)  shielding them improved the beam stability
Today, SPS mainly used as the injector of the LHC
Recently μw instability was seen for a single proton bunch at high energies in the SPS  one of the limitations for an intensity increase required by the HL-LHC project

## Slide 4: Uncontrolled emittance blow-up (1/3)
Measurements of high intensity single bunch at the SPS flat top
Double RF systems (200 MHz + 800 MHz) in bunch shortening mode (BSM) with V800 = V200/10
Measurements in 2012
Emittance blow-up can not be explained by potential well distortion with the SPS impedance model (ImZ/n ~ 3.5 Ω but ImZ/n >15 Ω is needed)  μw instability due to high frequency resonant impedance  blow-up during ramp

## Slide 5: Uncontrolled emittance blow-up (2/3)
Single bunch with high intensity in double RF system (V800 = V200/10)
200 MHz RF voltage calculated for constant bucket area 0.5 eVs  larger filling factor during cycle  more Landau damping
Measurements in 2014 in Double RF BSM
Instability during ramp
For 0.26 eVs
2.5x1011 p

## Slide 6: Uncontrolled emittance blow-up (3/3)
Lower threshold in a single RF system with same 200 MHz voltage program (bucket area = 0.5 eVs)
Instability during ramp
Measurements in 2014 in Single RF
For 0.26 eVs
1.7x1011 p

## Slide 7: Impedance identification (1/2)
Beam measurements at injection energy (26 GeV/c) with long bunches ( ns) and RF off
Small momentum spread  more unstable and slow debunching
Line density modulated at 200 MHz and a higher frequency (1.4 GHz)
Transform
Fourier
200 MHz TWC
Example at Np = 1.0x1011 p

## Slide 8: Impedance identification (2/2)
  Impedance measurements and electromagnetic simulations for different devices/structures in the SPS ring:
  Vacuum flanges are the best candidate with strong peak at fr = 1.4 GHz with R/Q = 9 kΩ (different types,~ 500)
Group I
Group II

## Slide 9: μw instability with a resonator
Microwave instability threshold in a single RF system:
  broad-band impedance: 
  
Particle simulations carried out to verify this analytical result using the code BLonD (longitudinal beam dynamics code developed at CERN)
Criterion for Instability threshold: or ps
ε = 0.3 eVs – Nth =3.5E11
ε = 0.5 eVs – Nth =3.4E11
Q20 - Double RF - V200 = 7 MV

## Slide 10: Simulations – single RF (1/2)
Simulations at SPS flat top (450 GeV/c) with V200 = 2 MV
Scanning but keeping constant
Instability threshold from simulations in a single RF
Same threshold for  narrow-band regime  is important
For  broad-band regime  is important

## Slide 11: Simulations – single RF (2/2)
Instability threshold from simulations in a single RF
:
   narrow-band regime
   approaching the
  broad-band regime
Simulations at SPS flat top (450 GeV/c) with V200 = 2 MV
Scanning but keeping constant

## Slide 12: Simulations – double RF (1/2)
Second harmonic RF system: h2/h1 = 2 and V1/V2=2
Simulations at SPS flat top (450 GeV/c) with V200 = 2 MV
Similar dependence with
= 10
= 250
Double RF in BSM has the highest threshold and double RF in BLM the lowest  Dependence on the

## Slide 13: Simulations – double RF (2/2)
Fourth harmonic RF system: h2/h1 = 4 (SPS today)
Simulations at SPS flat top (450 GeV/c) with V200 = 2 MV
After a certain single RF is better for stability
Can be correlated with the synchrotron frequency distribution inside the bunch (?)
= 250

## Slide 14: SPS longitudinal impedance model
Includes: RF cavities, resistive wall, injection and extraction kickers, Beam Position Monitors (BPMs), vacuum flanges etc.
Jose E. Varela et al.
The SPS longitudinal impedance model
200 MHz TWC
Vacuum flanges

## Slide 15: Simulations vs measurements
Macroparticle simulations at the SPS flat top (450 GeV/c) using the full SPS impedance model
Distribution function:  form measurements
Double RF V200 = 2 MV – V800 = 0.2 MV – N=1.47x1011 p
Discrepancy due to transfer functions

## Slide 16: Simulations vs measurements single bunch
Good agreement between measurements and simulations
From measurements in 2014: 2.5x1011 p
(more points are needed)
From particle simulations with 0.35 eVs (maximum single particle trajectory): 2.5x1011 p
Measurement in 2012 correspond to higher initial 0.45 eVs (from simulations) but points at lower intensity are missing
In simulation: 2.0x1011 p
Double RF V200 = 2 MV – V800 = 0.2 MV – N=1.47x1011 p

## Slide 17: Simulations vs measurements single bunch
Increasing the RF voltage in both RF systems  larger  larger increase the instability threshold  μw type of instability
Probably due to the synchrotron frequency distribution inside the bunch
Complicated shape: in both but much more spread in the case of 0.3 eVs
Double RF - )

## Slide 18: Simulations vs measurements multi-bunch
Simulations for 6 bunches (25 ns spacing) at SPS flat top
Intensity threshold as a function of bunch length for 1 & 6 bunches
Qualitative agreement of simulations with measurements:
Nth of 6 bunches is ~ twice lower than of single bunch (limitation for the HL-LHC parameters ~ 2.5x1011 p/b)
Only a few bunches are coupled, no coupled bunch modes  indeed in measurements 25 ns and 50 ns spaced bunches are coupled, but batches spaced by 225 ns are decoupled
Nth increases with emittance
Double RF V200 = 7 MV – V800 = 0.7 MV
Preliminary results show that Nth increases by a factor of 2 without the impedance of vacuum flanges (single and multi bunch)  impedance reduction under discussion

## Slide 19: Summary
Signs of μw instability are observed in the SPS  uncontrolled emittance blow-up
Beam measurements identified the vacuum flanges as the main impedance source (strong resonant peak at 1.4 GHz and many more resonances with high Q values)
μw instability threshold for this type of resonators scale with R/Q (as expected from theory in single RF)
Double RF vs single RF
  h2/h1 = 2: higher Nth in BSM and lower in BLM (as expected from Δp/p)
  h2/h1 = 4: lower Nth in BSM above a certain emittance
Simulations with the current SPS longitudinal impedance model verify the uncontrolled blow-up  good agreement with the measurements
Nth increases by a factor of 2 without the impedance of vacuum flanges (single and multi bunch)  impedance reduction under discussion at CERN