## Slide 1: Benchmarking the SPS transverse impedance model: headtail growth rates
C. Zannini, H. Bartosik, G. Iadarola, G. Rumolo, B. Salvant
Acknowledgment: M. Barnes, T. Bohl, F. Caspers, E. Chapochnikova, H. A. Day, E. Métral, V.G. Vaccaro, J.E. Varela

## Slide 2: Overview
SPS transverse impedance model
Benchmarking of the model
  Previous benchmarks
  Headtail growth rates
    Q20 optics
    Q26 optics
Conclusions and future plans

## Slide 3: Overview
SPS transverse impedance model
Benchmarking of the model
  Previous benchmarks
  Headtail growth rates
    Q20 optics
    Q26 optics
Conclusions and future plans

## Slide 4: SPS transverse impedance model
Elements included in the database:
  Wall impedance that takes into account the different SPS vacuum chambers (analytical calculations)
  Kickers (CST 3D simulations)
  RF cavities (200 MHZ and 800 MHz) without couplers (CST 3D simulations)
  Broadband impedance of step transitions (CST 3D simulations)
  Horizontal (BPH) and vertical (BPV) beam position monitors (CST 3D simulations)
Kickers
Beam pipe
BPH
BPV
RF cavities
Step transitions

## Slide 5: SPS transverse impedance model
Elements included in the database:
  Wall impedance that takes into account the different SPS vacuum chambers (analytical calculations)
  Kickers (CST 3D simulations)
  RF cavities (200 MHZ and 800 MHz) without couplers (CST 3D simulations)
  Broadband impedance of step transitions (CST 3D simulations)
  Horizontal (BPH) and vertical (BPV) beam position monitors (CST 3D simulations)
Kickers
Beam pipe
BPH
BPV
RF cavities
Step transitions

## Slide 6
SPS transverse impedance model

## Slide 7: Overview
SPS transverse impedance model
Benchmarking of the model
  Previous benchmarks
  Headtail growth rates
    Q20 optics
    Q26 optics
Conclusions and future plans

## Slide 8
100 %
20 %
40 %
60 %
80 %
The SPS impedance model explains more than 90% of the measured vertical coherent tune shift
Vertical coherent tune shift: Measurements performed in September 2012
Benchmarking the SPS transverse impedance model: coherent tune shift

## Slide 9
The SPS impedance model predicts a very small horizontal tune shift (almost flat) in agreement with the measurements
Horizontal coherent tune shift: Measurements performed in February 2013
Benchmarking the SPS transverse impedance model: coherent tune shift

## Slide 10: Benchmark of the SPS transverse impedance model: TMCI thresholds
Two regimes of instability in measurements
  Fast instability threshold with linear dependence on εl
  Slow instability for intermediate intensity and low εl
Very well reproduced with HEADTAIL simulations
  SPS impedance model includes kickers, wall, BPMs and RF cavities
  Direct space charge not included
10
measurements
HEADTAIL simulations
4.5x1011 p/b
@ 0.35 eVs
nominal
Island of slow instability

## Slide 11
11
measurements
HEADTAIL simulations
4.5x1011 p/b
@ 0.35 eVs
nominal
Island of slow instability
Benchmark of the SPS transverse impedance model: TMCI thresholds

## Slide 12
12
measurements
HEADTAIL simulations
4.5x1011 p/b
@ 0.35 eVs
nominal
Island of slow instability
Benchmark of the SPS transverse impedance model: TMCI thresholds

## Slide 13: Overview
SPS transverse impedance model
Benchmarking of the model
  Previous benchmarks
  Headtail growth rates
    Q20 optics
    Q26 optics
Conclusions and future plans

## Slide 14: Growth rate versus chromaticity: Measurements
Measurements performed on February 2013
ξ = ξ(ACNR)

## Slide 15: Growth rate measurements
H. Burkhardt, G. Rumolo, F. Zimmermann, “Coherent Beam Oscillations and Transverse Impedance in the SPS”, 2002.
Amplitude of peak in FFT

## Slide 16: Growth rates versus chromaticity: comparing measurements and impedance model
Analytical
HEADTAIL
simulation
SPS impedance model
Non linear chromaticity
Double RF system
Same as used for TMCI studies

## Slide 17: Growth rates versus chromaticity: comparing measurements and impedance model
Strong indication that the SPS transverse impedance model is close to reality up to 500 MHz

## Slide 18: Growth rates versus chromaticity: comparing measurements and impedance model
The SPS impedance model explains about 90% of the measured headtail growth rates

## Slide 19: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.04

## Slide 20: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.14

## Slide 21: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.34

## Slide 22: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.54

## Slide 23: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.74

## Slide 24: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.84

## Slide 25: Comparing measurements and impedance model: intra-bunch motion
ξ = -0.94

## Slide 26: Overview
SPS transverse impedance model
Benchmarking of the model
  Previous benchmarks
  Headtail growth rates
    Q20 optics
    Q26 optics
Conclusions and future plans

## Slide 27: Growth rate versus chromaticity: Measurements
Measurements performed on February 2013
ξ = ξ(ACNR)

## Slide 28: Growth rates versus chromaticity: comparing measurements and impedance model
Strong indication that the SPS transverse impedance model is close to reality up to 1.8 GHz

## Slide 29: Growth rates versus chromaticity: comparing measurements and impedance model
The SPS impedance model explains about 90% of the measured headtail growth rates

## Slide 30: Overview
SPS transverse impedance model
Benchmarking of the model
  Previous benchmarks
  Headtail growth rates
    Q20 optics
    Q26 optics
Conclusions and future plans

## Slide 31: Conclusions and future plans
HEADTAIL simulations with the SPS impedance model explains the frequency dependent behaviour of the headtail growth rates for both Q20 and Q26 optics
The simple analytical formula seems to work much better for Q20 than for Q26 (to be further investigated)
Headtail growth rates measurements in the horizontal plane

## Slide 32: Thank you for your attention

## Slide 33: Appendix

## Slide 34: Growth rate versus chromaticity: Measurements
Fitting curves

## Slide 35: Growth rate versus chromaticity: Measurements
Beam Intensity measured at the PS

## Slide 36: Growth rate versus chromaticity: Measurements

## Slide 37: Growth rate versus chromaticity: Measurements

## Slide 38: Headtail growth rates: analytical calculation