## Slide 1: Analysis of schemes for doublet production
J. F. Esteban Müller, E. Shaposhnikova
LIU-SPS BD WG – 30 January 2014
Acknowledgments:
T. Argyropoulos, H. Bartosik, T. Bohl, G. Iadarola, G. Rumolo, H. Timko

## Slide 2: Outline
Introduction
Schemes:
  LHC at injection
  SPS at injection
  SPS at 200 GeV
  SPS at flat top
Conclusions

## Slide 3: Introduction (I)
Special beam made of bunch doublets is considered for scrubbing of the LHC
  Enhance e-cloud  Reduction of the scrubbing time needed (Simulations by G. Iadarola & G. Rumolo)
Doublets spacing:
  Split in the LHC  2.5 ns
  Split in the SPS  5 ns: Preferred option

## Slide 4: Introduction (II)
Splitting process:
Small energy spread needed to reduce losses and emittance blow-up  Minimum initial voltage
RF phase shift of 180º or injection to unstable phase
Filamentation  Emittance ≈ bucket area
Particles move away from unstable phase
When particles are around the new stable phase, voltage quickly increased to capture them

## Slide 5: Introduction (III)
Main issues:
  Particle losses
  Emittance blow-up
  25 ns high intensity (> 1.5x1011 ppb) Slower acceleration in SPS due to the power limitation
Simulations using ESME without intensity effects
  Losses and emittance blow-up may be underestimated
  Minimum voltage in the SPS was chosen taking into account the beam loading
4 different schemes:
  LHC at injection
  SPS at injection
  SPS at 200 GeV
  SPS at flat top
800 MHz RF system off during splitting to minimize losses, because it operates in BSM

## Slide 6: LHC at injection (I)
SPS settings:
  Gaussian bunch of 0.5 eVs
  Voltage reduced to 1 MV before extraction (2.88 ns)
LHC settings:
  Injection at 3 MV
  Voltage step to 4 MV 11 ms after  Losses 2 %

## Slide 7: LHC at injection (II)
Doublet: 2.07 ns bunch length  0.90 eVs
Subsequent injections:
  Losses > 20 % after 3 more injections
  Up to 12 injections needed to fill the LHC
  Voltage program can be optimized to reduce losses: 1st inj. 3↗3.5 MV, 2nd inj. 3.5↗4 MV, 3rd inj. 4↗4.5 MV, …  But losses at injection rise to 5%

## Slide 8: Summary: LHC at injection
Advantages:
  Doublets issues restricted only to the LHC
  No special RF hardware required
Disadvantages:
  High losses at high energy
  Large emittance blow-up
  2.5 ns doublet spacing is less efficient than 5 ns

## Slide 9: SPS at injection (I)
PS settings to reproduce measurements:
  Distribution generated from bunch profile at the PS extraction (h=48, 300 kV)
SPS settings:
  Q26 optics (for comparison with measurements)
  Injection at 1 MV (beam loading issues for lower voltage)
  Voltage step to 3 MV 1 ms after (rise time 8 ms)

## Slide 10: SPS at injection (II)
Results:
  Emittance blow-up: 0.35  0.42 eVs
  Losses < 1 % due to the very small energy spread of the injected bunch
Subsequent injections:
  Losses 8 % after 3 more injections  Emittance reduced to 0.38 eVs
  Only 4 injections needed (maybe 5 if using BCMS)
  Losses can be compensated by injecting higher intensities from the PS

## Slide 11: SPS at injection (III)
T. Argyropoulos, H. Bartosik, T. Bohl, G. Iadarola, G. Rumolo, H. Timko
Comparison with measurements:
  Splitting well reproduced
  Losses slightly higher in measurements  Effects not included in simulations as injection phase error, energy mismatch or intensity effects
Simulations
Measurements

## Slide 12: Summary: SPS at injection
Advantages:
  Acceptable losses and at low energy
  Small emittance blow up
  Already tested during MDs
  No special RF hardware required
Disadvantages:
  e-cloud can be an issue with this beam at injection energy
  Low level RF and transverse damper should work from injection to flat top

## Slide 13: SPS at 200 GeV (I)
SPS settings:
  Q20 optics
  Gaussian bunch of 0.35 eVs
  Voltage reduced to 1 MV before splitting (beam loading)
  Voltage step to 2 MV 2.2 ms after  Losses 5 %

## Slide 14: SPS at 200 GeV (II)
Emittance blow-up: 0.35  0.82 eVs
Acceleration to 450 GeV: Voltage program for 1 eVs bucket area (qp = 0.9)
Voltage at SPS extraction 7 MV
LHC injection: 6 MV  emittance blow-up to 1.04 eVs

## Slide 15: Summary: SPS at 200 GeV
Advantages:
  E-cloud weaker at 200 GeV
Disadvantages:
  Special RF hardware required for the phase jump
  Longer SPS cycle
  Larger emittance blow-up
  Higher losses at higher energy (200 GeV)

## Slide 16: SPS at flat top (I)
SPS settings:
  Q20 optics
  Gaussian bunch of 0.5 eVs
  Voltage reduced to 1 MV before splitting (beam loading)
  Voltage step to 2 MV 3.3 ms after  Losses 5 %

## Slide 17: SPS at flat top (II)
Emittance growth: 0.5  1.36 eVs
Voltage at SPS extraction 7 MV (2.99 ns bunch length)
LHC injection: 6 MV
  Emittance reduced to 1.2 eVs
  15 % injection losses
  1 % satellites

## Slide 18: Summary: SPS at flat top
Advantages:
  E-cloud weaker at 450 GeV
Disadvantages:
  Special RF hardware required for the phase jump
  Larger emittance blow-up
  High losses at high energy in both SPS and LHC

## Slide 19: Conclusions
The preferred scheme is the SPS at injection:
  5 ns doublet spacing
  Acceptable losses and at low energy
  Small emittance blow up
  Already tested during MDs
  No special RF hardware required
If e-cloud is too strong at 26 GeV:
  SPS scrubbing run with doublets
  Use the scheme “SPS at 200 GeV”