## Slide 1: Momentum slip-stacking of the nominal I-LHC beam in the SPS Particle simulations (preliminary)
T. Argyropoulos, E. Shaposhnikova
LIU-SPS BD WG 30/01/2014

## Slide 2: History
Previous studies in the SPS to increase bunch intensity:
  Protons: D. Boussard and Y. Mizumachi. Production of beams with high line-density by azimuthal combination of bunches in a synchrotron. IEEE Trans. Nucl. Sci. Vol. NS-26 No. 3, 3623, June 1979.
  Ions: T. Linnecar. Azimuthal combination - slip stacking. Slides, SLI Meeting 2001-10-11, CERN.
2013 proposal (R. Garoby): Interpose two super batches of the nominal I-LHC Beam (100 ns bunch spacing)beam of 50 ns bunch spacing.
Same way of implementation

## Slide 3: Slip-stacking procedure
Two super batches into the ring
Circulating in the ring diametrically opposed
Captured by the two pairs of 200 MHz TW cavities
Change frequency of each cavity pair  first batch is decelerated & second is accelerated
Until buckets are just touching (approximate condition for beam independence, =α=4)
Change both RFs at the centre frequency
Recapture both up and down batches with high enough RF Voltage  connection to the final emittance

## Slide 4: Slip-stacking procedure
Buckets do not interact in that case
In reality we need α>5 for both batches to slide without emittance blow-up
Simulations are focused on the last part –recapture of the batches

## Slide 5: Slip-stacking parameters
Based on: T. Bohl, Note-2013-26
Flat bottom: not studied here
  large recapture voltage needed
  influence of RF noise, IBS and space charge (observed under present operational conditions)

## Slide 6: Slip-stacking parameters
Flat top (450 GeV/c):
  Longitudinal emittance: εL = 0.125 eVs/A
  Initial RF Voltage: VRF = 0.225 MV (filling factor of 0.9)
  momentum separation: dp/p=2x10-3
  min. dist. of mean radial pos: ΔR = 6.8 mm
Simulations were performed for the last part bring the batches back starting from the maximum distance
from the central orbit

## Slide 7: Designed RF programs
Programs calculated for a single RF for constant bucket area

## Slide 8: Varying parameters
  ΔfRF
  Time of the cycle, Tcycle
  Time of recapture
  VRF recapture
  Tcycle
  ΔfRF

## Slide 9: Example ΔfRF = 4fs
Initial losses (~2 %) can be possibly eliminated

## Slide 10: Example ΔfRF = 4fs
εL = 0.3 eVs/A
Losses = 10 %
Decreasing VRF = 0.7 MV
εL = 0.29 eVs/A
Losses = 15 %

## Slide 11: ΔfRF < 4fs
εL = 0.3 eVs/A
Losses = 7 %
Decreasing VRF = 0.7 MV
εL = 0.28 eVs/A
Losses = 12-15 %
For ΔfRF > 4fs we don’t gain in intensity but more emittance blow-up

## Slide 12: Increasing Tcycle
Increasing the total time reduces the losses by ~ 20 %
And also the final εL can be reduced by a ~5%
More time is still needed for fine tuning

## Slide 13: Summury
Time required for manipulations: ~ 1.0 s ttot = 0.45 s (slipping) + 0.2 s (up-down) +0.35 s (filamentation)
(maybe more time will be needed, +0.2 s ?)
Beam parameters: losses >7%, emittance blow-up by ~ factor 2.5 => OK for extraction to LHC after 200 MHz upgrade in the SPS (or 200 MHz in LHC)
Further optimization is needed!