## Slide 1: Impedance of the 800 MHz cavity.
Summer student: Bazyl Dmitry, NRNU “MEPhI”
Supervisors: Elena Shaposhnikova,
José Enrique Varela Campelo,
CERN, BE-RF department.
06 August, LIU-SPS BD WG

## Slide 2: Content:
Introduction
Characterization of the fundamental mode
  Periodic cell - Dispersion diagram
    Simulations
  Full model - Frequency domain
      Simulations
      Measurements
Characterization of the higher order modes
    Wakefields
      Simulations
    Eigenmode – R/Q
      Simulations
      Measurements
Conclusion

## Slide 3: Characterization of the 800 MHz TWC:
Computation of the dispersion diagram for longitudinal modes using CST MWS software.
Measurements and computations of the acceleration voltage for the fundamental passband.
Computation of impedance of the longitudinal higher order modes.
Computation and measurements of the R/Q of the longitudinal higher order modes.
Introduction:

## Slide 4: Several reasons to do it:
No detailed information about the cavity. No information about the fundamental passband (central frequency, operating mode, acceleration voltage , and so on).
There is longitudinal beam instabilities in the SPS. No studies were done in a past for the longitudinal HOMs for the 800 MHz TWC. It is well known that HOMs have a negative impact on the beam quality. So it’s kind of necessary to check if there are any potentially dangerous HOMs.
Complete impedance model of the 800 MHz TWC is needed for beam dynamics studies.

## Slide 5: Content:
Introduction
Characterization of the fundamental mode
  Dispersion diagram
    Simulations – single cell
  Accelerating voltage
      Simulations
      Measurements
Characterization of the Higher Order Modes
    Wakefields
      Simulations
    Eigenmode – R/Q
      Simulations
      Measurements
Conclusion

## Slide 6: Dispersion diagram for longitudinal modes:
One cell model (x-cut plane)
Fundamental passband
Forward wave
accelerating mode
Central frequency of the
passband
Potentially high impedance regions

## Slide 7: Acceleration Voltage
Simulations
Measurements
Longitudinal effective acceleration voltage V is an important quantity for the design of RF cavities. By knowing V one can calculate the longitudinal shunt impedance Rsh. eff. . The shunt impedance of an RF cavity determines how effectively this cavity can convert supplied RF power to accelerating gradient.
vs

## Slide 8
Frequency domain simulations in CST MWS were done for the fundamental passband.
Results of the simulations were post-processed using MATLAB. As the result, the effective longitudinal acceleration voltage was computed for 150 frequencies in the fundamental passband.
Full model (x-cut plane)
Acceleration Voltage - Simulations

## Slide 9
Bead-pull
Nonresonant perturbation theory
Post-process measurements -> get the fields using mathematical approach from [1]
Calculate accelerating voltage
PC
Vector Network Analyzer
Motor controller
Needle
Cavity
[1] A Nonresonant Perturbation Theory // Steele, C.W., Microwave Theory and Techniques, IEEE Transactions (Volume: 14, Issue: 2), 1966.
Acceleration Voltage - Measurements

## Slide 10
Acceleration Voltage - Measurements

## Slide 11
Measured broadband matching of -19.5 dB
Maximum voltage for 0.5W input power 2.48 kV
pA at 800.8MHz is 91.2deg
Acceleration Voltage – Measurements vs Simulations

## Slide 12
pA at 800.8MHz is 91.2 deg
Amplitude difference = 9%
Acceleration Voltage – Measurements vs Simulations

## Slide 13: Content:
Introduction
  Characterize the 800 MHz TWC
    Describe the cavity
  Several reasons
    There is no detailed info on the cavity
    Impedance of the HOMs
Characterization of the fundamental mode
  Periodic cell - Dispersion diagram
    Simulations
  Full model - Frequency domain
      Simulations
      Measurements
Characterization of the Higher Order Modes
    Full model - Wakefields
      Simulations
    Full model - Eigenmode – R/Q
      Simulations
      Measurements
Conclusion

## Slide 14: Characterization of the Higher Order Modes
Computation of Impedance of the longitudinal higher order modes using CST Wakefield solver.
Computation and measurements of the R/Q for the longitudinal higher order modes.
Simulations | Measurements
Wakefield | -
R/Q | R/Q

## Slide 15
Wakefield simulation
HOM#1
F1 = 1.935 GHz
Abs(Z) = 319 kOhm
Fundamental mode;
F = 800.8 MHz
Abs(Z) = 809 kOhm
HOM#2
F1 = 2.59 GHz
Abs(Z)= 73 kOhm

## Slide 16: R/Q simulations
Using the information about the location of longitudinal higher order modes that we’ve got from the wakefield simulation we have computed R/Q values for two modes with frequencies F = 1.9 GHz and F = 2.59 GHz respectively.
All simulations were done in CST MWS using eigenmode solver.

## Slide 17: R/Q Simulations – F = 1.9 GHz

## Slide 18
R/Q Simulations – F = 2.59GHz

## Slide 19
R/Q - Simulations vs measurements – F = 1.9 GHz
№ | F, GHz | Measured R/Q¦¦, Ohm | Simulated R/Q¦¦, Ohm
1 | 1.9219 | 0.19 | 0.51
2 | 1.9230 | 0.21 | 0.49
3 | 1.9307 | 11.9 | 11.3
4 | 1.9347 | 90.4 | 96.1
5 | 1.9367 | 16.4 | 13.1

## Slide 20
R/Q – simulations vs measurements – 1.9 GHz
F = 1.935 GHz
R/Q sim. = 96.1 Ohm
R/Q meas. = 90.4 Ohm

## Slide 21: Conclusion and further work:
Acceleration voltage was computed and measured. The results showed that computed values is in a good agreement with experimental data.
Wakefield simulation show that there is two potentially dangerous longitudinal higher order modes.
Measured and computed values of R/Q are in a good agreement but there is still noise in the measured field profiles. Also the measured field doesn’t completely fit to the simulated one.
  Further measurements of HOMs needed (improve signal excitation, etc)
  Carry out the measurements of the R/Q for F = 2.59 GHz mode and compare it to computed values.