## Slide 1: Shielding of the SPS Vacuum Flanges - Design Studies –
Jose E. Varela and Jaime Perez
12 March 2015

## Slide 2: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 3: Introduction
Today we report on the progress made in the design of suitable shields for vacuum flanges belonging to group I.
This presentation will not cover the redesign of the bellows belonging to group I (production of elliptical bellows) nor the impedance reduction measures for flanges belonging to group II (QD flanges).
More information can be found in previous presentations [LIU-SPS BD WG meetings on 09-10-2014 and 04-09-2014]

## Slide 4: Introduction
Originally, two shield concepts were proposed to reduce, not only the impedance, but also the R/Q of the 1.4GHz resonance coming from the SPS vacuum flanges.
It was demonstrated, by means of simulations and measurements, that these two solutions could reduce the R/Q by factor 8-10.
Today, we report on the design of shields that significantly reduce the impedance and satisfy both vacuum and mechanical requirements.

## Slide 5: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 6: Reference Model (I)
An MBA – MBA closed flange with a short bellows was chosen as reference model.
  As opposed to enamelled flanges, the analysis is much simpler and faster.
  Comparison with future measurements is straight forward.
All comparisons are made in terms of R/Q since the direct impedance comparison is not fair.
Of course, the other flange types (in group I) will experience a similar R/Q reduction for a given strategy.

## Slide 7: Reference Model (II)
 |  | Damping Resistor | fres [GHz] | Q | Z [kΩ] | R/Q [Ω]
MBA – QF Non enamelled | HFSS | No | 1.415 | 1828 | 145 | 80
 | Wake | No | 1.404 | 1750 | 138 | 79
 | Eig. | No | 1.413 | 1800 | 150 | 82
 | Meas. | No | 1.401 | 1300 | 111 | 85 ± 2.5%
 | Meas. | Short | 1.395 | 200 | 16 | 81 ± 2.5%
In addition, the R/Q of this type of flange is well known. It has been computed in three different ways and measured with very good agreement.

## Slide 8: Reference Model (and III)
f [GHz] | Z [kΩ] | Q | R/Q [Ω]
1.40 | 145 | 1850 | 78
2.35 | 23.8 | 1650 | 14.4
In order to have a fair comparison, a new model was created.
This model is used as the standard geometry to which the shields are attached to.
All the simulations were run with the same configuration.
Im(Z)/n ≈ 3.53mΩ

## Slide 9: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 10: Shield Implementation – General Considerations
Several simplifications were introduced to simplify the analysis. These simplifications are consistent for all four different shields.
As aforementioned, the selected study case has short bellows. The specification for the compression/extrusion of this type of bellows is ± 4mm. However, this study considers that the bellows can be compressed/extruded up to ± 10mm to be on the safe side.
The ± 10mm variation analysis allows us to ‘be prepared’ for non-conformal cases. In practice, we could work with ‘ranges’, i.e. produce a certain percentage of shields slightly longer/smaller to deal with these cases.
The following analysis deals only with the ‘shield’, the gap in the side without bellows is left untouched. As already shown, filling this gap has a significant impact on the overall impedance.
We consider three different positions for each possible shield implementation:
  Nominal
  Plus 10mm (extruded bellows)
  Minus 10mm (compressed bellows)

## Slide 11: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 12: Shield I
A model was built from the mechanical sketch.
Several simplifications were introduced to simplify the analysis. These simplifications are consistent for all four different shields.
The convolution was assumed to be thicker and to have perfect contact with the two shield parts.

## Slide 13: Shield I
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.55 | 14.3 | 550 | 26 | 1.19mΩ
Plus 10 | 1.54 | 9.1 | 410 | 22 | -
Minus 10 | 1.37 | 9.0 | 490 | 13 | -
Impedance of the ‘Plus 10mm’ case
This shield implementation manages to reduce the R/Q of the main resonance a factor ≈3 in the nominal case.

## Slide 14: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 15: Shield II
Two part shield with convolutions on the horizontal plane.
Same simplifications were used in the construction of the model:
The convolution was assumed to be thicker and to have perfect contact with the two shield parts.

## Slide 16: Shield II
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.33 | 4.6 | 350 | 13 | 0.95 mΩ
Plus 10 | 1.31 | 4.2 | 350 | 12 | 0.94 mΩ
Minus 10 | 1.35 | 5.0 | 350 | 14 | 0.80 mΩ
Impedance of the ‘Plus 10mm’ case
This shield implementation manages to reduce the R/Q of the main resonance a factor ≈ 6 in the three cases.

## Slide 17: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 18: Shield III
Single piece shield with the convolutions making ‘contact’ with the flange walls.
In principle, this solution would be reasonable if the movement of the bellows is constrained to ±5mm.
The ±10mm case has been analysed here for comparison purposes.
Same simplifications were used in the construction of the model:

## Slide 19: Shield III
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.45 | 6.5 | 410 | 16 | 1.62 mΩ
Plus 10 | 1.48 | 6.3 | 460 | 14 | -
Minus 10 | 1.43 | 5.6 | 370 | 17 | -
Impedance of the ‘Nominal’ case
This shield implementation manages to reduce the R/Q of the main resonance a factor ≈ 5 in the Nominal case.

## Slide 20: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 21: Shield IV
Tube-like shield without convolutions (similar to the current shield of the pumping ports). Fingers making contact near the bellows region.
The fingers are very simplified in the model.

## Slide 22: Shield IV
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.53 | 30 | 880 | 34 | 1.31 mΩ
Plus 10 | 1.49 | 46 | 990 | 47 | -
Minus 10 | 1.51 | 8 | 470 | 17 | -
Impedance of the ‘Nominal’ case
This shield implementation manages to reduce the R/Q of the main resonance a factor ≈ 2.3 in the Nominal case.
Cleanest spectrum!
No high frequency resonances

## Slide 23: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 24: Shield Comparison - R/Q Reduction
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Ref | 1.40 | 145 | 1850 | 78 | 3.53mΩ
Shield I | 1.55 | 14.3 | 550 | 26 | 1.19mΩ
Shield II | 1.33 | 4.6 | 350 | 13 | 0.95mΩ
Shield IV | 1.53 | 29.8 | 880 | 34 | 1.31mΩ
Vacuum Flange Shield Comparison of the ‘1.4GHz Resonance’ and Low Frequency Contribution
Overestimated Q values.
NOT COMPARABLE
Relevant parameters for comparison
As expected, ‘Shield II’ gives the biggest reduction in both R/Q and Im(Z)/n.
For reference, the initial proposal for the shielding of the bellows was:
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω]
Measurement | 1.4 | >0.7 | >55 | 13.3
Sim. Wake | 1.3 | 9 | 525 | 16
Sim. Eig. | 1.3 | 8.6 | 510 | 17

## Slide 25: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 26: Detailed Analysis - Shield II
The more detailed analysis of this implementation considers:
  The real thickness and shape of the convolutions
  A finer mesh
The results of this analysis point out in which direction we should continue

## Slide 27: Detailed Analysis – Shield II
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.32 | 4.0 | 325 | 12 | 1.25 mΩ
Plus 10 | - | - | - | - | -
Minus 7 | 1.32 | 3.8 | 320 | 12 | 1.24 mΩ
Impedance of the ‘Minus 7mm’ case

## Slide 28: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 29: Next Steps
From the design point of view, there are three main points of interest:
  The combination of the convolutions of ‘Shield II’ with a tube-like shield (similar to the current pumping port shields) in one or both sides.
  Mitigation of the consequences of the potential gap between shield and vacuum chamber.
  First steps towards building a prototype.
    Some details can not be simulated and measurements are necessary.
    Check availability of spare parts to build the prototype.
From the organization point of view:
  A detailed list of positions is in preparation
    With relevant information such as,
      Type of flange
      Type of intervention needed
      …
  Cost estimation – Once the position list is completed
    Schedule estimation

## Slide 30: Next Steps
From the design point of view, there are three main points of interest:
  The combination of the convolutions of ‘Shield II’ with a tube-like shield (similar to the current pumping port shields) in one or both sides.
  Mitigation of the consequences of the potential gap between shield and vacuum chamber.
  First steps towards building a prototype.
    Some details can not be simulated and measurements are necessary.
    Check availability of spare parts to build the prototype.
From the organization point of view:
  A detailed list of positions is in preparation
    With relevant information such as,
      Type of flange
      Type of intervention needed
      …
  Cost estimation – Once the position list is completed
    Schedule estimation

## Slide 31: Outline
Introduction
Vacuum Flange Shielding Studies
  Reference Model
  Shield Implementation – General Considerations
  Shield Implementation I
  Shield Implementation II
  Shield Implementation III
  Shield Implementation IV
Shield Comparison – R/Q Reduction
  Detailed Analysis - Shield Implementation II
Next Steps
Conclusions

## Slide 32: Conclusions
Progress in the design of a shielding for the SPS vacuum flanges belonging to group I has been reported.
The first batch of potential implementations has been analysed and the best one has been identified.
This solution is undergoing a second more detailed impedance assessment which shows the need to ensure good contact between the shield and the vacuum pipe in a known location.
Mainly, one additional implementation possibility has been identified and is currently under analysis.
First steps towards building a prototype will be taken in the near future. This will allow us to evaluate several important points which cannot be taken into account in simulations.