## Slide 1: Shielding of the SPS Vacuum Flanges - Design Studies – Update
Jose E. Varela and Jaime Perez
21 May 2015

## Slide 2: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 3: Introduction
Today we report on the progress made in the design of suitable shields for vacuum flanges belonging to group II.
This presentation will not cover the redesign of the bellows belonging to group II (production of elliptical bellows) nor the impedance reduction measures for flanges belonging to group I (QD flanges).
More information can be found in previous presentations [LIU-SPS BD WG meetings on 09-10-2014, 04-09-2014 and 12-03-2015]

## Slide 4: Introduction
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Ref | 1.40 | 145 | 1850 | 78 | 3.53mΩ
Shield I | 1.55 | 14.3 | 550 | 26 | 1.19mΩ
Shield II | 1.33 | 4.6 | 350 | 13 | 0.95mΩ
Shield IV | 1.53 | 29.8 | 880 | 34 | 1.31mΩ
Last time, four different shield implementations (without gap filling) were analysed and compared to the ‘reference’ (closed MBA-MBA vacuum flange without damping resistor) case.
Overestimated Q values.
NOT COMPARABLE
Relevant parameters for comparison
Three main points were stated as ‘next steps’:
  A more detailed analysis of the structure (realistic convolutions).
  The analysis of a tube-like shield (similar to the current pumping port shields) in one or both sides.
  Mitigation of the consequences of the potential gap between shield and vacuum chamber.
Vacuum Flange Shield Comparison of the ‘1.4GHz Resonance’ and Low Frequency Contribution.

## Slide 5: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 6: Previously…
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.33 | 4.6 | 350 | 13 | 0.95 mΩ
Plus 10 | 1.31 | 4.2 | 350 | 12 | 0.94 mΩ
Minus 10 | 1.35 | 5.0 | 350 | 14 | 0.80 mΩ
Impedance of the ‘Plus 10mm’ case
Initial (simplified) analysis showed that this implementation gives the highest impedance reduction.

## Slide 7: More Realistic Analysis
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Nominal | 1.32 | 4.0 | 325 | 12 | 1.25 mΩ
Plus 10 | 1.31 | 4.2 | 325 | 13 | 1.11 mΩ
Minus 7 | 1.32 | 3.8 | 320 | 12 | 1.24 mΩ
Impedance of the ‘Minus 7mm’ case
+ 25%

## Slide 8: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 9: Tube & Double Tube
Tube-like and double tube-like shields are also under consideration.

## Slide 10: Tube & Double Tube
Longitudinal impedance comparison at the nominal position for the reference, tube and double tube shields.
Im( Z )/n = 1.26
Im( Z )/n = 0.97
Im( Z )/n = 1.27
The double tube solution creates two small (but relevant) low frequency resonances that increase the Im(Z)/n.
The single tube solution improves the reference shield.

## Slide 11: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 12: Pumping Port Fingers
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Reference | 1.32 | 4.3 | 340 | 12.5 | 1.26 mΩ
Fingers | 1.34 | 4.6 | 340 | 13.7 | 1.03 mΩ
As anticipated, using RF fingers in the gap between the shield and the bellows wall reduces the impedance contribution of HOMs.

## Slide 13: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 14: Gap Filling
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Reference | 1.32 | 4.3 | 340 | 12.5 | 1.26 mΩ
Gap | 1.15 | 0.7 | 150 | 4 | 0.77 mΩ
Gap + fing | 1.15 | 0.6 | 145 | 4.3 | 0.54 mΩ
As shown in the past, filling the left gap further reduces the impedance.

## Slide 15: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 16: Shield Comparison - R/Q Reduction
 | f [GHz] | Z [kΩ] | Q | R/Q [Ω] | ≈Im( Z )/n
Original | 1.40 | 145 | 1850 | 78 | 3.53mΩ
Ref. | 1.32 | 4.3 | 340 | 12.5 | 1.26mΩ
Best | 1.15 | 0.62 | 145 | 4.3 | 0.54mΩ
Vacuum Flange Shield Comparison of the ‘1.4GHz Resonance’ and Low Frequency Contribution
Overestimated Q values.
NOT COMPARABLE
Relevant parameters for comparison
Best solution so far gives a factor ≈20 reduction in R/Q and a ≈ 85% reduction in Im(Z)/n.

## Slide 17: Outline
Introduction
Vacuum Flange Shielding Studies
  New Reference
  Tube & Double Tube
  Pumping Port Fingers
  Gap Filling
Shield Comparison – R/Q Reduction
Next Steps

## Slide 18: Next Steps
From the design point of view, once more, there are three main points of interest:
  The study of the ‘single tube’ + ‘PP fingers’ + ‘gap filling’ case.
  Extrusion/compression analysis for the best solution.
  The prototype was delayed, but we expect to have it soon available for measurements.
+