## Slide 1: BEAM LOADING COMPENSATION IN THE SPS. Motivation for a Model-based approach
P. Baudrenghien, CERN, BE-RF
T. Mastoridis, California Polytechnic State University, San Luis Obispo, USA

## Slide 2: Outline
A quick tour of the SPS Beam Loading compensation…
then the LHC…
then a glimpse of HiLumi…
and the strategy for LIU-SPS

## Slide 3: Beam Loading Compensation in the SPS
The SPS was designed as a low intensity accelerator. Regulation of the cavity field counted on a classic Amplitude/Phase loop tandem, with a time constant longer than one turn-> No effect on Transient Beam Loading and no effect on CBI
However the relatively low stored energy in the structure (200 MHz cavity) has given us some fears about transient beam loading …the only troublesome phenomena….are the rather well-known coupled bunch instabilities [Boussard, 77]
CBI (mode n=1) was observed in 1977 (1.2E13 ppp). A phase loop was added to cure it.
[Boussard, 77] D. Boussard et al., Longitudinal Phenomena in the CERN SPS, IEEE Trans. on NS, Vol. NS-24, No 3, June 77

## Slide 4
Above 1.8E13 ppp, more CBI modes were observed at injection (dipole, n=12,13) [Boussard, 79]
A novel RF feedback system was installed in 83, the so-called One-Turn delay Feedback (OTFB). The BW was covering +- 1 MHz. We had two systems, one feeding back on a 43 cells cavity and one on a 54 cells cavity
The design of an upgrade was launched in 1999 as part of the SPS as LHC injector project as the emittance must be kept below 0.6 eVs at 450 GeV
The OTFB was upgraded (increased BW and 1 system per cavity). A feedforward and later a longitudinal feedback acting on the 200 MHz cavities were added [Baudrenghien, 00, 01]
Installation/optimization took place during a series of SPS-LHC MDs during years 2000, 2001 and 2002 (longitudinal feedback)
A good dose of trial-and-error… The BW, for example, that much depends on the amplifier’s non-linearity.
[Boussard , 79] D. Boussard et al., Longitudinal Phenomena in the CERN SPS, IEEE Trans. on NS, Vol. NS-26, No 3, June 79
[Baudrenghien, 00] P. Baudrenghien, G. Lambert, Reducing the impedance of the Travelling Wave Cavities Feed-Forward and one turn delay feed-back, Chamonix X, Jan 2000
[Baudrenghien, 01] P. Baudrenghien, G. Lambert, Control of strong beam loading, Results with beam, Chamonix XI, Jan 2001

## Slide 5: Beam Loading Compensation in the LHC
The LHC was designed as an high intensity machine. Reduction of the cavity impedance was a must
The design included all possible beam loading mitigations
  Short loop delay RF feedback
  OTFB
  Feed-forward (planned but never installed)
But the design was done without precise specifications [Baudrenghien,07]
Around the LHC start-up, a collaboration was launched with SLAC, under the US-LARP agreement. They designed a complete model of the LLRF, from which they calculate the cavity impedance seen by the beam (at the fundamental), then the CBI growth rates. These are then compared to the Landau damping [Mastorides, 10]. This approach is closely inspired by the optimization of PEPII LLRF [Rivetta, 07].
[Baudrenghien,07] P. Baudrenghien et. Al., The LHC Low Level RF, presented at LLRF07 workshop
[Mastorides, 10] T. Mastorides et al., RF system models for the CERN Large Hadron Collider with application to longitudinal dynamics, PRST AB 13, 102801 (2010)
[Rivetta, 07] C. Rivetta et al., Modeling and simulation of longitudinal dynamics for Low Energy Ring-High Energy Ring at the Positron-Electron Project, PRST AB 10, 022801 (2007)
Modal growth rates for LHC (top) and PEP LER

## Slide 6: Beam Loading Compensation in the HiLumi LHC
The question is whether the present beam loading reduction will be sufficient for 2.2E11 p/bunch
Detailed model of the RF and LLRF, including cavity, klystron ,LLRF (digital and analog feedback, OTFB), latency (cables, waveguide, processing delay)
From these we compute the impedance seen by the beam Z(w)
Then we calculate the CBI growth rate
That we compare to the tune spread (simplified criterium)
P. Baudrenghien, T. Mastoridis, Fundamental Cavity Impedance and Longitudinal Coupled-Bunch Instabilities at the High Luminosity Large Hadron Collider, submitted to PRST AB
HiLumi LHC. Machine full before ramping. OTFB OFF. Dipole mode (m=1)

## Slide 7: Back to LIU-SPS
For the LHC the model-based calculations were done after completion of the design, and used to confirm that the installed system could deal with nominal intensity
For the HiLumi, the analysis confirms that the LLRF needs not be changed
For the LIU-SPS we want to use the model-based simulations to drive the specifications of the hardware being designed
This work is part of the collaboration on the HiLumi LHC.