## Slide 1: TWC 200 MHz impedance in BLonD and its effect on beam stability s LIU-SPS Beam Dynamics Working Group 03/11/2016
J. Repond

## Slide 2: Outline
Motivations
Simulations overview
TWC 200 MHz impedance
  HOMs
  Main harmonic, feedback and feed-forward
Conclusion and future work

## Slide 3: Motivations

## Slide 4: Motivations
Accelerating cavities known to be the main contributor to the impedance.

## Slide 5: Motivations
Accelerating cavities known to be the main contributor to the impedance.
Two major tasks in simulation

## Slide 6: Motivations
Accelerating cavities known to be the main contributor to the impedance.
Two major tasks in simulation
  Study different parts of the impedance model (TWC200) and their impact on the dynamic.

## Slide 7: Motivations
Accelerating cavities known to be the main contributor to the impedance.
Two major tasks in simulation
  Study different parts of the impedance model (TWC200) and their impact on the dynamic.
  Modelize correctly the low-level RF acting directly on the impedance seen by the beam.

## Slide 8: Simulations
SPS Flat-Top (451.15 GeV).
72 bunches spaced by 25ns.
Double RF (800 MHz), bunch shortening mode, 10% of the 200 MHz.
Two models of impedance and RF
  2x4 sections + 2x5 sections TWC 200 MHz + Flanges + max 7 MV available.
  4x3 sections + 2x4 sections TWC 200 MHz + Flanges impedance reduction from J.Vasela (factor 20) + max 10 MV available.
Parameters : 1 million macroparticles and 256 slices per bunch.

## Slide 9: TWC 200 MHz impedance

## Slide 10: TWC 200 MHz impedance
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1997 | 850 | 450 | 1888. 9
0.2003 | 2060 | 400 | 5150
0.201 | 850 | 425 | 2000
0.6289 | 80 | 700 | 114.3
0.6299 | 220 | 250 | 880
0.914 | 770 | 5000 | 154
0.9148 | 772 | 5000 | 154.4
1.1319 | 132 | 4000 | 33
1.1331 | 156 | 5000 | 31.2
1.1335 | 160 | 5000 | 32
1.5073 | 174 | 8000 | 21.75
1.5076 | 236 | 8000 | 29.5
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1999 | 600 | 600 | 1000
0.2 | 2400 | 370 | 6486.5
0.2006 | 2200 | 600 | 3666.7
0.6291 | 260 | 300 | 866.7
0.6299 | 140 | 500 | 280
0.9142 | 940 | 4500 | 208.9
0.9148 | 720 | 4500 | 160
1.1317 | 520 | 4000 | 130
1.1332 | 196 | 4500 | 43.6
1.5074 | 240 | 7000 | 34.3
1.5078 | 184 | 7000 | 26.3
Two 4 tank 200 MHz Cavities
Two 5 tank 200 MHz Cavities

## Slide 11: TWC 200 MHz impedance
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1997 | 850 | 450 | 1888. 9
0.2003 | 2060 | 400 | 5150
0.201 | 850 | 425 | 2000
0.6289 | 80 | 700 | 114.3
0.6299 | 220 | 250 | 880
0.914 | 770 | 5000 | 154
0.9148 | 772 | 5000 | 154.4
1.1319 | 132 | 4000 | 33
1.1331 | 156 | 5000 | 31.2
1.1335 | 160 | 5000 | 32
1.5073 | 174 | 8000 | 21.75
1.5076 | 236 | 8000 | 29.5
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1999 | 600 | 600 | 1000
0.2 | 2400 | 370 | 6486.5
0.2006 | 2200 | 600 | 3666.7
0.6291 | 260 | 300 | 866.7
0.6299 | 140 | 500 | 280
0.9142 | 940 | 4500 | 208.9
0.9148 | 720 | 4500 | 160
1.1317 | 520 | 4000 | 130
1.1332 | 196 | 4500 | 43.6
1.5074 | 240 | 7000 | 34.3
1.5078 | 184 | 7000 | 26.3
Two 4 tank 200 MHz Cavities
Two 5 tank 200 MHz Cavities

## Slide 12: TWC 200 MHz HOMs
630MHz
915MHz

## Slide 13: TWC 200 MHz HOMs

## Slide 14: TWC 200 MHz HOMs
R/Q = cst

## Slide 15: TWC 200 MHz HOMs
R/Q = cst
Effects of the 915MHz negligible

## Slide 16: TWC 200 MHz HOMs

## Slide 17: TWC 200 MHz HOMs

## Slide 18: TWC 200 MHz HOMs
630 MHz HOM damping improves the situation already with small factor.
Present : 14% increase in threshold at 1.65 ns.
Future : 17% increase in threshold at 1.65 ns.
Worth to damp this harmonic.

## Slide 19: TWC 200 MHz HOMs

## Slide 20: TWC200 impedance
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1997 | 850 | 450 | 1888. 9
0.2003 | 2060 | 400 | 5150
0.201 | 850 | 425 | 2000
0.6289 | 80 | 700 | 114.3
0.6299 | 220 | 250 | 880
0.914 | 770 | 5000 | 154
0.9148 | 772 | 5000 | 154.4
1.1319 | 132 | 4000 | 33
1.1331 | 156 | 5000 | 31.2
1.1335 | 160 | 5000 | 32
1.5073 | 174 | 8000 | 21.75
1.5076 | 236 | 8000 | 29.5
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1999 | 600 | 600 | 1000
0.2 | 2400 | 370 | 6486.5
0.2006 | 2200 | 600 | 3666.7
0.6291 | 260 | 300 | 866.7
0.6299 | 140 | 500 | 280
0.9142 | 940 | 4500 | 208.9
0.9148 | 720 | 4500 | 160
1.1317 | 520 | 4000 | 130
1.1332 | 196 | 4500 | 43.6
1.5074 | 240 | 7000 | 34.3
1.5078 | 184 | 7000 | 26.3
Two 4 tank 200 MHz Cavities
Two 5 tank 200 MHz Cavities

## Slide 21: TWC 200 MHz HOMs
1130 MHz
1500 MHz

## Slide 22: TWC 200 MHz HOMs

## Slide 23: TWC 200 MHz HOMs
Effects of higher HOM negligible

## Slide 24: TWC 200 MHz Main Harmonic
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1997 | 850 | 450 | 1888. 9
0.2003 | 2060 | 400 | 5150
0.201 | 850 | 425 | 2000
0.6289 | 80 | 700 | 114.3
0.6299 | 220 | 250 | 880
0.914 | 770 | 5000 | 154
0.9148 | 772 | 5000 | 154.4
1.1319 | 132 | 4000 | 33
1.1331 | 156 | 5000 | 31.2
1.1335 | 160 | 5000 | 32
1.5073 | 174 | 8000 | 21.75
1.5076 | 236 | 8000 | 29.5
fr [GHz] | Rsh [kOhm] | Q | R/Q [Ohm]
0.1999 | 600 | 600 | 1000
0.2 | 2400 | 370 | 6486.5
0.2006 | 2200 | 600 | 3666.7
0.6291 | 260 | 300 | 866.7
0.6299 | 140 | 500 | 280
0.9142 | 940 | 4500 | 208.9
0.9148 | 720 | 4500 | 160
1.1317 | 520 | 4000 | 130
1.1332 | 196 | 4500 | 43.6
1.5074 | 240 | 7000 | 34.3
1.5078 | 184 | 7000 | 26.3
Two 4 tank 200 MHz Cavities
Two 5 tank 200 MHz Cavities

## Slide 25: TWC 200 MHz Main Harmonic
200 MHz

## Slide 26: TWC 200 MHz Main Harmonic
Main contribution to all the impedance.

## Slide 27: TWC 200 MHz Main Harmonic
Main contribution to all the impedance.
Beam loading effect

## Slide 28: TWC 200 MHz Main Harmonic
Main contribution to all the impedance.
Beam loading effect
  Voltage seen by the beam smaller.
  Synchronous phase shifted.
Thank to T. Argyropoulos for the figure.

## Slide 29: TWC 200 MHz Main Harmonic
Main contribution to all the impedance.
Beam loading effect
  Voltage seen by the beam smaller.
  Synchronous phase shifted.
FF and FB try to correct phase
  and voltage -> First approx.
  20 dB reduction.
Thank to T. Argyropoulos for the figure.
-20dB

## Slide 30: Beam loading and FF/FB
FF and FB act on a window in frequency (+- 6MHz both sides).

## Slide 31: Beam loading and FF/FB
FF and FB act on a window in frequency (+- 6MHz both sides).
Model not sufficient to simulate the effects of FF/FB.
Synchronous phase shift.

## Slide 32: Synchronous phase shift
Synchronous phase shift, measurements 21.09.2016.
Synchronous phase shift, simulations without FB,FF.

## Slide 33: Beam loading and FF/FB
Thank to T. Argyropoulos for the figure.
(see T. Argyropoulos thesis)

## Slide 34: Synchronous phase shift
Synchronous phase shift, measurements 21.09.2016.
Synchronous phase shift, simulations using more accurate model of FB,FF.
Need qualibration of Hff and Hfb, simulations running.

## Slide 35: Conclusion
The most important HOM is the 630 MHz one.
Compensation of the beam loading needs a more accurate model.
Future work
  Qualibrate the FF/FB impedance reduction and check old predictions.
  Take into account the maximum power available (maximum voltage)

## Slide 36: Thank you for your attention !
Acknowledgement
  Many thanks to the BLonD team for countless fruitful discussions.
  Thank to T. Argyropoulos for priceless discussions about the FB/FF and the figures.
  Thank to G. Hagmann for the help with the feedback.