## Slide 1: 200 MHz TWC impedance
LIU-SPS BD WG meeting
3.11.2016

## Slide 2: Beam loading
V=4.5 MV is used on flat bottom for beam capture:
  Depending on RF power limit (700 kW, 750 kW or 1.05 MW) limitation on beam intensity changes from 1.5E11 to 2.4E11 => Effect of transients?
Beam losses on flat bottom are unacceptably high (~ 20%) for injected intensities above 1.8E11 and further increase with intensity
Due to bunch shape after rotation in the PS, the SPS bucket is completely full => continuous losses on the SPS flat bottom
Motion of uncaptured beam after injection shows large energy loss
Bunch lifetime decreases along the batch – compatible with e-cloud and beam loading effect

## Slide 3: 200 MHz TWC impedance
The 200~MHz impedance model used in beam dynamics simulations is different from analytical model of G. Dome –approximation of CST simulations by a few resonators (J. Varela)
BLonD simulations (done by J. Repond) show that different assumptions about impedance reduction by one-turn FB (amplitude and bandwidth) significantly affect multi-bunch stability threshold on the SPS flat top