## Slide 1: Preliminary results of simulations with 72 proton bunches s LIU-SPS Beam Dynamics Working Group 18/02/2015
A. Lasheen, J. Repond, E. Shaposhnikova

## Slide 2: Simulations with 24 bunches – “unrealistic”
Nominal LHC
SPS goal
(before scraping)
Impedance reduction gain (complete removal):
1: Flanges QF-type + HOM 630MHz
2: (1) + MKP
3: (2) + Flanges QD-type + other HOMs
1
2
3
3
1
2
Limit after LS2 without impedance reduction (reference point)
36 bunches measured instability threshold (2015)
72 bunches measured instability threshold (2012)

## Slide 3: Simulations with 24 bunches – “realistic”
Bunch length [ns]
Intensity threshold [1011 ppb]
24 bunches at flat-top, bunch shortening mode V200MHz = 7 MV, V800MHz = 0.7 MV
Achieved
Impedance reduction gain (“realistic” impedance reduction):
No impedance reduction
Impedance reduction
  QF flanges
  Main cavity higher order mode at 630 MHz divided by 3
Additional reduction of injection kicker (MKP) by 2
Not accessible
Longest bunch for transfer to LHC
LIU
HL-LHC
1.
2.
3.
4.
In order to have more realistic results for impedance reduction, simulations using 72 bunches were foreseen
Further development in BLonD allowed to lower the simulation time to ~1-3 days for 72 bunches

## Slide 4: Simulations with 72 bunches
Nominal LHC
Impedance reduction gain (“realistic” impedance reduction):
1: LIU baseline (Shielded QF type flanges and HOM 630MHz damping by a factor 3)
2: (1) + additional reduction of MKP (R divided by 2)
1
2
1
2
72 bunches measured instability threshold (2012)
SPS goal
(before scraping)

## Slide 5: Questions after 72 bunches simulations
Is there an impedance in the model that was overlooked, but that is dominant for 72 bunches ?
Is the “realistic” considerations (shielding model for the vacuum flanges, further damping of the HOM 630MHz by a factor 3), while already challenging, not enough to have an important gain in intensity ?
A new round of simulations to test as many assumptions as possible was started.

## Slide 6: Main contributions to the impedance model
HOM 200MHz cavity
BPV-QD flanges
BPH-QF flanges
MBA-QF & QF-QF closed with bellow
Unshielded pumping ports
Freq (Hz)
Abs(Z) (Ohm)

## Slide 7: Main impedances at high freq (flanges)
BPV-QD flanges
BPH-QF flanges
MBA-QF
Unshielded pumping ports
& QF-QF closed with bellow

## Slide 8: Kickers
Freq (Hz)
Abs(Z) (Ohm)

## Slide 9: Simulations with 72 bunches
Impedance reduction gain (complete removal):
1: Full
2: All HOMs
3: All Flanges
4: All Kickers
5: 2+3
6: 2+4
7: 3+4
8: 2+3+4

## Slide 10: Simulations with 72 bunches – Flanges
Impedance reduction gain (complete removal):
BQX = BPV-QD and BPH-QF
MQF = MBA-QF and QF-QF closed with bellow
UPP = Unshielded pumping ports
=> All those flanges has to be taken into account
PRELIMINARY !!

## Slide 11: Simulations with 72 bunches – HOMs
PRELIMINARY !!
Impedance reduction gain:
HOM630d3 = damping the 630MHz HOM by a factor 3
noHOM = removing ALL HOMs (200MHz and 800MHz)
=> The 630MHz HOM seems to be the most important one

## Slide 12: Conclusions and future work
Further simulations to check for the combinations of removing the HOM 630MHz, the different flanges (BPV-QD, BPH-QF, MBA-QF, QF-QF closed with bellow) and the unshielded pumping ports.
Specifications will be defined for the impedance reduction for the different type of flanges to have an acceptable gain in intensity. (but due to the high number of configurations, another strategy for simulations needs to be taken)
Simulations will be ran for 10MV and for the cavity configuration after LS2 (4 cavities of 3 sections + 2 cavities of 4 sections, vs 2 cavities of 4 sections + 2 cavities of 5 sections).
Simulations will be ran for 5MV to check the expected intensity gain if we do bunch rotation at flat top with the reduced impedance.