## Slide 1: Beam measurements and simulations for the last ion run (longitudinal plane) s LIU-SPS Beam Dynamics Working Group 18/02/2015
A. Lasheen, T. Bohl, E. Shaposhnikova, H. Timko

## Slide 2: Instability after transition crossing ?
During the ion run in December 2015, instabilities were observed in the longitudinal plane
The motivation to study the dynamics for ions was to test whether our simulations tools were able to reproduce what was observed in measurements (transition crossing + instabilities for ions)

## Slide 3: Outline
Measurements
Flat top simulations
Transition crossing simulations

## Slide 4: Measurements

## Slide 5: Measurements
Cycle: LHC_ION_12Inj_Q20_2015_V1 (LHCION2) –
Bunch spacing: 100ns – Batch spacing: 175ns (2 bunches per batch)
Important losses during the long flat bottom that leads to bunch-to-bunch variability
Data taken for 20 cycles (more data needed…)
Beam charges
Beam profile

## Slide 6: Variability in bunch length / intensity
Important losses during the long flat bottom that leads to bunch-to-bunch variability
In bunch length and intensity variability through the ramp :
Bunch length
Bunch intensity
Average
Minimum/Maximum
Average
Minimum/Maximum

## Slide 7: Variability in bunch length / intensity
Averaged for each bunch over all the acquired data
Bunches that stay longer at flat bottom: shorter and less intense
Error bars : 4
Bunch length before the ramp
Bunch intensity after losses

## Slide 8: Bunch phase oscillations
The two first bunches are stable (phase loop)
The first half (low intensity, small bunch length) is more unstable than the second (high intensity, long bunch length)
Example for Bunch #4
Dipole oscillations for each bunch

## Slide 9: Loss of Landau damping ?
Loss of Landau damping threshold for dipole mode in single RF:
Average bunch length before the ramp
Average bunch length at flat top

## Slide 10: Flat top simulations

## Slide 11: Simulations (BLonD)
Simulations were done taking flat top parameters (100,000 turns)
Loss of Landau damping was tested by giving a phase kick of +5° to the bunch, and the bunch is considered unstable if oscillations at the end of the simulations are > 2°
No intensity effects
With intensity effects
Bunch position (ns)
Bunch position (ns)

## Slide 12: Simulations
The loss of Landau damping scaling fits well with the simulations
There is a good agreement between measurements and simulations concerning the instability threshold (more measurement data needed…)

## Slide 13: Double RF system for ions
The second RF system in bunch shortening mode would give more synchrotron frequency spread, and lead to a better damping of these oscillations.

## Slide 14: Transition crossing simulations

## Slide 15: Momentum and RF program
The ramp was simulated using the real momentum program and RF voltage
Fixed frequency acceleration was included in the simulation

## Slide 16: Impedance & Space charge
The latest impedance model was used
The space charge impedance is much higher than for protons at flat bottom (17.07 Z GeV/c, Z/n~factor 10 w.r.t. protons at flat bottom)
Z/n (Ohm)
Abs(Z) (Ohm)
Time (s)
Freq (Hz)

## Slide 17: Impedance & Space charge
Impedance round uniform beam in rectangular chamber:
NB: was considered constant at the time the simulations were done => space charge slightly overestimated, but should be small impact (ln)
Z/n (Ohm)
Abs(Z) (Ohm)
Time (s)
Freq (Hz)

## Slide 18: Transition crossing simulations
A phase jump is applied on the RF phase, so that the bunch stays on the accelerating
Dipole oscillations are observed after transition crossing.
Bunch length during the ramp

## Slide 19: Intensity effects
Beam explodes after transition crossing
Very high intensity effects and important dipole oscillations after transition
Bunch length during the ramp

## Slide 20: LLRF implementation in BLonD
Fixed frequency acceleration
Phase loop
Fixed frequency acceleration, RF frequency is adjusted so that MHz in presence of the beam, but =>

## Slide 21: LLRF implementation in BLonD
Radial loop, LHC model (note from P. Baudrenghien):
is obtained from the average distribution at each simulation turn (no transverse coordinates in BLonD) from :
Machine dependent ? Necessity to implement a model that fits better the SPS implementation ?

## Slide 22: LLRF implementation in BLonD
Radial steering (the implementation in BLonD can be adjusted for slip stacking)
is given as an input

## Slide 23: Without intensity effects, with loops
The phase loop damps the dipole oscillations generated after transition crossing
Realistic gains are needed
Bunch length during the ramp

## Slide 24: With intensity effects, with loops
Radial loop has to be implemented to compensate long term drifts in the RF frequency and phase due to the synchronous phase shift due to intensity effects and for transition crossing
Realistic gains are needed for more realistic simulations
Bunch length during the ramp

## Slide 25: Conclusions and future work
The losses at flat bottom leads to a bunch-to-bunch variability, small bunches then suffer from loss of Landau damping (+ important perturbation due to transition crossing).
Models are ready to be used for future studies (slip stacking, higher intensities, etc.)
Higher orders of momentum compaction factor can be implemented when available
More realistic implementations and values of the gains are needed for the loops
Multibunch simulations through the ramp with intensity effects and loops are possible in a reasonable time (~3 days)