## Slide 1: LIU-SPS BD-WG
EM simulations studies for shielded vacuum flanges
Thomas Kaltenbacher with help of Christine Vollinger

## Slide 2: Outline
Which shielded VF design is in the current impedance model?
Study of double tube shielding performance
  VF gap fill
  RF-fingers at (weld) gap
Conclusions

## Slide 3: Current Status
Shielding for VF with 4-convolution bellows with MBA & QF beam pipes
The shielded VF with gap fill and RF-fingers is currently in the impedance model (J.E. Varela) and NOT the double tube shield
Shielding was referred to as ”shield II”
Shown values are given per element
f [GHz] | Q0 | R/Q [Ω]
1.33 | 350 | 13
w/o VF gap filling
with VF gap filling
f [GHz] | Q0 | R/Q [Ω]
1.15 | 145 | 4.3

## Slide 4: Unshielded Vs. Shielded VF
f [GHz] | Q0 [-] | R/Q [Ω]
1.41 | 1900 | 80.5
Unshielded VF
f [GHz] | Q0 [-] | R/Q [Ω]
1.55 | 186 | 4
Shielded VF & gap filled
f [GHz] | Q0 [-] | R/Q [Ω]
1.62 | 540 | 13.5
Shielded VF; no gap fill

## Slide 5: Shielded VF with & w/o gap fill
f [GHz] | Q0 [-] | R/Q [Ω]
1.55 | 186 | 4
Shielded VF & gap filled
f [GHz] | Q0 [-] | R/Q [Ω]
1.62 | 540 | 13.5
Shielded VF; no gap fill

## Slide 6: Shielded VF with & w/o RF-fingers

## Slide 7: Conclusions
Use RF-fingers or even better to close the gap (weld) structurally
VF gap filling is important to exploit shielding performance (R/Q scaling)
Reliable and robust shielding design needed: gap at weld, RF-fingers fixation and offsets, VF gap filling, etc.

## Slide 8: The End
THANK YOU!