## Slide 1: Follow up of Soft clamps production & testing Thomas Kaltenbacher & Christine Vollinger

## Slide 2: Open Questions (1/4)
Slide of Thomas from meeting 23/05/2016;
Shows the insulating layer on the beam pipe.
Proposed solution (José):
One strip of the insulation next to the VF is cut so that the copper braid of the clamp makes contact.

## Slide 3: Open Questions (2/4)
From tunnel visit:
Metal band from LEP era is still in place next to the VF.
Proposed solution (1):
Remove the metal band if it is without function.
Proposed solution (2):
Place the copper braid of the clamp more to the left of the VF.
Note: if there is an insulating foil and the metal band, the clamp has to be removed

## Slide 4: Open Questions (3/4)
From tunnel visit:
VSC equipment “isolating supports” next to the VF.
Proposed solution:
Make the connecting copper bridge (loop) longer so that the “isolating supports” does not pose an obstacle.

## Slide 5: Open Questions (4/4)
From tunnel visit:
The wide copper braid touches the orbital welds
Proposed solution:
Thin upstream clamp (9 mm wide) with slim (white) cable tie

## Slide 6: Remaining Open Question
In case we are going to do the test, shall we remove the QF SSS earth connection or not?
Pro removal: + avoid ground loops
Contra removal: + risk of floating sections
+ before LS1 many QF SSS were DC connected  ground loops