## Slide 1: Transverse Impedance General Considerations and Wake Field Simulations
Nasrin Esfahani
LIU-SPS BD WG – 11 May 2017

## Slide 2: Topics
The 900 MHz band HOM
Wake field results

## Slide 3: Field profiles of the π/2 mode
ϕ=90
f= 940.8 MHz
Electric Field
Magnetic Field

## Slide 4: Transverse force
y
x
ϕ= π/2 mode is not the disturbing HOM
x
y
Electric Fields

## Slide 5: Wake fields on a two-cell unit
909MHz
950MHz
Normalized Zx
ϕ= π/2 mode is not the disturbing HOM
920MHz

## Slide 6: Field profiles of the π/3 mode
ϕ=60
f= 939.6 MHz
t=0
t=T/4
Electric Fields

## Slide 7: Field profiles of the π/3 mode
ϕ=60
f= 939.6 MHz
t=0
t=T/4
Magnetic Fields

## Slide 8
ϕ= 60 ͦMode
y
x
Transverse force

## Slide 9: Wake field simulation
Freq (Hz)
Zx (Ω/m)
x

## Slide 10: Field profiles of the π/3 mode
ϕ=60
f= 939.6 MHz
t=0
t=T/4
Electric Fields

## Slide 11: 900 MHz band HOM
Freq (MHz) | Phase shift | Q | Type
939.2 (consistent with [1] and [2] ) | Approximately 60 | 61000 | Hybrid (consistent with [1] and [2])
[1] F. Caspers and G. Dome, “ The 938 MHz resonant damping loops for the 200 MHz SPS travelling wave cavities”, ATS-note-2012-065 (1982).
[2] R. J. Laukner and T. R. P Linnecar, “The transverse coupled bunch mode instability at 940 MHz in the SPS” SPS improvement report No. 186 (1979)

## Slide 12: Single section wake
Freq
Mode | F (MHz) | Real (Zx (MΩ/m))
1 | 937.04 | 34.7
2 | 937.77 | 16.3
Zx (Ω/m)

## Slide 13: Summary of the wake field results
 | Freq (MHz) | Zx (MΩ/m)
3 Cells | 937.12 | 10
11 Cells (without FPCs) | 937.04 | 34
11 Cells (with FPCS) | 937.45 | 28 (simulations on going)

## Slide 14: Measurement and Simulations
[1] R. J. Laukner and T. R. P Linnecar, “The transverse coupled bunch mode instability at 940 MHz in the SPS” SPS improvement report No. 186 (1979)
 | Freq (MHz) | Zx (4*11 cell)
[1] | 938 | 70 MΩ/m (Q=61000)
Wake field | 937.45 | 4*28=112 MΩ/m

## Slide 15: Conclusions
The 938 MHz HOM is a π/3 mode
Transverse wake fields on a single section (28 MΩ/m Horizontal mode)