## Slide 1: Measurements of beam instabilities during ramp with feedback off s 14th of September 2017
J. Repond
Acknowledgement: A. Lasheen, E. Shaposhnikova

## Slide 2: Instability threshold with 12 bunches
Courtesy: T. Argyropoulos
Latest results suggest:
Sharp dependence of intensity w.r.t. energy related to the feedback
Feedback more efficient at low energy
Focus on FB off

## Slide 3: MD Parameters
Dedicated MD: 12th of July, 23th of August and 6th of September 2017
LHC 25ns nominal cycle (Q20)
Single RF
Low Level RF:
  Phase loop: ON
  Longitudinal damper: ON/OFF
  Feedforward: OFF
  Feedback: OFF
  Blow-up: OFF
Batch: 12 bunches
Different emittances and voltage programs
Goals:
  Observe effect of LD on stability threshold
  Time when the instability is triggered w.r.t. intensity

## Slide 4: Intensity threshold 12 bunches – LD effect
Threshold~ ppb
LD off
LD on
Can be neglected in simulation
Threshold~ ppb
Threshold weakly affected by effect of LD
Time when instability starts (~energy) comparable (supported again on next slide)
Without feedback, its effect seems negligible

## Slide 5: Intensity threshold 12 bunches – time dependence
Courtesy: E. Shaposhnikova
For given voltage program  Minimum stability threshold during cycle can be estimated
Measured stability threshold is similar to analytical prediction
Constant filling factor
Could be used to find the frequency driving the instability
Gap
If Rsh=cst  Intensity

## Slide 6: Time dependence – different OP conditions
Analytical estimations show that the threshold:
  Decrease when emittance decrease
  Changes more weakly with voltage program
Measurements reproduce expectation
Ongoing study to extract, if possible, the leading frequency.
Bad shots, analysis must be refined

## Slide 7: Conclusion and future work
Effect of Longitudinal Damper negligeable in simulation
Time dependence of instability threshold similar to analytical estimation
  Maybe possible to extract the leading frequency
Ongoing study

## Slide 8
Thank you for your attention.

## Slide 9: Backup slides

## Slide 10: Instability threshold with 12 bunches
Sharp energy threshold with respect to bunch intensity
~6% scatter in bunch length
Courtesy: T. Argyropoulos

## Slide 11: Instability threshold with 12 bunches
Courtesy: T. Argyropoulos