## Slide 1: Latest MD results on losses
M. Schwarz
Acknowledgements:
A. Lasheen, J. Repond, P. Baudrenghien, E. Shaposhnikova H. Bartosik, T. Bohl, G. Papotti, SPS & PS operator team

## Slide 2
Losses at injection, possible sources:
  Transverse emittance?
  Longitudinal effects (bunch shape from PS, uncaptured PS beam,…)
  SPS llrf system
Losses at flat-bottom, possible sources:
  Momentum aperture and transverse emittance
  Full bucket (intensity effects, noise from llrf, magnetic field change,…)
Sources of losses
LHC25ns, V200=4.5MV

## Slide 3
MD 17/08/16: different momentum apertures
Settings:
72 bunches, 25ns spacing, vary intensity
LHC25ns (Q20) and LHC4inj (Q22),
Flat-bottom 0-11.1s, ramp to 450GeV 11.1-19.5s, flat-top 19.5-20s
Here: data from injection to first part of ramp (11.830s ~ 29 GeV)
About 10 acquisitions per data point
V200=4.5MV (Q20), V200=3.3MV (Q22), (4MV after 17:52), V800 = 0.1 V200
Momentum aperture δ=6.1e-3 (Q20) and δ=7.7e-3 (Q22) (Curtesy M. Patecki)
LHC25ns, Q20
LHC4inj, Q22
Slightly less losses for Q22

## Slide 4
MD 17/08/16: linear loss rate
rel. lin. loss, Q20
rel. lin. loss, Q22
Fit intensity by , : linear loss rate, : decay time
Relative linear loss rate: linear loss rate divided by initial intensity per bunch
,Q20
, Q22

## Slide 5
Δt = 2.7ms (120 turns),
450 points (4s to 5.2s)
Nyquist frequency 180 Hz
Noise at flat-bottom?
MD 17/08/23
MD 17/08/16
Δt = 55.3ms (2407 turns),
165 points (2s to 11.1s at flat-bottom)
Nyquist frequency 9 Hz
Under-sampled 50Hz?
Peak at half Nyquist frequency?
Take intensity at flat-bottom
Remove linear decrease
FFT
(inspired by F. Capsers)

## Slide 6
MD 17/08/23: different V200
Settings:
72 bunches, 25ns spacing, 1.3e11 particles per bunch
LHC25 (Q20), V800 = 0.1 V200
Flat-bottom 0-11.1s, ramp to 450GeV 11.1-19.5s, flat-top 19.5-20s
Here: data from injection to first part of ramp (11.830s ~ 29 GeV)
About 10 acquisitions per data point
Inject at V200=4.5MV (nominal case), change V200 at flat-bottom (ramp 50ms to 100ms after injection and at 10.75s)
MD 17/08/23
Minimal losses for V200=4.5MV
For V200=3.0MV
more losses at beginning, but
less during FB
For V200=7.0MV
less losses at beginning, but
more during FB

## Slide 7: MD 17/08/23: Intensities for different V200 at flat-bottom
Bucket height , V200=7MV momentum aperture ->
LHC25ns, V200=3.0MV
LHC25ns, V200=4.5MV
LHC25ns, V200=5.0 MV
LHC25ns, V200=7.0 MV
Uncaptured beam far
away from momentum aperture
BCT = batch
-> no uncaptured beam;
Losses from buckets

## Slide 8
Relative loss
Flat-bottom: before ramp ( for BCT, else)
Total: after ramp ()
Relative losses MD 17/08/23: different V200
Uncaptured beam lost at smaller dp/p -> further away from momentum aperture -> can ‘survive’ longer at flat-bottom
Uncaptured beam lost
at beginning of ramp
Why more losses
from bunch with smaller bucket area?
Bucket touches momentum acceptance -> scraping from bunch

## Slide 9
Fit Gaussian bunches to profiles at flat-bottom (starting 2s after injection)
Obtain bunch intensity and bunch length
Average bunch intensity normalized by maximum intensity at 2s of all data sets
Average bunch length change normalized bunch length at 2s of data set
MD 17/08/23: Bunch length vs intensity (Gaussian fit)
Intensity changes, but bunch length does not
-> bucket full

## Slide 10
‘typical’ pattern for V200=3MV, but constant pattern for V200=7MV voltage => losses due to scraping at V200=7MV
MD 17/08/23: Relative losses per bunch
3.0 MV
4.5 MV
5.0 MV
7.0 MV

## Slide 11
MD 17/08/30: Different transverse emittances
Settings:
48 bunches, 25ns spacing, 1.52e11 particles per bunch
V800 = 0.1 V200
Flat-bottom 0-11.1s, ramp to 450GeV 11.1-19.5s, flat-top 19.5-20s
Here: data from injection to first part of ramp (11.830s ~ 29 GeV)
About 10 acquisitions per data point
Inject at V200=4.5MV (nominal case), change V200 at flat-bottom (ramp 50ms to 100ms after injection and at 10.75s to 10.85s)
Compare LHC25ns and BCMS cycle (smaller transverse emittance)
Smaller losses for BCMS
Minimal losses
for V200=4.5MV

## Slide 12
Relative loss
Flat-bottom: before ramp ( for BCT, else)
Total: after ramp ()
MD 17/08/30: Relative losses
BCMS
LHC25ns
MD 17/08/30
Less losses for smaller transverse emittance

## Slide 13
MD 17/08/30: V200 increase after at 50ms vs 1ms
Lost particles recaptured earlier ->
BCT and batch intensity equal earlier
BCMS, V200=7.0MV
BCMS, V200=7.0MV @1ms

## Slide 14
V200=4.5MV minimizes overall losses
  Reducing V200 leads to particles lost at injection
  Increasing V200 leads to scraping from bucket
    momentum aperture for Q20
  Reducing transverse emittance lowers losses
Summary
Thank you for your attention!
Next steps
BLonD simulations with 72 bunches and Helga’s dynamic feed-back implementation
More systematic studies of uncaptured beam

## Slide 15
DETAILS MD 17/08/23: different V200
Settings:
72 bunches, 25ns spacing, 1.3e11 particles per bunch
LHC25 (Q20), V800 = 0.1 V200
Flat-bottom 0-11.1s, ramp to 450GeV 11.1-19.5s, flat-top 19.5-20s
Here: data from injection to first part of ramp (11.830s ~ 29 GeV)
About 10 acquisitions per data point
Inject at V200=4.5MV (nominal case), change V200 at flat-bottom (ramp 50ms to 100ms after injection and at 10.75s)
MD 17/08/23
Minimal losses for V200=4.5MV
For V200=3.0MV
More losses at beginning, but
Less during FB
For V200=7.0MV
less losses at beginning, but
more during FB

## Slide 16
Relative loss
Flat-bottom: before ramp ( for BCT, else)
Total: after ramp ()
Relative losses MD 17/08/23: different V200
Uncaptured beam lost at smaller dp/p -> further away from momentum aperture -> can ‘survive’ longer at flat-bottom
Uncaptured beam lost
at beginning of ramp
Why more losses
from bunch with smaller bucket area?
Bucket touches momentum acceptance -> scraping from bunch

## Slide 17: MD 17/08/23: Intensities for different V200 at flat-bottom
MD 17/08/23
LHC25ns, V200=3.0MV
LHC25ns, V200=4.5MV
LHC25ns, V200=5.0 MV
LHC25ns, V200=7.0 MV
Uncaptured beam far
away from momentum aperture
BCT = batch
-> no uncaptured beam;
Losses from buckets

## Slide 18
‘typical’ pattern for 3MV, but constant pattern for 7MV voltage => losses due to scraping at 7MV
MD 17/08/23: Relative losses per bunch
3.0 MV
4.5 MV
5.0 MV
7.0 MV

## Slide 19
Fit Gaussian bunches to profiles at flat-bottom (2s after injection)
Obtain bunch intensity and bunch length
Average bunch intensity normalized by maximum intensity at 2s of all data sets
Average bunch length change normalized bunch length at 2s of data set
MD 17/08/23: Bunch length vs intensity (Gaussian fit)
Intensity changes, but bunch length does not
-> bucket full

## Slide 20
DETAILS MD 17/08/30: Different transverse emittances
Settings:
48 bunches, 25ns spacing, 1.52e11 particles per bunch
V800 = 0.1 V200
Flat-bottom 0-11.1s, ramp to 450GeV 11.1-19.5s, flat-top 19.5-20s
Here: data from injection to first part of ramp (11.830s ~ 29 GeV)
About 10 acquisitions per data point
Inject at V200=4.5MV (nominal case), change V200 at flat-bottom (ramp 50ms to 100ms after injection and at 10.75s to 10.85s)
Compare LHC25ns and BCMS cycle (smaller transverse emittance)
Smaller losses for BCMS
Minimal losses
for V200=4.5MV

## Slide 21
Relative loss
Flat-bottom: before ramp ( for BCT, else)
Total: after ramp ()
MD 17/08/30: Relative losses
BCMS
LHC25ns
MD 17/08/30
Less losses for smaller transverse emittance

## Slide 22: MD 17/08/30:Intensities for different V200 at flat-bottom, LHC25ns
LHC25ns, V200=3.0MV
LHC25ns, V200=4.5MV
LHC25ns, V200=7.0MV
Uncaptured beam far
away from momentum aperture
BCT = batch
-> no uncaptured beam;
Losses from buckets

## Slide 23
BCMS, V200=3.0MV
BCMS, V200=6.0MV
BCMS, V200=4.5MV
BCMS, V200=7.0MV
MD 17/08/30:Intensities for different V200 at flat-bottom, BCMS
Uncaptured beam far
away from momentum aperture
BCT = batch
-> no uncaptured beam;
Losses from buckets

## Slide 24
MD 17/08/30: V200 increase after at 50ms vs 1ms
Lost particles recaptured earlier ->
BCT and batch intensity equal earlier
BCMS, V200=7.0MV
BCMS, V200=7.0MV @1ms

## Slide 25
MD 17/08/30: Relative losses per bunch, LHC25ns
LHC25ns, V200=3.0MV
LHC25ns, V200=4.5MV
LHC25ns, V200=7.0MV
MD 17/08/30

## Slide 26
MD 17/08/30: Relative losses per bunch, BCMS
BCMS, V200=3.0MV
BCMS, V200=4.5MV
BCMS, V200=6.0MV
BCMS, V200=7.0MV

## Slide 27
MD 17/08/30: Bunch length vs intensity (Gaussian fit),
LHC25ns
Compared to 1.3ppb, now change in bunch length
MD 17/08/30

## Slide 28
MD 17/08/30: Bunch length vs intensity, (Gaussian fit)
BCMS
MD 17/08/30

## Slide 29
DETAILS MD 17/08/16: different momentum apertures
Settings:
72 bunches, 25ns spacing, vary intensity
LHC25ns (Q20) and LHC4inj (Q22),
Flat-bottom 0-11.1s, ramp to 450GeV 11.1-19.5s, flat-top 19.5-20s
Here: data from injection to first part of ramp (11.830s ~ 29 GeV)
About 10 acquisitions per data point
V200=4.5MV (Q20), V200=3.3MV (Q22), (4MV after 17:52), V800 = 0.1 V200
Momentum aperture δ=6.1e-3 (Q20) and δ=7.7e-3 (Q22) (Curtesy M. Patecki)
LHC25ns, Q20
LHC4inj, Q22
Slightly less losses for Q22

## Slide 30
MD 17/08/16:Intensities Q20
1.2e11ppb, Q20
1.44e11ppb, Q20
1.6e11ppb, Q20
1.75e11ppb, Q20

## Slide 31
MD 17/08/16:Intensities Q22
1.18e11ppb, Q22
1.42e11ppb, Q22
1.59e11ppb, Q22
1.72e11ppb, Q22

## Slide 32
MD 17/08/16: linear loss rate
rel. lin. loss, Q20
rel. lin. loss, Q22
Fit intensity by , : linear loss rate, : decay time
Relative linear loss rate: linear loss rate divided by initial intensity per bunch
,Q20
, Q22

## Slide 33
MD 17/08/16: Bunch length vs intensity, BCMS (Gaussian fit) Q22
Note: intensities normalized to maximum intensity at each set

## Slide 34
MD 17/08/16: Bunch length vs intensity, BCMS (Gaussian fit) Q22
Note: intensities normalized to maximum intensity at each set

## Slide 35
MD overview
48 bunches, 25ns spacing, 1.52e11 particles per bunch
BCMS & LHC25ns cycles
Vary V200 at flat-bottom
MD 17/08/30
72 bunches, 25ns spacing, V200,Q20 =4.5MV, V200,Q22 =3.3MV
LHC25ns(Q20) & LHC4inj(Q22) cycles
Vary intensity
MD 17/08/16
72 bunches, 25ns spacing, 1.3e11 particles per bunch
LHC25ns cycles
Vary V200 at flat-bottom
MD 17/08/23
72 bunches, 25ns spacing, V200,Q20 =4.5MV, V200,Q22 =3.3MV
LHC25ns(Q20) & LHC4inj(Q22) cycles
Vary intensity
MD 17/08/02

## Slide 36
Fit intensity by
: linear loss rate
: decay time
Linear loss rate
MD 17/08/23

## Slide 37
Relative losses per bunch
MD 17/08/23

## Slide 38
Fit intensity by
: linear loss rate
: decay time
Linear loss rate
BCMS
LHC25ns
MD 17/08/30

## Slide 39
Relative losses per bunch, BCMS
MD 17/08/30

## Slide 40
Relative losses per bunch, LHC25ns
MD 17/08/30