## Slide 1: TMCI and instability studies in Q22
Mario Beck – LIU-SPS BD WG -14.12.2017
Thanks to: Hannes Bartosik, Kevin Li, Giovanni Rumolo, Michael Schenk,
The injectors operator teams

## Slide 2: Introduction I
: machine circumference
: longitudinal emittance
: vertical chromaticity
: slippage factor
: Impedance of broad band resonator model
: resonance frequency of broad band resonator model
: revolution frequency of the machine
: betatron function of the machine
Transverse Mode Coupling Instability (TMCI) is a single bunch instability caused by the transverse wake field.
Theoretically the TMCI threshold can be described as seen below [1]:
[1] H. Bartosik - Beam dynamics and optics studies for the LHC injectors upgrade

## Slide 3: Introduction II
The influence of the variable factors of the intensity threshold will be investigated.
TMCI has been measured in the SPS in Q20 and Q26 optics before [1].
Now the measurements in the SPS Q22 optic.
TMCI represents an intensity limitation and is thus a potential issue for the LIU.

## Slide 4: Overview over MD
TMCI MD the 19th to 20th of October 2017.
We observe high losses in the SPS.

## Slide 5: Pattern of the losses
But are the losses we see due to TMCI?
YES! => we observe the traveling wave pattern typical for TMCI.

## Slide 6: Overview over MD II
To see effects of different parameters on the TMCI threshold, scans were done.

## Slide 7: Intensity scan I
We observed a TMCI threshold of 2.5e11 ppb in the SPS.
RF200 at 2.7 MV
~ 0.7
~ 0.32 [eVs]

## Slide 8: Intensity scan II (smaller )
We observed a lower TMCI threshold of 1.8e11 ppb as expected.
RF200 at 2.7 MV
~ 0.7
~ 0.22 [eVs]

## Slide 9: Emittance vs. intensity scan
RF200 at 2.7 MV
0.7
The dependency on intensity and longitudinal emittance are clearly observed.

## Slide 10: Compare to Simulations
As no turn by turn data of the first turns is available, the growth rate of the measured data is represented by the losses from PS to SPS.
PyHEADTAIL was used for the simulations.

## Slide 11: Chromaticity scan
~ 0.32 [eVs]
RF200 at 2.7 MV
As expected; higher chromaticity leads to a higher TMCI threshold.

## Slide 12: Conclusion & outlook
The TMCI has been observed an investigated during measurements in the Q22 optics.
The theoretical dependencies have been shown in measurements.
A good setup of the machines can lead to a TMCI threshold which might just be suffucient for LIU.
Test the effect of the damper and the transverse wideband feedback on LIU intensity TMCI [2].
[2] K. Li - SPS TMCI with the Q22 optics – HSC section meeting – 27.11.2017

## Slide 13: Thank you for your attention! Questions?

## Slide 14: Backup slides

## Slide 15
Q22 TMCI MD 19/20 October 2017

## Slide 16
Q22 TMCI MD 19/20 October 2017

## Slide 17: Introduction
TMCI (Transverse Mode Coupling Instability) also called fast head tail instability.
Instability created due to the transverse wake.
The leading (transverse offset) particles create a transverse wake which excites the trailing particles.
The particles exchange their positon every half synchrotron period; the faster the synchronous motion is the higher the instability threshold gets.

## Slide 18: RF200 voltage scan
Injecting less intensity seems to avoid the fast TMCI losses.
The threshold further seems to be further approached.
~ 0.7
~ 0.32 [eVs]
: synchrotron tune
: RF voltage
: reference energy

## Slide 19: RF200 voltage scan I
As the TMCI threshold also depends on we changed the RF200 voltage [3].
~ 0.32 [eVs]
~ 0.7
: synchrotron tune
: RF voltage
: reference energy
[3] K. Li – USPAS longitudinal beam dynamics - 2015

## Slide 20: RF200 voltage scan II
We observe a principal scaling with the RF voltage.
But also a higher intensity in the SPS when injected less from the PS.
should scale
with : 2e11 with 1.5 MV
for 3MV:
Correct!

## Slide 21: Connecting to [1, 2]
: synchrotron tune
: RF voltage
: reference energy
: reference momentum
: longitudinal bunch length
: machine circumference
: longitudinal emittance
: vertical chromaticity
: slippage factor
: Impedance of broad band resonator model
: resonance frequency of broad band resonator model
: revolution frequency of the machine
: betatron function of the machine

## Slide 22: Overview over MD
TMCI MD the 19th to 20th of October 2017.
In Q22 optics, single bunch, no acceleration.
Machine setup:
QPH = -0.05 => Q’ = 1.6
QPV = -0.3 => Q’ = 0.7
RF200 = 2.7 MV
RF800 = 0.27 MV
Beam Setup: PSB: MD4: MD_LHCINDIV_HI_INT_SPS_IMPEDANCE PS : MD7: MD_LHCINDIV_HI_INT_SPS_IMPEDANCE_PS SPS: LHC2: MD_26_L7200_Q22_2017_V1
[4] H. Bartosik – Q22 optics - SPS injection losses review, 30 November 2017
TMCI threshold for LIU: 2.6e11 ppb [4]