## Slide 1: Update on simulation of capture losses in the SPS
M. Schwarz
Acknowledgements:
A. Lasheen, J. Repond, P. Baudrenghien, E. Shaposhnikova T. Bohl, SPS operator team
BLonD team

## Slide 2: Simulation setup
72 bunches
  Gaussian bunch profile, sigma=0.9ns
impedance model:
  analytic cavity impedance for four 200 MHz TWC
  full SPS impedance model
feed-back model:
  2MHz single-sided bandwidth, ‘FB time constant: 3 turns’
Model injection by creating 72 bunches (25ns spacing) at the center of SPS RF-bucket
Model feedback by multiplying impedance with FB-reduction factor of P. Baudrenghien (Charmonix X, 2001)
No action of feedback at turn 1
Continuously increase feedback strength after turn 1
-15.5 dB at f_RF
(i.e. Z(f_RF) multiplied by factor 0.17)
Z -> Z x ΓFB

## Slide 3: Losses in simulation
At turn 0 (injection), count number of macroparticles inside separatrix N0, for each bunch
At each turn N, count number of macroparticles inside separatrix Nn, for each bunch
Losses = (Nn / N0)-1 , for each bunch

## Slide 4: Losses in simulation
Acquire beam profiles along cycle
Intensity of bunch ~ sum of bunch profile
Fit linear function
Losses = (fit(t0) – fit(tend))\fit(t0)
8% losses for bunch 71
8% losses
for each bunch

## Slide 5: Simulation vs Measurement
curtesy: A. Lasheen
Shape of simulated losses agrees well: increased losses up to ~ bunch 30, ‘dip’ at ~ bunch 45
But: measured losses show offset of about 15 percent
Only 200 MHz TWC analytic impedance

## Slide 6: Simulation vs Measurement
curtesy: A. Lasheen
Full SPS impedance model
Maximum of losses now at ~bunch 25
Measured losses show increase of ~15% along batch, but simulations only give ~6%

## Slide 7: Measurement of induced voltage
MD 2208 (2017-06-07)
FF on, FB delay 100 μs
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches
Measured cavity voltage at f_RF from I/Q modulator
Scaled with beam intensity for each acquisition
Amplitude = sqrt(I^2+Q^2)
Average amplitude over acquisitions

## Slide 8: Measured losses
MD 2208 (2017-06-07)
FF on, FB delay 100 μs
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches
Single acquisition
Single acquisition
Averaged over all acquisition
Losses increase
during ramping

## Slide 9: Normalized amplitude

## Slide 10: Normalized amplitude

## Slide 11: Simulations vs Measurement
No FF,
FB starts after 3 turns
MD 2208 (2017-06-07)
FF starts at turn 1, FB starts after 3 turns
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches
turns when FB starts

## Slide 12: Simulation vs Measurement
Simulation:
No FF, FB starts after 3 turns
MD 2208 (2017-06-07)
FF starts at turn 1, FB starts after 3 turns
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches

## Slide 13
Simulation vs Measurement
Simulation:
No FF, FB starts after 3 turns
MD 2208 (2017-06-07)
FF starts at turn 1, FB starts after 3 turns
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches
Maximum amplitude relative to maximum amplitude at injection

## Slide 14
Simulation vs Measurement
MD 2208 (2017-06-07)
FF starts at turn 1, FB starts after 3 turns
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches
Simulation:
No FF, FB starts after 3 turns

## Slide 15
Simulation vs Measurement
No FF,
FB starts after 3 turns
MD 2208 (2017-06-07)
FF starts at turn 1, FB starts after 3 turns
V200 = 4.5 MV, V800 = 0.45 MV
Intensity per bunch ~ 1.13e11, 72 bunches

## Slide 16
Simulation vs Measurement
FF starts at turn 1,
FB starts after 3 turns
No FF,
FB starts after 3 turns

## Slide 17: Next steps: simulation
Summary:
Shape of simulated losses agrees well: increased losses up to ~ bunch 30, ‘dip’ at ~ bunch 45
Reasonable agreement at nominal intensity (1.15e11 ppb)
At high intensity: - measured losses have ‘offset’ of about 15 percent compared to simulation
- measured losses show increase of ~15% along batch, but simulations only give ~6%
Next steps
Use optimized PS bunches
Include FF impedance reduction factor in simulations
Implement method to compute losses in the same way as is used in measurements
Compute phase of simulated induced voltage
Currently, action of feedback in simulation independent of beam properties => implement dynamic feedback in simulation code BLonD

## Slide 18: Next steps: measurement
Summary:
Shape of simulated losses agrees well: increased losses up to ~ bunch 30, ‘dip’ at ~ bunch 45
Reasonable agreement at nominal intensity (1.15e11 ppb)
At high intensity: - measured losses have ‘offset’ of about 15 percent compared to simulation
- measured losses show increase of ~15% along batch, but simulations only give ~6%
Next steps
More systematic studies with FF/FB on/off (as was done this week 2017-06-13)
Influence of phase loop
Measure at higher intensities
Study losses with small ramp or ‘cleaning with longitudinal kicker’
Thank you for your attention!

## Slide 19: Summary and outlook
Summary:
Shape of simulated losses agrees well: increased losses up to ~ bunch 30, ‘dip’ at ~ bunch 45
But: - measured losses have ‘offset’ of about 15 percent compared to simulation
- simulated losses don’t show ‘dip’ for first bunches
Outlook:
Use optimized simulated bunches from the PS instead of Gaussian ones
Currently, action of feedback in simulation independent of beam properties => implement dynamic feedback in simulation code BLonD