## Slide 1: Instability mode studies s 16th of November 2017
J. Repond
Acknowledgements: E. Shaposhnikova, T. Bohl, A. Lasheen, M. Schwarz, G. Papotti, H. Bartosik, OP crew.
LIU-SPS Beam Dynamics Working Group

## Slide 2: 630 MHz HOM and stability threshold
The 630 MHz HOM has the lowest stability threshold for upgraded RF (10 MV) but for 7 MV it is «in competition» with vacuum flanges
Coupled-bunch instability caused by 630 MHz HOM has typical wake decay time of ~ 4 bunches
Threshold minimal on flat top
Can we identify instability source in measurements?
What has been presented until now
Stability threshold
450 GeV, 72 bunches, 7 MV + 0.7 MV
Old simulations with probably obsolete impedance model, new simulations still running
Courtesy: A. Lasheen

## Slide 3: Latest MD results – instability at flat top
Q20 nominal acceleration cycle, on 8th of November 2017
BCMS beam (48 bunches)
FB, LD, blow-up on
Intensity ~ RF program ~ nominal, 800 MHz at 15%
Acquisition of ~ 20 points per synchrotron period on flat top
Beam unstable after arrival at flat top
Controlled emittance blow-up
Evolution of the bunch length
Parameters

## Slide 4: Measurement of profile oscillations
One acquisition every 9 turns

## Slide 5: Bunch oscillations and instability mode(s)
 Most likely rigide dipole oscillations and quadrupole
Profiles superimposed
Contour plot bunch 34

## Slide 6: CBI modes and frequencies – estimation
The growth rate depends on a form factor
 For given (630 MHz) and (1.7 ns), the main mode that will grow can be predicted
For a given bunch length (1.7 ns) and resonant frequency, m for maximum growth rate can be estimated
m | 1 | 2 | 2.3 | 3 | 4
fr [MHz] | 340 | 565 | 630 | 790 | 1000
On flat top, 630 MHz HOM excites dipole and quadrupole oscillations
Courtesy: E. Shaposhnikova
For a given bunch distribution

## Slide 7: Dipole/quadrupole oscillations on flat top – measurements
~ 270 Hz
~ 543 Hz
ns
Synchrotron frequency
Dipole and quadrupole excited
 Higher order mode?
Fourier transform of bunch length and position
~ 515 Hz
~ 545 Hz

## Slide 8: Tomography on flat top
Special thanks to A. Lasheen

## Slide 9: Simulations on flat top
~ 270 Hz
~ 490 Hz
Modes of oscillations similar to measured one: dipole and quadrupole excited
Matched bunches (1.65 ns), 200 ms evolution , full impedance model, ppb
Peak at for bunch length oscillations not observed in measurements, probably due to effect of phase loop
~ 540 Hz

## Slide 10: Conclusion and future work
Complicated to distinguish the source of the instability
  Intensity thresholds of 630 MHz HOM and vacuum flanges close to each other
  Bunch length reduction during acceleration excites different harmonics
Theory predicts for the 630 MHz growth of dipole and quadrupole
  Both modes observed
  Rigide dipole seems to be the leading oscillation
Frequencies of the oscillations are in a good agreement between measurement and simulations
Instability very likely to be caused by the 630 MHz HOM
Future
  Measurements should be carried out without controlled emittance blow-up
  Simulations with realistic bunch shape are required + ramp
  Phase shift between oscillations of each bunch will give the coupled-bunch mode excited

## Slide 11
Thank you for your attention

## Slide 12: Backup slides