## Slide 1: Future instability thresholds in simulations with beam loading limitation s 17th of August 2017
J. Repond
Acknowledgement: E. Shaposhnikova

## Slide 2: Instability threshold – Previous results
FT simulations: 72b, 25 ns spacing, 2RF: 10MV at 200 MHz, 1MV at 800 MHz
 Voltage constant with intensity.
 In reality beam loading reduces the available voltage.
 Less voltage for high intensity.
RFU = RF upgrade

## Slide 3: SPS 200 MHz RF system – Power limitation
Limited power available:
  if no acceleration and zero , L = cavity length, .
Below ppb: V > 10 MV, above: V < 10 MV.
 Instability threshold flatter.
 Larger bunch length will not be as stable as predicted previously.
ppb
4 sections: 1.6 MW
3 sections: 1.0 MW
After RF upgrade

## Slide 4: Simulations scenarios – Post-LS2
Impedance:
  QF flange in SSS will be shielded with RF fingers.
  HOM damping by factor 1.6 is feasible, factor 3 initial baseline.
    Latest results (today): factor 3.3 feasible
  Effect of QD shielding simulated but negligible.
Effect of 800 MHz voltage increase simulated (10% of if not specified).
Different number of bunches considered (48, 72, 80).
Two different time: 0.5s FT (operation) and 2s (threshold).

## Slide 5: 72b power limitation – HOMs damping, QF shielding
Running average on threshold. No fit in : voltage varies for each intensity.
Observations:
  Threshold flatter at high intensity.
  QF shield stabilizing for small bunch length (high freq. impedance > 1.4 GHz).
  HOMs and QF threshold close to each other.
    Their impedance must be reduced together.
  Stable HL-LHC proton batch for nominal FT (0.5s) if HOM/3 + QF shield.
    Feasible according to last results.
0.5s
2s

## Slide 6: 72b power limitation – Effect of HOMs damping
Damping of the HOMs until a factor 4 increases the instability threshold.
0.5s
2s

## Slide 7: 72b power limitation – HOM/1.6 + shield
0.5s
2s
HOM/1.6 + QF shield barely sufficient for the stability of the HL-LHC proton batch with bunch length discrepancy around 1.65 ns.

## Slide 8: 72b power limitation – HOM/3 + shield
0.5s
2s
Stable HL-LHC proton batch with in bunch length around 1.65 ns for 0.5s FT, HOM/3 + QF shield.

## Slide 9: 80b power limitation – HOMs damping, QF shielding
0.5s
2s
A batch of 80 bunches could be used to increase the luminosity in the LHC.
Threshold similar to 72 bunches.

## Slide 10: 80b power limitation – comparison with 72b
2s, 80b
2s, 72b
Instability threshold very similar between 72 and 80 bunches.

## Slide 11: 80b power limitation – 800 MHz voltage increase
2s, 80b
10% increase in stability threshold using 15% instead of 10% of . Realistic value for future operation.

## Slide 12: 48b power limitation – HOMs damping, QF shielding
Instability threshold for BCMS beam.
0.5s
2s

## Slide 13: 48b power limitation – comparison with 72b
Only a few percent in intensity threshold between 72 and 48 bunches.
2s, 48b
2s, 72b

## Slide 14: Conclusion and future work
Taking into account power limitation flattens the threshold.
  Zero voltage above ppb.
  V < 10 MV for intensities larger than ppb.
Instability threshold due to HOMs or QF impedance close.
   Damping of HOMs AND shielding of QF necessary.
Instability threshold for 48/72/80 bunches close to each other (few %).
  Negligible gain in stability threshold using BCMS beam.
Damping of HOMs by a factor 3 + QF shield insure the stability of the HL-LHC proton beam for the 0.5 s flat top.
More ongoing simulations:
  Fixed (1MV, 1.5MV)
  Multibatch

## Slide 15
Thank you for your attention.

## Slide 16: Backup slides