## Slide 1: 200MHz cavities HOM impact on transverse stability
D.Amorim
Thanks to N.Biancacci, K.Li, E.Métral, B.Salvant
LIU-SPS beam dynamic WG meeting
02/03/2017

## Slide 2: Outline
Introduction
Stability simulations results for the SPS impedance model in presence of a transverse resonator
Sensitivity to the resonator parameters
Conclusion and next steps

## Slide 3: Outline
Introduction
Stability simulations results for the SPS impedance model in presence of a transverse resonator
Sensitivity to the resonator parameters
Conclusion and next steps

## Slide 4: Introduction
Need to reduce the 620MHz longitudinal HOM
Doing so might modify the 940MHz transverse HOM
We want to assess the transverse stability margin if this mode grows when optimizing the 620MHz HOM
Method: stability simulations and analytical considerations on the sensitivity to resonator parameters

## Slide 5: Outline
Introduction
Stability simulations results for the SPS impedance model in presence of a transverse resonator
Sensitivity to the resonator parameters
Conclusion and next steps

## Slide 6: Stability simulations parameters
SPS impedance model (without 200MHz cavities) + transverse resonator
Resonator parameters
  , Q=1000 (E. Shaposhnikova, SL-Note 96-49 RF)
  Scan in shunt impedance:
Growth rates obtained with DELPHI
  Vertical plane
  924 bunches (25ns spacing)
  Single bunch intensity
  Zero chromaticity, no damper (conservative parameters)
Notes: Put Delphi params in appendix

## Slide 7: Stability simulations parameters
Impedance model (without 200MHz cavities) + Resonator
Resonator parameters
  , Q=1000
  Scan in shunt impedance:
Growth rates obtained with DELPHI
  Single bunch intensity
  924 bunches (25ns spacing)
  Zero chromaticity, no damper
Re(Z)
Im(Z)
Impedance model without resonator

## Slide 8: Stability simulations parameters
Impedance model (without 200MHz cavities) + Resonator
Resonator parameters
  , Q=1000
  Scan in shunt impedance:
Growth rates obtained with DELPHI
  Single bunch intensity
  924 bunches (25ns spacing)
  Zero chromaticity, no damper
Q=1000
Re(Z)
Im(Z)
Notes: Redo plot with Re on front

## Slide 9: Stability simulations results
For and Q=1000 the effect of the resonator starts to be seen at

## Slide 10: Outline
Introduction
Stability simulations results for the SPS impedance model in presence of a transverse resonator
Sensitivity to the resonator parameters
Conclusion and next steps

## Slide 11: Sacherer formula
Sacherer formula allows for an approximate calculation of rise time and frequency shift:
  With the effective impedance
  is the power spectrum
The growth rate (in s-1) is proportional to the real part of the transverse impedance
Notes: Explain h
Put the resonator impedance picture

## Slide 12: Sacherer formula
Sacherer formula allows for an approximate calculation of rise time and frequency shift:
  With the effective impedance
  is the power spectrum
The growth rate (in s-1) is proportional to the real part of the transverse impedance
Negative frequencies increase the growth rate (instability)
Positive frequencies decrease the growth rate (damping)
A.W. Chao
Notes: Explain h
Put the resonator impedance picture

## Slide 13: Sacherer formula
The impedance is sampled every
M: Number of bunches
Coupled bunch mode number:
Revolution frequency
Notes: Explain h

## Slide 14: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 15: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 16: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 17: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 18: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 19: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 20: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 21: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 22: Sacherer formula
The impedance is sampled every
Notes: Explain h

## Slide 23: Sacherer formula
The impedance is sampled every
Each couple of lines (negative and positive) is spaced by (16KHz in this case)
Notes: Explain h

## Slide 24: Resonator bandwidth > revolution frequency
Here , multiple coupled bunch lines are covered by the resonance
Resonator impedance (line)
Coupled bunches modes lines (dots)
Resonator bandwidth
Positive and negative lines almost compensate

## Slide 25
Here , two coupled bunch lines are covered by the resonance and have almost the same amplitude
Resonator impedance (line)
Coupled bunches modes lines (dots)
Resonator bandwidth
Resonator bandwidth < revolution frequency
Notes: Here: compenstae

## Slide 26
Here one coupled bunch line falls on top of the resonance
Resonator impedance (line)
Coupled bunches modes lines (dots)
Resonator bandwidth
The resonance frequency is shifted by
Resonator bandwidth < revolution frequency
Notes: Here: no compendsation

## Slide 27: Summary of the two cases
Depending on the resonator bandwidth
  If the resonance covers multiple coupled bunch lines
    Most of the growth rate given by the negative lines is compensated by the damping provided by the positive lines
  If the resonance can:
    Cover two lines, both having the same amplitude: the growth rate is compensated by the damping
    Cover two lines, one having a larger amplitude: the growth rate can become much larger than the damping: an instability may rise

## Slide 28: Conclusion
First studies show (for , ) no impact until
Qualitative analysis show that () shouldn’t impact transverse stability
But higher ( , ) might drive an instability, with a sensibility on the resonance frequency
Next steps
Check the corresponding single bunch stability margins (effect of )
Run the simulations for 4620 bunches (5ns)
  Increased total intensity should lead to higher growth rates
  Same qualitative behavior w.r.t. Q expected as line spacing is
Study in more detail the coupled-bunch instability as a function of resonator parameters
Implement realistic HOM with values from impedance simulations

## Slide 29: References
E. Shaposhnikova, Resonant impedances in the SPS, SL-Note 96-49 RF
N. Biancacci, Impact of transverse HOM on beam stability in the HL-LHC, 10/12/2014
R.J. Lauckner and T.P.R Linnecar, The transverse coupled bunch mode instability at 940MHz in the SPS, 03/09/1980
K.Y.Ng, Coupling Impedances and Beam Instabilities in Accelerator Rings, 2015

## Slide 30: Stability simulations results
Growth rate linear with beam intensity, shunt impedance threshold is not changed
Nb=1e11 Baseline value: 2600 s-1
Nb=2e11 Baseline value: 5000 s-1
Notes: Put reso param

## Slide 31: Stability simulations results
For (, Q=10000) the effect of the resonator starts to be seen at
Nb=1e11 Baseline value: 2600 s-1
Nb=2e11 Baseline value: 5000 s-1

## Slide 32: Theory considerations
Resonator impedance (line)
Coupled bunches modes lines (dots)
Resonator bandwidth