## Slide 1: LIU-SPS MDs 2017

## Slide 2: LIU-SPS related MD subjects (I)
Further characterization and minimization of losses (to define mitigation strategy)
  Study effects of LLRF systems on losses
  PS-to-SPS transfer studies (bunch rotation optimization)
  Studies in view of exotic options (RF capture system in SPS, …)
  (8b4e studies for LLRF specifications to improve beam loading compensation)
Q22 optics
  Commissioning of MD cycles including transverse damper!
  Instabilities (TMCI threshold, longitudinal instabilities in comparison to Q20, …)*
  Losses at start of acceleration (more efficient use of available RF power?)
  Maximum intensity reach with 25 ns beam and present RF*
  Studies of incoherent effects … any showstoppers?
Longitudinal impedance, instabilities and intensity limitations
  Check calibration of 800 MHz cavity voltage with beam
  Single bunch vs. coupled bunch instability thresholds and impedance identification*
  Extraction of longer bunches to LHC (for LIU beam parameter reach)**
  Further explore intensity limit for 25 ns beam with present RF*
  Bunch rotation at 450 GeV for high intensity 25 ns beams*
  Check impact of soft clamps (i.e. after removing them during TS1)
  Longitudinal space charge at different energies*
* Requires dedicated MD
** Requires MD in LHC

## Slide 3: LIU-SPS related MD subjects (II)
Transverse coupled bunch instabilities and usage of octupoles
  Coupled bunch instability studies for benchmarking existing SPS impedance model
  Impact of octupoles (is mainly amplitude detuning or Q’’ the stabilizing mechanism?)
  Study effect of Q’’ on single bunch mode 0 negative chromaticity instability (using LOE extraction octupoles to cancel amplitude detuning)
Transverse damper and high-bandwidth feedback
  Further optimization and improvements for LHC beams including high intensity (high bandwidth, sensitivity to tunes, horizontal coupled bunch instability with high intensity 25 ns beam)
  Continuation of high-bandwidth transverse feedback studies
  TMCI in presence of transverse damper
Electron cloud and high intensity: few days of dedicated floating MD in September (“mini scrubbing run”)*
  Impact of transverse emittance on beam stability and losses (BCMS vs. standard)
  Studies on beam stability and lifetime with full bunch train
  Pressure rise in aC-coated sector
  Comparison of different optics configurations in terms of losses and beam stability
  Tests with prototype wire scanner prototype with high intensity
  Benchmarking of losses with simulation models
  Losses for different beam types to isolate effects of RF capture from e-cloud
* Requires dedicated MD

## Slide 4: LIU-SPS related MD subjects (III)
Space charge and non-linear model (also in view of ions)
  Difference with de-Gaussing of nonlinear elements?
  Losses and emittance blow-up close to resonances in view of ions (benchmark experiments), resonance compensation
Studies in view of collimation system
  Benchmarking of loss location with and without present momentum scraper (in parallel to other MDs with 25 ns beams)
  Closed orbit stability along the run
Miscellaneous
  Commissioning of new wire scanner prototype
  Commissioning of BSRT, DOROS BPM electronics and diamond BLMs in LSS4/LSS6

## Slide 5: Planning
Dedicated MDs:
23 blocks of 10h
about 10 for LIU (which ones?)
?
mini scrubbing run here? (moving blocks from startup)

## Slide 6
Thank you for your attention!