## Slide 1: Update on loss studies
Acknowledgements:
A. Lasheen, J. Repond, E. Shaposhnikova, H. Bartosik, V. Kain, T. Bohl, G. Papotti,
H. Timko, P. Baudrenghien, P. Kramer, I. Karpov
SPS & PS operator team, BLonD dev team
M. Schwarz

## Slide 2: Outline
Review of previous results
Simulations with
  Different bunch distributions
  Phase loop
  Modulated intensity and bunch length
  High intensity for present and future setup
First results of simulations with dynamic one-turn delay feedback

## Slide 3
Measured and simulated losses: previous results
72 bunches (25ns spacing) and Q22 in both measurement and simulation
Measured and simulated intensity obtained by integrating profile +/-0.575 RF-buckets around bunch peak
Example with highest intensity (1.7e11ppb) in measurements and low V200 voltage (2.0MV)
Simulation
Measurement
Shape and time scale agree very well!
Simulated losses to high compared to measurements: phase loop not included

## Slide 4
Simulation parameters
Use different bunch distributions simulated in the PS (courtesy of A. Lasheen)
  Out of the 4M macro-particles, randomly select 1M macro-particles for tracking in the SPS for each of the 72 bunches
  Place bunches at center of bare RF-bucket
Use ‘impedance reduction’ to model one-turn delay feedback of 200 MHz TWC
Phase loop gain: 5e3 1/s; Radial loop gain: 5e9; PL averages over 12 bunches (hard edge)
Bunch parameters
Same methods used to analyze measured and simulated bunch profiles
Bunch intensity obtained by integrating profile +/-0.575 RF-buckets around bunch peak
Bunch length obtained from FWHM and converted to
Bunch position relative to bare RF-bucket spaced 25ns apart (1st bunch assumed to be at center of RF-bucket)
Bunch loss
Measurement setup
MD 17/11/14
72 bunches, Q22 optic
Vary intensity (here only show 1.7e11 ppb) and V200 (from 2.0 MV up to 6.0 MV)
FF on/off (here only FF off)

## Slide 5
Use different bunch distributions simulated in the PS (courtesy of A. Lasheen)
  Out of the 4M macro-particles, randomly select 1M macro-particles for tracking in the SPS for each of the 72 bunches
  Place bunches at center of bare RF-bucket
  Use ‘impedance reduction’ method to simulate SPS one-turn delay feedback
Full SPS impedance model
Simulated particle distributions used
Distribution 2
Distribution 1
Distribution 3

## Slide 6
Simulated bunch intensity, no beam loading
0 bunch intensity -> losses due to overlap of bunch distribution with RF-bucket
V200 = 3.5 MV
V200 = 2.0 MV
0% losses
< 1% losses
~ 1% losses
0% losses
~ 0% losses
< 1% losses
Distribution 2
Distribution 1
Distribution 3

## Slide 7
Simulations phase loop
1.7e11 ppb; V200=2.0MV; distribution 2

## Slide 8
Simulations with different distributions vs measurements
Measurement
With phase loop, simulated and measured losses also in quantitative agreement
But notice modulation of losses in measurements (every 4th bunch = 10 MHz)
Distribution 2
Distribution 3
1.7e11 ppb; V200=2.0MV

## Slide 9
Investigate 10 MHz modulation
Both initial bunch length and intensity modulated with 10 MHz
To model this effect in simulations:
  Modulate bunch intensity (# of macro-particles) with pattern [0.9, 0.97, 1.03, 1.1] every four bunches
  Modulate bunch length by choosing distributions with 4σFWHM [4.25ns, 4.17ns, 4.09ns, 3.97ns]

## Slide 10
Simulations with different distributions vs measurements
Measurement
Modulation of bunch length leads to stronger loss modulation compared to intensity modulation
When modulating bunch lengths, losses decrease for last bunches!?
Modulation of bunch intensity
(distribution 3)
Modulation of bunch length
(based on distribution 2)
1.7e11 ppb; V200=2.0MV

## Slide 11
Correlations with losses
Loss after 1s correlated with injected bunch length, but no correlation with injected intensity
Bunch positions change -> reproduced in simulations?

## Slide 12
Simulated losses for high intensity
present
Simulation parameters present:
  72 bunches, 2.6e11 ppb
  V200 = 3.5 MV
  Feedback strength at -15 dB reduction
  Phase loop averages over 12 bunches
  Two 5-section and two 4-section cavities
  Present SPS impedance model
Simulation parameters future:
  72 bunches, 2.6e11 ppb
  V200 = 3.5 MV
  Feedback strength at -26 dB reduction
  Phase loop averages over all bunches
  Two 4-section and four 3-section cavities
  Future SPS impedance model
18/02/12
future

## Slide 13
Motivation:
Previously, SPS OTFB modeled by ‘impedance reduction’, i.e. no dynamic implementation
Dynamic OTFB developed for BLonD (H. Timko)
Here, present first comparisons with measurements
Measurements:
48 bunches, 1.48e11 ppb
V200 = 4.5 MV, Q22 optic
Simulation parameters:
48 bunches, 1M macro-particles per bunch
V200 = 4.5 MV, Q22 optic
Present full SPS impedance model
Present ‘best settings’ (G_LLRF_4 = 8.0, G_LLRF_5 = 10.0)
Results:
Induced voltage in short TWC ‘undershoots’ around turn 10; asymptotic behavior represented well
For long TWC, OTFB does not reduce induced voltage enough!?
First results with dynamic OTFB

## Slide 14
With inclusion of phase loop, simulated losses are also in quantitative agreement with measurements
Started to investigate influence of different initial distributions on losses
Assuming future parameters (improved PL, OTFB, SPS impedance), simulations for high intensity yield losses below 2% after 1s
First results of dynamic OTFB show good results for 4-section cavity, but not for 5-section cavity
Summary
Thank you for your attention!
More 1s long simulations for different cases to study losses after 1s
  Why losses for last bunches in simulations sometimes smaller?
  Bunch positions
Further work on dynamic OTFB
Next steps

## Slide 15: Appendix

## Slide 16
MD 17/11/14: 1.7e11 ppb bunch-by-bunch losses

## Slide 17
FFT bunch-by-bunch losses -> 10 MHz modulation

## Slide 18
MD 17/11/14: 1.7e11 ppb FFT of relative 4σFWHM

## Slide 19
MD 17/11/14: 1.7e11 ppb FFT of relative bunch intensity

## Slide 20
MD 17/11/14: 1.7e11 ppb FFT of relative bunch intensity

## Slide 21
MD 17/11/14: 1.7e11 ppb loss@1s VS injection bunch length

## Slide 22
MD 17/11/14: 1.7e11 ppb loss@1s VS injection bunch intensity