## Slide 1
Nasrin Esfahani
Evaluating the new couplers based on measurements on 4-section cavities in the SPS tunnel

## Slide 2
Overview
Measurement Considerations
Measurement results
Examining effect of the new coupler on both Q and R/Q
Conclusions

## Slide 3: Problems of simultaneous evaluation of new & old couplers
This example clarifies the situation:
When an un-damped mode is surrounded by two damped modes which are very close to each other , the effect of damping the un-damped one on S21 is very small.
This is the situation which we have in case of the 4-section SPS TWC cavities from 629-630 MHz.
Freq | 629.15 | 629.22 | 629.5 | 629.92
Q | Damped | High Q | Completely Damped with old couplers | Damped
R/Q | Large(400) | Moderate (40) | Small | Large (300)
Effect of new couplers | Drastic reduction in R/Q Reduction in Q | Drastic reduction in Q R/Q unchanged | No further damping is needed | Reduction in both Q and R/Q

## Slide 4: Tunnel Measurements on Cavity 2 (Feedback loops)
S1F5S4F10
S1F6S4F10
S1F4S4F10
3 modes in the 629-630 MHz are damped by the new couplers

## Slide 5: Tunnel Measurements on Cavity 2 (New HOM couplers)
First & Last new HOM
Freq | 629.15 | 629.22 | 629.5 | 629.92
Q | Damped | High Q | Completely Damped with old couplers | Damped
R/Q | Large(400) | Moderate (40) | Small | Large (300)
Effect of new couplers | Drastic reduction in R/Q Reduction in Q | Drastic reduction in Q R/Q unchanged | No further damping is needed | Reduction in both Q and R/Q

## Slide 6
2 & 4 new HOM
Freq | 629.15 | 629.22 | 629.5 | 629.92
Q | Damped | High Q | Completely Damped with old couplers | Damped
R/Q | Large(400) | Moderate (40) | Small | Large (300)
Effect of new couplers | Drastic reduction in R/Q Reduction in Q | Drastic reduction in Q R/Q unchanged | No further damping is needed | Reduction in both Q and R/Q

## Slide 7: Fundamental passband
No effect on the fundamental passband

## Slide 8: Conclusions
Measurement using the feedback loops as input and output show that the new couplers effectively damp the mode in 929 MHz-930MHz region
Measurements using the new couplers as input and output show that both Q and R/Q are reduced using the new couplers
New couplers have no negative effect on the fundamental passband

## Slide 9: Thank you!