## Slide 1: Online bunch length measurement for SPS OP
G. Papotti (RF-BR), F. Follin (OP-SPS)
acks: T. Bohl (RF-BR), M. Jaussi (RF-CS)
LIU SPS-BD WG, 2018-11-20

## Slide 2: introduction
from LIU SPS-BD WG on 2017-12-14:
  H. Bartosik: “The most important is to be able to measure the bunch length bunch by bunch along the batch.”
  correction from 2018-11-15: add “along the cycle”
ideas:
  reuse hardware installed for OP in CCR
  reuse SPS BQM algorithms
  get the new system done during the YETS
operational as of April 2018
  bbb bunch length measurement along the cycle available in the CCC

## Slide 3: outline
design ideas
hardware
FESA class
many GUI screenshots
future developments

## Slide 4: main design ideas
OP mode (main functionality)
  one measurement of one turn, every x ms
    data analysis and transfer at every acquisition
  x: typ 200 ms; HB 20 ms
    20 ms clamped by GUI; maybe somewhat faster is feasible
  logged in Timber (extract without fundamental filter!)
MD mode
  one measurement of many turns, once in the cycle, one transfer per cycle
GUI to orchestrate all settings and their coherence
  LTIMs, number of acquisitions in FESA, VTU settings, …
stored in LSA
  GuruSettings, with proper value generators
  non-PPM Calibration Factors, derived wrt BQM SPS

## Slide 5: hardware
Acqiris card installed since years in CCR for OP long. observations
  not much used recently
  removed it from Oasis database on 18-19 Dec 2017
wrote dedicated FESA class
later moved to BA3 Faraday Cage, seized CCC PicoScope signal
  a better signal than to the CCR
  signal amplitude remains at the limit for p+ probes and ions

## Slide 6: FESA class
“ABWLM”: A for RF, Beam, Wideband, Longitudinal, Measurement
  keep it simple: call it “Bunch length measurement”, like the GUI in the CCM
RTAs:
  prepare first acquisition, at start of cycle
  retrieve data, analyse, prepare for next acquisition if necessary
publish results in 2 separate properties
  latest acquisition only (used for logging)
  aggregate all results once per cycle (used by GUI)

## Slide 7: GUI
user selection
config settings and readout
PPM attenuator
suggestion: stop acquisition for changing settings
console messages
choice of view for results

## Slide 8: GUI: Trends display
bunch number and pattern
bunch length
  min-mean-max
bunch intensity [a.u.]
  min-mean-max
bbb peak available but not displayed by GUI

## Slide 9: GUI: Snapshot display
RT evolution of bunch length and intensity
  particularly appreciated during many MDs
can use Time Selection slider to replay evolution
GUI also reconstructs pattern
  used also for wire scanners setup

## Slide 10: GUI: Bunch Wave display
RT bunch profile display
  can select one bunch at a time (stop acquisition first)
useful to check if acquisition saturates
  if saturation: no results

## Slide 11: GUI: MD mode
e.g. AWK bunch rotation setup
suggestion: always cross-check the settings sent (JavaFX!)
apologies
for the ugly screenshots!

## Slide 12: measurement in coast
suggestion: set one measurement every 500-1000 ms

## Slide 13: work ahead
hardware:
  during LS2: fibre optics transmission
  sometime after restart: change ADC
software: include tomography for the SPS
  some work started by S. Albright, discussions ongoing across machines
    every machine wants a tomoscope!
    support common efforts
  ABWLM+GUI the perfect user for such common tomo-code
    piggyback on C++ code development, perfect synergy
    ready to use MD mode of acquisition
    GUI smart way to get LSA settings
Notes: from LSA: voltage program and harmonic, energy
from user: phase,