## Slide 1: Losses at flat-bottom
Acknowledgements:
A. Lasheen, J. Repond, E. Shaposhnikova, H. Bartosik, V. Kain, T. Bohl, H. Timko,G. Papotti,
P. Baudrenghien, P. Kramer, I. Karpov
SPS & PS operator team, BLonD dev team
M. Schwarz

## Slide 2
Motivation
Instability of simulated losses with radial loop
Comparison between measurements and simulation with frequency loop
Simulations for 2.6e11 particles per bunch
Content

## Slide 3
Losses at injection, possible sources:
  Longitudinal effects (bunch shape from PS, uncaptured PS beam,…)
  SPS LLRF system
Losses at SPS flat-bottom, possible sources:
  Momentum aperture and transverse emittance
  Full bucket (intensity effects, noise from LLRF)
Sources of losses in the SPS
Simulated PS bunch in SPS RF-bucket (courtesy of A. Lasheen)

## Slide 4
Simulation parameters
Use different bunch distributions simulated in the PS (courtesy of A. Lasheen)
  Out of the 4M macro-particles, randomly select 1M macro-particles for tracking in the SPS for each of the 72 bunches; ‘seed’ parameter determines which macro-particles are used for tracking; average simulation results for different seeds
  Place bunches at center of bare RF-bucket
Use ‘impedance reduction’ to model one-turn delay feedback of 200 MHz TWC
V800 = 0 MV
Phase loop gain: 5e3 1/s; PL averages over 12 bunches (hard edge)
  Radial loop gain: 5e9
  Frequency loop gain: 0.09
Either with full SPS impedance or with just 200 MHz TWC impedance
Initial intensity per bunch: 1.7e11 (both measurement and simulation)
Simulation parameters
  number of bins / RF-bucket (64, 128, or 256)
  Frequency resolution (df= 4 f_rev)
  Six different seeds for initial distribution
  Number of macro-particles: 1M
Calculate intensity of bunches after 1s (~43k turns) and calculate loss relative to initial intensity
Distribution 2
Distribution 3

## Slide 5
LLRF loops
Phase loop: displaces RF, such that beam phase equals synchronous phase; damps dipole oscillations
Radial loop: adjust RF to keep beam orbit centered
no beam loading
beam loading
Frequency loop: adjust RF to design frequency
~# macroparticles -> numerically expensive

## Slide 6
Instability with radial loop
Seed 0
Seed 1980
Tiny variation in initial distribution leads to five times more losses
Notice different
intensity scales!
Seed 0
Seed 1980

## Slide 7
Average bunch length and beam energy
Up to ~400ms nearly identical behavior;
Seed 0
Seed 0
Seed 1980
Seed 1980

## Slide 8
Seed 0
Seed 1980
Instability with radial loop: phase space animation of 1st bunch
For seed ‘1980’, bunch center starts to oscillate at ~400ms
For seed ‘1980’, ‘sub-bunch’ develops into a ‘ring’ around main core
Changing numerical simulation parameters (# bins, frequency resolution) does not improve stability

## Slide 9
Using frequency loop
Results independent of:
  numerical simulation parameters
  initial seed
Simulation factor 2 faster than with radial loop
-> use frequency loop in the following
SPS uses synchro-loop for protons instead of radial loop
Sensitivity of simulations with radial loop not completely understood
  Possible reason: both phase and radial loop depend directly on beam parameters (phase and energy); frequency loop only looks for changes in RF-frequency

## Slide 10
Simulation parameters
Use different bunch distributions simulated in the PS (courtesy of A. Lasheen)
  Out of the 4M macro-particles, randomly select 1M macro-particles for tracking in the SPS for each of the 72 bunches; ‘seed’ parameter determines which macro-particles are used for tracking; average simulation results for different seeds
  Place bunches at center of bare RF-bucket
Use ‘impedance reduction’ to model one-turn delay feedback of 200 MHz TWC
V800 = 0 MV
Phase loop gain: 5e3 1/s; PL averages over 12 bunches (hard edge)
  Frequency loop gain: 0.09
Either with full SPS impedance or with just 200 MHz TWC impedance
Initial intensity per bunch: 1.7e11 (both measurement and simulation)
Simulation parameters
  64 number of bins / RF-bucket
  Frequency resolution: df= 4 f_rev
  Six different seeds for initial distribution
  Number of macro-particles: 1.5M
Distribution 2
Distribution 3
Measurement setup
72 bunches, 1.7e11 ppb, 25ns bunch spacing
Q22 optics
V800 = 0 MV

## Slide 11
Simulation vs measurement: V200 scan
distribution 2 frequency loop
distribution 3 frequency loop
Smaller simulated losses for distribution with less tails
Slightly more losses when including full SPS impedance in simulations
Agreement between measurement and simulation for small V200, where beam loading is more prominent
For large tails, simulated losses still below measured losses
  due to on-set off flat-bottom losses (like momentum aperture limitation), which are not present in simulation?

## Slide 12
Simulation vs measurement: bunch-by-bunch loss pattern
Over all, good qualitative and quantitative agreement, but
  Measured 10 MHz modulation (every 4th bunch) not reproduced here, because no initial bunch modulation (see presentation https://indico.cern.ch/event/705636/)
  ‘bump’ for bunches 40 to 50 not as pronounced in measurement
  Up to 10ms, simulated losses larger by about 1%
V200 = 2.0 MV
Distribution 3

## Slide 13
Simulation vs measurement: bunch-by-bunch loss pattern
For high V200, measured and simulated loss patterns become more ‘flat’
  less influence of beam loading for higher V200
For high V200, simulated losses below measured ones
  Mechanism of flat-bottom losses not implemented in simulation
distribution 2 2.0 MV
distribution 2 3.5 MV
distribution 2 5.5 MV
distribution 3 2.0 MV
distribution 3 3.5 MV
distribution 3 5.5 MV

## Slide 14
Bunch length, distribution 3, frequency loop, V200 scan
Nice agreement for higher voltages and simulations
For V200=2.0, simulated bunch lengths larger at end of batch
V200 = 2.0 MV

## Slide 15
Bunch position, distribution 3, frequency loop, V200 scan
Bunch position relative to ideal RF-bucket
Adjust mean of simulated bunch position to mean of measured bunch position
Within errors, perfect agreement 
V200 = 2.0 MV

## Slide 16
Simulated losses for high intensity, 2.6e11 ppb
present
Simulation parameters present:
  72 bunches, 2.6e11 ppb
  V200 = 3.5 MV
  Feedback strength at -15 dB reduction
  Phase loop averages over 12 bunches
  Two 5-section and two 4-section cavities
  Present SPS impedance model
Simulation parameters future:
  72 bunches, 2.6e11 ppb
  V200 = 3.5 MV
  Feedback strength at -26 dB reduction
  Phase loop averages over all bunches
  Two 4-section and four 3-section cavities
  Future SPS impedance model
future
Losses ~2%

## Slide 17
Summary
Simulations with radial loop up to 1s can very sensitive to tiny variations of initial parameters
Simulations with frequency loop more robust (and faster by factor 2)
Comparing measurements with simulations with frequency loop yield
  good agreement for low V200 where beam loading is more prominent
  systematically lower simulated losses for high V200; either initial distribution not correct, or mechanism for flat-bottom losses (such as momentum aperture) not included in simulations
Thank you for your attention!

## Slide 18: Appendix

## Slide 19
bbb loss pattern, distribution 2, frequency loop, V200 scan
Good qualitative and quantitative agreement for low V200
For high V200, measured and simulated loss patterns become more ‘flat’
For high V200, practically no simulated losses -> all tails captured

## Slide 20
bbb loss pattern, distribution 3, frequency loop, V200 scan
Good qualitative and quantitative agreement for low V200
For high V200, measured and simulated loss patterns become more ‘flat’
For high V200, simulated losses smaller than measured losses -> not enough tails in simulated distribution

## Slide 21
Bunch length, distribution 2, frequency loop, V200 scan
Nice agreement for higher voltages and simulations with full SPS impedance model
For V200=2.0, model with only 200MHz TWC impedance gives better agreement

## Slide 22
Bunch length, distribution 3, frequency loop, V200 scan
Nice agreement for higher voltages and simulations with full SPS impedance model

## Slide 23
Bunch position, distribution 2, frequency loop, V200 scan
Bunch position relative to ideal RF-bucket
Adjust mean of simulated bunch position to mean of measured bunch position
Within errors, perfect agreement 

## Slide 24
Bunch position, distribution 3, frequency loop, V200 scan
Bunch position relative to ideal RF-bucket
Adjust mean of simulated bunch position to mean of measured bunch position
Within errors, perfect agreement 