## Slide 1: Longitudinal instabilities on SPS flat bottom
H. Bartosik, T. Bohl, A. Lasheen, G. Papotti, J. Repond, M. Schwarz, E. Shaposhnikova SPS & PS operators
LIU-SPS BD WG meeting 18/09/25

## Slide 2: Outline
Measurement of instability threshold
Instability for different LLRF system settings
First simulation results

## Slide 3
Flat bottom instability
Setup:
MD 11 September 2018: 12 bunches, 25ns spacing, Q20
Intensity variable: protons per bunch 0.8e11 to 1.3e11
Bunch length ( at filamentation): 2.5ns to 2.85ns
FeedBack: off, FeedForward: off, Phase loop: on, long. damper: off
V200 =4.5 MV, V800 off
Consider data at flat bottom up to 19.2 s; then ramp
LIU-SPS BD WG meeting

## Slide 4
Flat bottom instability: threshold
Threshold scales as coupled bunch instability threshold (no fit)

## Slide 5
Flat bottom instability: start of instability
Mild anti-correlation between start of instability and bunch intensity

## Slide 6
Flat bottom instability: loss after ramp
No difference in losses between stable and unstable beams

## Slide 7
High intensity
Setup:
MD 04 September 2018: 2 batches,12 bunches, 25ns spacing, Q20
Intensity: 2.5e11 protons per bunch
FeedBack: on/off, FeedForward: on/off, Phase Loop: on/off, long. damper: on/off
V200 =4.5 MV, V800 off
Consider data at flat bottom up to 11.2 s
LLRF becomes power limited after injection of 2nd batch
Bunch length plots have been smoothed for clarity by moving average (n=20)
LIU-SPS BD WG meeting

## Slide 8
High intensity: FB off, FF off, LD off, PL off
1st batch: last bunches ‘blow up’ after injection, others may become unstable at flat bottom (see next slide)
2nd batch: stable but last bunches have large losses (~50%)
offset by 2ns
offset by 50%
Bunch lengths of 2nd batch shifted by 2ns, and losses by 50% for clarity

## Slide 9
High intensity: FB off, FF off, LD off, PL off
offset by 2ns
offset by 50%
1st batch: last bunches ‘blow up’ after injection, first bunches become unstable at flat bottom
2nd batch: stable but last bunches large losses (~50%)
first bunches become unstable

## Slide 10
High intensity: FB on, FF off, LD off, PL off
Both batches filament and are stable
Biggest contribution to losses at capture (10%)
offset by 2ns
offset by 50%

## Slide 11
High intensity: FB off, FF off, LD off, PL on
1st batch: bunch lengths of all bunches begins to grow 100ms after injection
2nd batch: filaments and stable
offset by 50%

## Slide 12
High intensity: FB on, FF off, LD off, PL on
offset by 2ns
offset by 50%
1st batch is stable and capture losses are ~ 5%
2nd batch stable, but larger bunch length and losses for last bunches

## Slide 13
High intensity: FB on, FF on, LD off, PL on
with FF on, both batches are stable, but higher flat-bottom losses
offset by 2ns
offset by 50%

## Slide 14
High intensity: FB on, FF on, LD on, PL on
With LD on, all bunches become unstable at the same time
offset by 2ns
offset by 50%

## Slide 15
First simulation results
Setup:
12 bunches, 25ns spacing, Q20
Intensity: 2.2e11, 2.4e11, 2.5e11 protons per bunch
FeedBack: off, FeedForward: off, Phase loop: on, long. damper: off
V200 =4.5 MV, V800 off
With these settings, measured bunch length increases within 1s -> simulate 1s (43k turns)
Use full SPS impedance model
Use different bunch distributions simulated in the PS (courtesy of A. Lasheen)
  : 3.5ns, 3.8ns
  Out of the 4M macro-particles, randomly select 2M (3M) macro-particles for tracking in the SPS for each of the 12 bunches; ‘seed’ parameter determines which macro-particles are used for tracking
Place bunches at center of bare RF-bucket
Same data analysis routines as used to analyze measured bunch profiles

## Slide 16
Simulation vs Measurement: bunch length
similar bunch lengths, but simulated bunch length first filaments during first 100ms
simulation
measurement

## Slide 17
Simulation vs Measurement: losses
First bunches have same losses in simulation and measurement, but simulated bunch lengths increase at later time
Simulated losses too large for last bunches
simulation
measurement

## Slide 18
Summary 12 bunches measurements
High intensity (2.5e11 ppb, V800 off)
FB on: stable
  + PL on: stable
  + FF on: stable
  + LD on & 2nd batch: unstable
FB off, FF off, LD of, PL on, V800: off
FB off:
  + PL on: unstable
  + PL off: last bunches unstable
Next steps:
Scan V800 voltage and FB off
Measure instability threshold for 1x24 bunches

## Slide 19
Summary Simulation
Simulations:
  First simulations show agreement between measurement and simulation (but not perfect)
Systematic study with different initial PS bunch distributions
Fix phase loop gain problem (gain threshold to low in simulation)
Simulations of entire flat bottom (19s ~ 800k turns) for nominal intensity and different long. emittance, to compare simulated threshold to measurements
Next steps simulation
Thank you for your attention!

## Slide 20
4x12 bunches, 2e11 ppb at flat top
Smaller bunch length at flat top with Joel’s ‘optimized’ momentum program of 800 MHz cavity
800 MHz cavity at constant 10%
800 MHz cavity optimized during ramp

## Slide 21
Simulation vs Measurement: bunch length
Similar bunch length
simulation
measurement

## Slide 22
Simulation vs Measurement: losses
First bunches have same losses in simulation and measurement
Simulated losses too large for last bunches
simulation
measurement

## Slide 23
High intensity: FB off, FF off, LD off, PL off
Batch spacing: 2000ns
…
offset by 2ns
offset by 50%

## Slide 24
High intensity: FB off, FF off, LD off, PL off
Batch spacing: 1200ns
…
offset by 2ns
offset by 50%

## Slide 25
High intensity: FB off, FF off, LD off, PL off
Batch spacing: 600ns
…
offset by 2ns
offset by 50%

## Slide 26
High intensity: FB off, FF off, LD off, PL off
Batch spacing: 300ns
…
offset by 2ns
offset by 50%

## Slide 27
High intensity: FB off, FF off, LD off, PL off
Batch spacing: 250ns
…
offset by 2ns
offset by 50%

## Slide 28
High intensity: FB off, FF off, LD off, PL off
Batch spacing: 200ns
…
offset by 2ns
offset by 50%